## Slide 1: JVET-AI0095 EE1-related: Improved gain for NN in-loop filters using early cropping
Jacob Ström, Mitra Damghanian, Du Liu and Per Wennersten
Ericsson

## Slide 2: Cropping in HOP, LOP and VLOP

## Slide 3: Background
Current LOP3 always uses padding=(1,1) for 3x3 convolutions, which preserves patch size
  144x144 in → 144x144 out for a 3x3 conv2D
By using padding=(0,0) it is possible to reduce patch size
  144x144 in → 142x142 out for a 3x3 conv2D

## Slide 4: Previous proposal
Previous proposal AH0195 used padding=(0,0) to avoid the unnecessary calculations at the end of the neural network
  Produced the same result as LOP3 (bit exact)
  Saved 0.8% kMAC/pixel
LOP3
144x144
144x144
AH0195
144x144
128x128
padding=(0,0) in last few layers

## Slide 5: Current proposal
Use padding earlier in the network
LOP3
144x144
144x144
current proposal
144x144
128x128
padding=(0,0) in a few layers in the beginning

## Slide 6: Motivation
Reducing the patch size has a big influence on kMAC for a conv2D layer
Example: first 1x1 in backbone in LOP3, patch size = 36x36 (which is needed for 144x144 size)
  Kx*Ky*W*H*Cin*Cout = 1*1*36*36*144*32 = 5 971 968
If we could get that down to 32x32 (which is needed for 128x128 size) we would get
  Kx*Ky*W*H*Cin*Cout = 1*1*32*32*144*32 = 4 718 592
  This is a reduction of 21%
Idea: Go down to the minimum resolution early in LOP3
Use the saved complexity to increase the number of backbone blocks and the channel width

## Slide 7: Proposed changes in blue
First two backbone blocks:
crop bypass
padding =(0,0)
Remaining N-2 backbone blocks
same as in LOP3

## Slide 8: Spending the savings
By cropping early, we the kMAC/pixel is lowered from 16.9 kMAC/pixel to 14.1 kMAC/pixel (-16.5%)
To increase back to 16.9 kMAC/pixel we
  Increase the number of backbone blocks from NY=14 to NY=15
  Increase the width of the backbone block from CY1=144 to CY1=176 (both divisible by 16).
  This gives a complexity of 16.8 kMAC/pixel

## Slide 9: Results:
Int16 results over NNVC9.1rc with int16-LOP3 and NNIntra:
RA-BDR -0.26% (Y) -1.33% (U) -1.00% (V) 101% DecT
AI-BDR -0.26% (Y) -1.21% (U) -1.08% (V) 104% DecT
LD-BDR -0.23% (Y) -0.85% (U) -0.59%. (V) 96% DecT
Thanks to Nokia for inference crosscheck!

## Slide 11: Detailed Results
 | Random access Main10 |  |  |  | 
 | BD-rate Over NNVC-8.0 Intra+LOP int16 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT CPU
Class A1 | -0.12% | -1.84% | -1.18% | 88% | 103%
Class A2 | -0.23% | -1.93% | -0.75% | 95% | 103%
Class B | -0.31% | -1.40% | -1.22% | 107% | 102%
Class C | -0.33% | -0.43% | -0.79% | 122% | 97%
Class E |  |  |  |  | 
Overall | -0.26% | -1.33% | -1.00% | 104% | 101%
Class D | -0.56% | -0.99% | -0.98% | 132% | 96%
Class F | -0.22% | -0.45% | -0.02% | 135% | 98%
 | Low delay B Main10 |  |  |  | 
 | BD-rate Over NNVC-8.0 Intra+LOP int16 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT CPU
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.18% | -1.63% | -1.58% | 68% | 101%
Class C | -0.42% | 0.23% | 0.60% | 80% | 97%
Class E | -0.06% | -0.97% | -0.54% | 100% | 86%
Overall | -0.23% | -0.85% | -0.59% | 79% | 96%
Class D | -0.33% | 0.99% | 0.92% | 90% | 96%
Class F | -0.23% | 1.13% | -1.83% | 77% | 95%
 | All Intra Main10 |  |  |  | 
 | BD-rate Over NNVC-8.0 Intra+LOP int16 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT CPU
Class A1 | -0.24% | -1.45% | -0.45% | 93% | 104%
Class A2 | -0.21% | -1.45% | -0.76% | 92% | 104%
Class B | -0.23% | -1.24% | -1.25% | 92% | 103%
Class C | -0.26% | -0.82% | -0.85% | 105% | 103%
Class E | -0.37% | -1.17% | -2.01% | 101% | 105%
Overall | -0.26% | -1.21% | -1.08% | 97% | 104%
Class D | -0.38% | -0.65% | -0.48% | 107% | 106%
Class F | -0.21% | -0.22% | -0.11% | 103% | 104%