## Slide 1
JVET-AI0102
Non-EE2: Regression-based SGPM blending
Xinwei Li, Ru-Ling Liao, Jie Chen, Yan Ye
Alibaba group

## Slide 2
实验室名称
Spatial GPM (SGPM) for intra prediction
  two intra predictors are blended according to a partition mode
  an SGPM candidate list is built and reordered  16 candidates
Regression-based GPM blending for inter GPM
  a blending matrix is derived from the template and used to blend two inter predictors
Introduction

## Slide 3
实验室名称
non-CCP chroma intra prediction modes reordering was proposed
  -0.05% luma gain for camera-captured contents
  -0.18% luma gain for class F
  -0.22% luma gain for class TGM
It is recommend to further study this proposal in EE2cross-checking
It is proposed to extend the idea of regression-based GPM blending method to SGPM
the SGPM candidate list is extended with regression-based SGPM (RSGPM) candidates and reordered together
for each RSGPM candidate:
  two intra modes are selected from the primary MPM list and up to 6 BVs
  the blending matrix is derived based on 1 line template to blend the two intra predictors
up to two RDOs are added to select from the proposed SGPM candidate list
the DIMD mode is used to select the transform kernel for RSGPM
the matrix-based intra prediction mode replacement is applied to SGPM
Proposed Method

## Slide 4
实验室名称
Simulation results
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.12% | 0.00% | 0.04% | 103.4% | 101.3% | 100.1% | 100.6%
Class A2 | -0.11% | -0.10% | 0.02% | 102.7% | 101.8% | 100.2% | 100.7%
Class B | -0.11% | -0.02% | -0.13% | 104.3% | 102.7% | 103.3% | 101.0%
Class C | -0.10% | -0.05% | 0.05% | 103.9% | 102.9% | 100.7% | 101.3%
Class E | -0.18% | 0.16% | 0.00% | 104.8% | 102.5% | 100.6% | 101.2%
Overall | -0.12% | -0.01% | -0.02% | 103.9% | 102.3% | 101.2% | 101.0%
Class D | -0.08% | -0.05% | -0.28% | 103.9% | 103.9% | 100.8% | 101.4%
Class F | -0.06% | 0.04% | 0.07% | 102.6% | 102.1% | 100.6% | 101.3%
Class TGM | -0.02% | -0.02% | -0.02% | 102.7% | 102.6% | 100.4% | 101.1%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.09% | -0.20% | -0.20% | 100.8% | 100.8% | 100.2% | 100.2%
Class A2 | *-0.05% | -0.21% | -0.04% | 100.5% | 100.1% | 99.7% | 100.4%
Class B | -0.07% | 0.06% | -0.12% | 101.3% | 100.5% | 100.5% | 100.9%
Class C | -0.07% | -0.06% | 0.01% | 101.0% | 100.4% | 100.9% | 101.2%
Class E |  |  |  |  |  |  | 
Overall | *-0.07% | -0.08% | -0.09% | 101.0% | 100.4% | 100.4% | 100.7%
Class D | 0.03% | -0.04% | 0.01% | 100.3% | 100.4% | 100.7% | 101.8%
Class F | -0.02% | 0.26% | 0.24% | 101.2% | 101.0% | 100.2% | 101.7%
Class TGM | -0.12% | -0.09% | 0.04% | 100.8% | 100.1% | 101.3% | 101.1%

## Slide 5
实验室名称
a regression-based SGPM blending method is proposed
  -0.12% luma gain in AI
  *-0.07% luma gain in RA
It is recommend to further study this proposal in EE2
Thanks vivo for crosschecking
Conclusion

## Slide 6
实验室名称
Thanks！