## Slide 1: JVET-aI0200 Non-EE2: Use Luma Reconstruction Signal for Chroma ALF
Changyue Ma, Xiaoyu Xiu, Xianglin Wang

## Slide 2: Introduction
Chroma ALF input in ECM13.0:
Chroma reconstruction signal.
Chroma fixed filter output.
Figure 1. chroma ALF filter shape in ECM13.0.

## Slide 3: Proposal
Chroma ALF takes luma reconstruction signal as additional input:
Down-sample luma reconstruction signal.
3x3 cross filter shape.
Figure 1. chroma ALF filter shape in the proposed method.

## Slide 4: Performance evaluation
Summary of results
Over ECM13.0 |  |  |  |  | 
 | All Intra |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | -0.63% | -1.14% | 100.8% | 100.6%
Class A2 | 0.03% | -0.82% | -0.93% | 100.5% | 100.9%
Class B | 0.05% | -1.24% | -1.43% | 99.8% | 99.5%
Class C | 0.01% | 0.03% | -0.07% | 99.7% | 101.0%
Class E | 0.00% | -0.08% | -0.22% | 99.9% | 99.9%
Average | 0.03% | -0.59% | -0.79% | 100.1% | 100.3%
Class D | 0.02% | -0.17% | -0.12% | 99.7% | 99.7%

## Slide 5: Performance evaluation
Summary of results
Over ECM13.0 |  |  |  |  | 
 | Random Access |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.04% | -0.70% | -0.94% | 100.4% | 100.0%
Class C | 0.01% | -0.06% | 0.02% | 100.0% | 99.8%
Class E |  |  |  |  | 
Average |  |  |  |  | 
Class D | -0.01% | -0.08% | -0.06% | 100.3% | 100.1%

## Slide 6: Conclusion
Summary:
It is proposed to take luma reconstruction signal as additional input for chroma ALF.
Achieve noticeable coding benefits with minor enc/dec run-time impact.
It is recommended to study the proposed method in the next round of EE.