## Slide 1: AHG12: Improved implicit MTS
Charles Bonnineau, Saurabh Puri, Ismail Marzuki, Renan Utida, Karam Naser, Tangi Poirier , Fabrice Le Léannec

## Slide 2: Introduction
Implicit MTS infers non-separable primary transform pair using information known at decoder side.
  Applied to ISP blocks (CTC) or to all intra blocks (non-CTC)
The Implicit MTS method of ECM-13.0 remained unchanged since VVC.
    trHor =
    trVer =
In the ECM, explicit MTS method uses an extended set of transforms and is also intra mode and TU size dependent.

## Slide 3: Proposed method
This contribution introduces a new implicit MTS method for ECM-13.0.
A lookup-table (LUT) is used to infer primary transform pair based on intra mode and TU size.
  Same intra mode as in explicit MTS is considered.
  Max block size 32x32.
The transform pair candidates in the LUT are based on ECM-13.0 primary transforms:
  {DCT2, DCT5, DCT8, DST1, DST4, DST7}
For ISP blocks, the default implicit MTS method of ECM-13.0 is used.

## Slide 4: Proposed implicit MTS vs ECM-13.0 implicit MTS
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 (MTS=0, MTSImplicit=1) |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.14% | 0.05% | -0.22% | 101.1% | 102.8% | 100.2% | 99.5%
Class A2 | -0.15% | 0.04% | 0.05% | 100.4% | 102.2% | 100.3% | 99.5%
Class B | -0.17% | 0.09% | 0.09% | 100.0% | 102.7% | 100.8% | 99.7%
Class C | -0.12% | -0.01% | 0.07% | 100.1% | 101.7% | 99.7% | 100.2%
Class E | -0.13% | 0.04% | -0.05% | 100.5% | 100.8% | 100.1% | 100.1%
Overall | -0.14% | 0.04% | 0.01% | 100.4% | 102.1% | 100.2% | 99.8%
Class D | -0.15% | -0.16% | -0.03% | 100.0% | 101.0% | 100.1% | 100.0%
Class F | -0.08% | -0.05% | 0.05% | 100.3% | 102.4% | 100.6% | 100.1%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 (MTS=0, MTSImplicit=1) |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | -0.06% | -0.06% | 0.03% | 100.8% | 100.6% | 100.1% | 99.9%
Class C | -0.04% | 0.17% | 0.28% | 100.2% | 100.4% | 100.5% | 100.1%
Class E |  |  |  |  |  |  | 
Overall |  |  |  |  |  |  | 
Class D | -0.06% | 0.10% | -0.03% | 99.8% | 99.3% | 100.2% | 100.1%
Class F | -0.03% | -0.15% | -0.09% | 99.7% | 101.8% | 99.9% | 99.7%
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 (MTS=0, MTSImplicit=1) |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B |  |  |  |  |  |  | 
Class C | 0.00% | -0.37% | 0.08% | 99.8% | 98.5% | 100.1% | 100.1%
Class E | -0.09% | 0.36% | 0.11% | 101.1% | 100.5% | 99.1% | 100.2%
Overall |  |  |  |  |  |  | 
Class D | 0.06% | 0.29% | 0.57% | 97.6% | 97.6% | 100.1% | 100.1%
Class F |  |  |  |  |  |  | 
Class TGM |  |  |  |  |  |  | 

## Slide 5: Proposed implicit MTS vs MTS OFF
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 (MTS=0) |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.51% | -0.25% | -0.45% | 100.2% | 103.3% | 99.7% | 100.1%
Class A2 | -0.62% | -0.40% | -0.40% | 99.1% | 102.2% | 100.1% | 99.8%
Class B | -0.36% | -0.41% | -0.50% | 99.4% | 103.2% | 101.6% | 100.0%
Class C | -0.36% | -0.39% | -0.31% | 100.1% | 100.9% | 100.1% | 100.1%
Class E | -0.51% | -0.30% | -0.39% | 100.5% | 100.8% | 100.1% | 100.1%
Overall | -0.45% | -0.36% | -0.41% | 99.8% | 102.2% | 100.4% | 100.0%
Class D | -0.27% | -0.33% | -0.31% | 100.3% | 100.4% | 100.0% | 99.9%
Class F | -0.22% | -0.02% | -0.16% | 101.8% | 104.0% | 99.6% | 100.3%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 (MTS=0) |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | -0.35% | -0.13% | -0.13% | 101.4% | 100.3% | 100.1% | 100.3%
Class C | -0.20% | -0.08% | -0.01% | 100.7% | 101.1% | 100.5% | 100.1%
Class E |  |  |  |  |  |  | 
Overall |  |  |  |  |  |  | 
Class D | -0.19% | 0.14% | -0.25% | 99.8% | 98.8% | 100.1% | 100.1%
Class F | -0.15% | -0.33% | -0.04% | 100.6% | 100.8% | 99.8% | 99.7%
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 (MTS=0) |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B |  |  |  |  |  |  | 
Class C | -0.09% | -0.33% | 0.13% | 100.4% | 99.0% | 100.1% | 100.2%
Class E | -0.19% | 0.34% | 0.10% | 100.6% | 99.3% | 100.1% | 100.2%
Overall |  |  |  |  |  |  | 
Class D | 0.00% | 0.05% | 0.83% | 97.8% | 97.8% | 100.4% | 100.1%
Class F |  |  |  |  |  |  | 

## Slide 6: ECM-13.0 explicit MTS vs MTS OFF
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 (MTS=0) |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -1.07% | 0.00% | -0.50% | 115.9% | 100.4% | 109.4% | 100.2%
Class A2 | -1.36% | -0.28% | -0.29% | 113.4% | 100.4% | 112.5% | 100.0%
Class B | -0.99% | 0.08% | 0.03% | 117.8% | 101.0% | 116.8% | 99.9%
Class C | -0.98% | 0.06% | 0.04% | 119.8% | 100.2% | 100.8% | 100.1%
Class E | -0.95% | 0.05% | 0.16% | 113.7% | 100.2% | 102.3% | 99.9%
Overall | -1.05% | 0.00% | -0.09% | 116.5% | 100.5% | 108.7% | 100.0%
Class D | -0.83% | 0.05% | 0.22% | 120.9% | 99.5% | 100.3% | 99.9%
Class F | -0.53% | 0.26% | -0.06% | 105.1% | 100.9% | 101.6% | 100.1%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 (MTS=0) |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | -0.71% | -0.02% | 0.07% | 104.0% | 96.8% | 99.9% | 99.7%
Class C | -0.62% | -0.06% | -0.13% | 104.5% | 100.5% | 100.1% | 100.0%
Class E |  |  |  |  |  |  | 
Overall |  |  |  |  |  |  | 
Class D | -0.62% | 0.28% | -0.04% | 103.1% | 98.1% | 100.2% | 100.1%
Class F | -0.46% | -0.16% | 0.13% | 101.1% | 97.1% | 100.0% | 99.7%
Class TGM |  |  |  |  |  |  | 
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 (MTS=0) |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B |  |  |  |  |  |  | 
Class C | -0.47% | 0.18% | 0.55% | 107.4% | 100.9% | 100.1% | 100.1%
Class E | -0.68% | 1.34% | -0.16% | 103.6% | 101.5% | 100.2% | 100.1%
Overall |  |  |  |  |  |  | 
Class D | -0.27% | -0.07% | 0.99% | 103.9% | 98.2% | 100.0% | 100.1%
Class F |  |  |  |  |  |  | 
Class TGM |  |  |  |  |  |  | 

## Slide 7: Conclusion
The proposed implicit method offers -0.14% gains (AI) over ECM-13.0 implicit MTS method
Comparison with explicit MTS shows:
  Proposed implicit MTS: -0.45% gains for 100.4% EncT
  Explicit MTS: -1.05% gains for 116.5% EncT
It is proposed to include the proposed implicit MTS method in the ECM software.
Thanks HHI for crosschecking.

## Slide 8
 | All Intra Main 10 |  |  | Random Access Main 10 |  |  | Low delay B Main 10 |  | 
 | Over ECM-13.0 |  |  | Over ECM-13.0 |  |  | Over ECM-13.0 |  | 
 | Y | EncT | MTS gain kept | Y | EncT | MTS gain kept | Y | EncT | MTS gain kept
Class A1 | 0.70% | 87.2% | 35.22% |  |  |  |  |  | 
Class A2 | 0.90% | 88.8% | 35.17% |  |  |  |  |  | 
Class B | 0.80% | 86.0% | 20.08% | 0.43% | 96.7% | 39.92% |  |  | 
Class C | 0.75% | 83.5% | 24.37% | 0.46% | 96.2% | 26.66% | 0.39% | 93.7% | 18.09%
Class E | 0.57% | 87.9% | 39.89% |  |  |  | 0.58% | 96.0% | 15.10%
Overall | 0.75% | 86.4% | 29.73% |  |  |  |  |  | 
Class D | 0.72% | 83.0% | 14.31% | 0.49% | 97.0% | 21.18% | 0.20% | 96.5% | 24.21%
Class F | 0.40% | 96.6% | 25.27% | 0.34% | 99.9% | 26.12% |  |  | 
 | All Intra Main 10 |  |  | Random Access Main 10 |  |  | Low delay B Main 10 |  | 
 | Over ECM-13.0 |  |  | Over ECM-13.0 |  |  | Over ECM-13.0 |  | 
 | Y | EncT | MTS gain kept | Y | EncT | MTS gain kept | Y | EncT | MTS gain kept
Class A1 | 0.57% | 86.4% | 47.86% |  |  |  |  |  | 
Class A2 | 0.75% | 87.4% | 45.89% |  |  |  |  |  | 
Class B | 0.64% | 84.3% | 36.59% | 0.37% | 97.5% | 48.99% |  |  | 
Class C | 0.63% | 83.5% | 36.33% | 0.42% | 96.4% | 32.99% | 0.38% | 93.5% | 18.6%
Class E | 0.44% | 88.3% | 53.86% |  |  |  | 0.50% | 97.0% | 27.8%
Overall | 0.61% | 85.7% | 43.02% |  |  |  |  |  | 
Class D | 0.56% | 83.0% | 32.60% | 0.43% | 96.9% | 30.82% | 0.26% | 94.2% | 0.9%
Class F | 0.31% | 96.9% | 41.33% | 0.32% | 99.5% | 31.98% |  |  | 
Comparison between proposed implicit MTS method and explicit MTS
Comparison between ECM-13.0 implicit MTS method and explicit MTS