## Slide 1: Description of SDR and HDR Technology by Sharp and Foxconn
JVET-J0026

## Slide 2: Highlights
Proposal Highlights
  We describe a HDR video coding system
  The system uses the SDR video coding approach that is described in JVET-J0026
  For HDR, new tools for QP signaling, loop filtering and bit-depth expansion are also incorporated
  We achieve 34.3% bit-rate reduction for PQ content and 32.2% bit-rate reduction for HLG content for random access configuration using the wPSNR metric. (An improvement of 8.9% and 5.6% compared to the JEM.)

## Slide 3: Overview
Overview
Proposal Description (HDR)
  QP Signaling
  Loop Filtering
Performance
  Overall
  Tool Level
Relationship to JVET-J0027
Conclusions

## Slide 4
Proposal Description (HDR)

## Slide 5: QP Signaling
QP Signaling
  Proposal supports the explicit signaling of QP on a CU group size basis
  Additionally, we include a method for inferring the QP value based on the average value of the prediction
  Inferred QP is determined with a look up table that is transmitted in the bit-stream and maps the average value to the QP
  Note: The same LUT is used as in the CfP anchor
QP prediction and application process when operating on PQ-HDR content.

## Slide 6: Loop Filtering
CTU Adaptive Band Offset
  We extend the SAO band offset tool in the JEM
  Goal is to better handle the limited dynamic range of the HDR chroma channels
  Our approach
    Adjust the band position based on the minimum value of the CTU in addition to the signaled band position
    Chose the band range based on the dynamic range of the CTU

## Slide 7: Internal Bit Depth Increase (IBDI)
Internal Bit Depth Increase (IBDI)
  For HDR content, the chroma values may not use the entire dynamic range of the container
  To improve fidelity, our proposal increases the bit-depth from 10-bits to 11-bits for HDR content
  This allows decoding the HDR data with fine granularity
 | JEM (anchor) | Proposal
IBDI | 10-bit | 11-bit

## Slide 8
Performance

## Slide 9: Overall Performance
We report on the objective performance of the described method
Two results are provided in the contribution
  “February Result”: Corresponds to the bit-streams submitted for visual evaluation
  “April Result”: Corresponds to current performance of the proposal and captures further encoder control and coding tool improvements
  April Results are provided in the next slides and full results are in the contribution
*With Improved Encoder Control

## Slide 10: Overall Performance (HDR)
HDR Random Access
Improvement relative to HM (wPSNR)
  HDR-PQ: -34.3%
  HDR-HLG: -32.2%
 | Constraint Set 1 |  |  |  |  |  |  | 
 | Over HM16.16 |  |  |  |  |  |  | 
 | BD-rate |  |  |  |  |  |  | 
 | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV
DayStreet | -61.0% | -41.1% | -39.8% | -57.0% | -70.3% | -38.8% | -55.6% | -68.7%
PeopleInShoppingCenter | -51.9% | -33.9% | -33.0% | -58.8% | -54.7% | -32.7% | -56.4% | -54.4%
SunsetBeach | -59.9% | -28.5% | -23.7% | -82.5% | -83.3% | -24.5% | -78.1% | -83.6%
Market | -37.0% | -30.2% | -30.5% | -27.3% | -8.0% | -27.6% | -20.0% | 5.3%
ShowGirl2 | -42.6% | -33.2% | -33.5% | -72.4% | -51.7% | -31.1% | -72.8% | -51.8%
Hurdles | -49.0% | -43.0% | -42.2% | -50.8% | -39.5% | -39.2% | -43.4% | -32.4%
Starting | -35.5% | -37.8% | -36.2% | -37.8% | -15.2% | -33.8% | -34.6% | -3.4%
Cosmos1 | -40.2% | -30.2% | -29.1% | -67.2% | -84.1% | -27.2% | -66.8% | -83.6%
Average HDR-A | -57.6% | -34.5% | -32.2% | -66.1% | -69.4% | -32.0% | -63.4% | -68.9%
Average HDR-B | -40.8% | -34.9% | -34.3% | -51.1% | -39.7% | -31.8% | -47.5% | -33.2%
Average all | -47.1% | -34.7% | -33.5% | -56.7% | -50.8% | -31.9% | -53.5% | -46.6%
Enc Time[%] | 4126% |  |  |  |  |  |  | 
Dec Time[%] | 1636% |  |  |  |  |  |  | 
Max Delta Rate[%] | -0.2% |  |  |  |  |  |  | 
Min Delta Rate[%] | -4.4% |  |  |  |  |  |  | 
Max Delta PSNR | 1.02 | 1.33 | 2.84 | 2.23 | 2.25 | 2.50 | 2.13 | 2.28
Min Delta PNSR | 0.31 | 0.29 | 0.48 | -0.07 | 0.08 | 0.48 | -0.23 | -0.17

## Slide 11: Overall Performance (HDR)
HDR Random Access
Improvement relative to JEM (wPSNR)
  HDR-PQ: -8.9%
  HDR-HLG: -5.6%
 | Constraint Set 1 |  |  |  |  |  |  | 
 | Over JEM7.0 |  |  |  |  |  |  | 
 | BD-rate |  |  |  |  |  |  | 
 | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV
DayStreet | -7.6% | -7.7% | -7.6% | -4.0% | -6.7% | -7.4% | -3.9% | -7.3%
PeopleInShoppingCenter | -5.6% | -6.3% | -6.3% | -4.7% | -3.4% | -6.3% | -4.0% | -3.9%
SunsetBeach | -11.4% | -3.3% | -3.4% | -9.6% | -27.5% | -3.2% | -8.7% | -27.6%
Market | 1.4% | -7.7% | -7.4% | 14.4% | 51.5% | -5.6% | 17.6% | 59.4%
ShowGirl2 | -22.1% | -9.3% | -8.4% | -34.7% | -34.9% | -7.4% | -40.2% | -39.7%
Hurdles | -3.5% | -13.5% | -13.5% | 2.1% | 23.4% | -12.4% | 6.8% | 27.6%
Starting | -4.6% | -10.4% | -8.7% | -7.4% | 12.9% | -7.4% | -6.2% | 17.0%
Cosmos1 | -14.1% | -8.1% | -6.6% | -5.5% | -35.9% | -5.9% | -5.4% | -31.3%
Average HDR-A | -8.2% | -5.8% | -5.8% | -6.1% | -12.5% | -5.6% | -5.6% | -12.9%
Average HDR-B | -8.6% | -9.8% | -8.9% | -6.2% | 3.4% | -7.7% | -5.5% | 6.6%
Average all | -8.4% | -8.3% | -7.8% | -6.2% | -2.6% | -7.0% | -5.5% | -0.7%
Enc Time[%] | 651% |  |  |  |  |  |  | 
Dec Time[%] | 188% |  |  |  |  |  |  | 
Max Delta Rate[%] | -0.2% |  |  |  |  |  |  | 
Min Delta Rate[%] | -4.4% |  |  |  |  |  |  | 
Max Delta PSNR | 0.19 | 0.39 | 0.80 | 0.53 | 0.45 | 0.72 | 0.56 | 0.47
Min Delta PNSR | -0.15 | 0.02 | 0.02 | -0.93 | -1.19 | -0.01 | -0.97 | -1.22

## Slide 12: Tool Performance
We also provide ”tool on” performance for the described method. This includes:
  HDR Tools
    Inferred QP
    IBDI
    New band offset

## Slide 13: Tool Performance
Anchors
Software configured with all JEM and proposed tools off with exception of BT (binary tree with half offset). Encoder configured to use luma adaptive QP as in the CfP anchor.
Software configured with all proposed tools off. Encoder configured to use luma adaptive QP as in the CfP anchor.
HDR Tools (wPSNR)
Tested tool name | “Tool On” test results |  |  |  | 
 | Class HDR |  |  |  | 
 | BD-rate |  |  | Runtime | 
 | Y | Cb | Cr | Enc | Dec
Inferred QP1 | -1.3% | -0.9% | -1.2% | 100% | 100%
IBDI 11-bit2 | -0.2% | -5.5% | -9.7% | 104% | 101%
New Band Offset1 | 0.1% | -1.4 % | -2.2 % | 101% | 100%

## Slide 14
Relationship to JVET-J0027

## Slide 15: Relationship to JVET-J0027
The structure described here is also used in JVET-J0027, which is a joint response from NHK and SHARP.
Relationship
  JVET-J0027 uses a lower complexity configuration of the partitioning structure
  HDR tools in the proposal are also enabled
Additional tools from NHK are included and deferred to the presentation of JVET-J0027 by NHK

## Slide 16
Conclusions

## Slide 17: Conclusions
Conclusions
  We described a HDR video coding system
  The system uses the SDR video coding approach that is described in JVET-J0026
  For HDR, new tools for QP signaling, loop filtering and bit-depth expansion are also incorporated
  We achieved 34.3% bit-rate reduction for PQ content and 32.2% bit-rate reduction for HLG content for random access configuration. (An improvement of 8.9% and 5.6% compared to the JEM.)