## Slide 1: Tencent test sequences for video coding development
JVET-J0052
Jing Ye, Xiang Li, Shan Liu, Lori Wu, Chemin Xie, Keane Liu, Berton Wang, Ping Liu, Kane Dong, Ying Kuang, Weizhong Feng (Tencent)

## Slide 2: Introduction
As the online streaming service is getting popular. More and more contents can be streamed on internet and consume a lot of bandwidth.
Millions of viewers watch live concert, or live eSports on internet.
Those contents are quite different from the test materials currently in use, and have their unique characteristics:
  Frequently light changing
  Larger scenes with zoom-in, and zoom-out
  Panning, and rotation
  A lot computer generated texture details
Notes: For these sequences, it is more difficult to encode with the exiting coding tools.

## Slide 3: The sequences (1)
We provided 6 concert sequences, and 4 eSports sequences.
The six concert sequences are captured by Atomos Shogun Studio and created MOV files with bitrate at 115Mb/s. FFMPEG is used to generate the YUV from the MOV files. The command line is in the word document of this proposal.
The two 1920x1080 eSports sequences are captured by a modified eGame platform that can capture the screen YUV information via GPU and store the YUV in the local HDD. The captured YUV is 4:4:4 format, and it is converted into 4:2:0 format by the HDRtools .
The rest two 2176x1080 eSports sequences are captured by modifing the android code and generate an APK file to capture the RGB information of the screen. Then the RGB is converted into YUV 4:4:4. The YUV 4:4:4 is converted into YUV 4:2:0 by the HDRtools.
Notes: monitor/phone/tablet screen
AOV 80 million daily active users（DAU）PUBG mobile 2 million daily active users (DAU), and it is among the 3 Top free mobile games

## Slide 4: The test sequences (2)
Sequence | Capture method | Frame rate | Resolution | Color primaries | Frame number
Concert1_man_n_robot | Atomos Shogun Studio | 25 fps | 1920x1080 | 709 | 250
Concert2_group_dance1 | Atomos Shogun Studio | 25 fps | 1920x1080 | 709 | 250
Concert3_band_rising | Atomos Shogun Studio | 25 fps | 1920x1080 | 709 | 390
Concert4_robot_band | Atomos Shogun Studio | 25 fps | 1920x1080 | 709 | 250
Concert5_drum | Atomos Shogun Studio | 25 fps | 1920x1080 | 709 | 250
Concert6_group_dance2 | Atomos Shogun Studio | 25 fps | 1920x1080 | 709 | 250
AOV_middle_group_fight | Capture screen | 30 fps | 2176x1080 | 709 | 300
AOV_small_group_fight | Capture screen | 30 fps | 2176x1080 | 709 | 300
PUBG_MOBILE_car | Capture screen | 30 fps | 1920x1080 | 709 | 300
PUBG_MOBILE_parachute | Capture screen | 30 fps | 1920x1080 | 709 | 300

## Slide 5: Concert1_man_n_robot

## Slide 6: Concert2_group_dance1
Concert2_group_dance1

## Slide 7: Concert3_band_rising

## Slide 8: Concert4_robot_band

## Slide 9: Concert5_drum

## Slide 10: Concert6_group_dance2

## Slide 11: AOV_middle_group_fight

## Slide 12: AOV_small_group_fight

## Slide 13: PUBG_MOBILE_car

## Slide 14: PUBG_MOBILE_parachute

## Slide 15: JEM and HM coding performance

## Slide 16: RD curves (1)
JEM Random Access

## Slide 17: RD curves (2)
HM Random Access

## Slide 18: RD curves (3)
JEM Low Delay B

## Slide 19: RD curves (4)
HM Low Delay B

## Slide 20: Conclusion
The proposed sequences are popular internet streamed videos, which have unique characteristics and are difficult to compress with existing video codec.
We suggest to include these sequences in test conditions when developing future video coding standard.

## Slide 21: Thank you!