## Slide 1: JVET-K0027
CE7 Summary Report on
Quantization and
Coefficient Coding

## Slide 2: Tools under Test
 | Proponent | Document | Tool description
1 | Qualcomm | JVET-J0021 | Coefficient Coding (JEM 7.0)
2 | HHI | JVET-J0014 | Coefficient Coding
3 | HHI | JVET-J0014 | Coefficient Coding with dependent quantization
4 | Samsung | JVET-J0024 | Coefficient Coding
5 | Huawei | JVET-J0024 | Transform Domain Residual Sign Prediction
6 | Huawei | JVET-J0025 | Adaptive quantization step size scaling
7 | Huawei | JVET-J0025 | Coefficient Coding (JEM 7.0) with complexity reduction [Note: The tool is not described in JVET-J0025]
8 | MediaTek | JVET-J0018 | Extension of QP value range
9 | MediaTek | JVET-J0018 | Derivation of chroma QP from luma QP
10 | KDDI | JVET-J0016 | Block size dependent coefficient scanning
11 | NHK | JVET-J0027 | Coefficient reordering for transform-skipped and bi-predicted CU [withdrawn]

## Slide 3: Subtests
Subtest 7.1
Four competing methods for transform coefficient coding
Subtest 7.2
One method for quantization (comparison to sign data hiding)
Subtest 7.3
Three approaches for deriving / signaling of quantization step sizes / QPs
Subtest 7.4
One approach for modifying scanning order
Subtest 7.5
Two configurations for sign prediction in transform domain

## Slide 4: Subtest 7.1: Transform Coefficient Coding
Test 7.1.1: (Qualcomm) JEM / BMS coefficient coding
Document JVET-K0069 (related: JVET-K0319)
Test 7.1.2: (HHI) Coefficient coding
Document JVET-K0071 (related: JVET-K0072, JVET-K0281)
Test 7.1.3: (Samsung) Scan-region based coefficient coding
Document JVET-K0138
Test 7.1.4: (Huawei) JEM / BMS coefficient coding with complexity reduction
Document JVET-K0321
Cross checks
Results and implementations verified by at least one cross checker (for all tests)

## Slide 5: Subtest 7.1: Characterization of Approaches
 |  | CE7-1.1 |  | CE7-1.2 |  | CE7-1.3 |  | CE7-1.4 | 
scan method |  | diagonal |  | diagonal |  | diagonal (scan region) |  | diagonal | 
sigCGFlag |  | 4 | (2+2) | 4 | (2+2) |  |  | 4 | (2+2)
lastXY |  | 58 | (2x(25+4)) | 58 | (2x(25+4)) | 58 | (2x(25+4)) | 58 | (2x(25+4))
sigLuma |  | 58 | (3x18) | 18 |  | 47 |  | 58 | (3x18)
sigChroma |  | 12 |  | 12 |  |  |  | 12 | 
gt1 luma |  | 16 |  | 21 |  | 18 |  | 16 | 
gtx luma |  |  |  | 21 |  |  |  |  | 
gt1 chroma |  | 6 |  | 11 |  |  |  | 6 | 
gtx chroma |  |  |  | 11 |  |  |  |  | 
regular bins |  | 16 sig, |  | 16 sig, |  | max(scanR/2,8) GT1, |  | 16 sig, | 
 |  | 8 GT1/CG, |  | up tp GT4 for |  | max(scanR/16,1) GT2 |  | 8 GT1/CG, | 
 |  | 1 GT2/CG |  | all coefficients |  |  |  | 1 GT2/CG | 
RiceParameter |  | VTM/BMS |  | JVET-K0071 |  | VTM/BMS |  | VTM/BMS | 
total # ctx |  | 150 |  | 156 |  | 123 |  | 150 | 

## Slide 6: Subtest 7.1: Average Results
subtest 7.1 |  | over VTM-1 (BMS in VTM config.) |  |  |  |  | over BMS-1 |  |  |  |  | over BMS-1 with HEVC coeff. coding |  |  |  | 
 |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
AI | test 7.1.1 | -1.3% | -1.1% | -1.1% | 105% | 101% | 0.0% | 0.0% | 0.0% | 100% | 100% | -0.8% | -0.8% | -0.8% | 108% | 102%
 | test 7.1.2 | -1.8% | -1.7% | -1.8% | 102% | 100% | -0.4% | -0.9% | -0.1% | 94% | 98% | -1.2% | -1.8% | -1.0% | 101% | 100%
 | test 7.1.3 (1) | -0.9% | 0.0% | 0.0% | 105% | 106% | 0.1% | 1.0% | 0.9% | 100% | 102% | -0.7% | 0.1% | 0.1% | 108% | 103%
 | test 7.1.3 (2) | -0.9% | -0.1% | -0.1% | 102% | 102% | 0.1% | 0.8% | 0.8% | 99% | 101% |  |  |  |  | 
 | test 7.1.4 | -1.3% | -1.1% | -1.1% | 105% | 101% | 0.1% | 0.0% | 0.0% | 100% | 100% | -0.8% | -0.8% | -0.8% | 108% | 102%
RA | test 7.1.1 | -0.9% | -0.6% | -0.6% | 103% | 100% | 0.0% | 0.0% | 0.0% | 100% | 100% | -0.6% | -0.6% | -0.4% | 107% | 101%
 | test 7.1.2 | -1.2% | -1.1% | -1.0% | 101% | 100% | -0.3% | -0.7% | 0.0% | 95% | 99% | -0.8% | -1.2% | -0.4% | 101% | 100%
 | test 7.1.3 (1) | -0.3% | 0.3% | 0.3% | 101% | 105% | 0.3% | 1.0% | 0.9% | 98% | 102% | -0.3% | 0.4% | 0.5% | 105% | 103%
 | test 7.1.3 (2) | -0.5% | 0.0% | 0.0% | 100% | 101% | 0.1% | 0.6% | 0.6% | 98% | 100% |  |  |  |  | 
 | test 7.1.4 | -0.9% | -0.6% | -0.6% | 106% | 100% | 0.1% | 0.0% | -0.1% | 101% | 100% | -0.5% | -0.5% | -0.5% | 108% | 101%
LB | test 7.1.1 | -0.6% | -0.4% | -0.3% | 105% | 101% | 0.0% | 0.0% | 0.0% | 100% | 100% | -0.3% | -0.5% | -0.3% | 106% | 102%
 | test 7.1.2 | -0.9% | -1.5% | -0.1% | 101% | 101% | -0.3% | -0.8% | 1.0% | 96% | 97% | -0.6% | -1.2% | 0.7% | 102% | 99%
 | test 7.1.3 (1) | 0.6% | 1.2% | 1.2% | 100% | 105% | 0.8% | 1.3% | 1.5% | 96% | 99% | 0.5% | 0.8% | 1.2% | 101% | 101%
 | test 7.1.3 (2) | 0.0% | -0.2% | -0.1% | 99% | 100% | 0.5% | 0.3% | 0.5% | 96% | 100% |  |  |  |  | 
 | test 7.1.4 | -0.6% | -0.6% | -0.3% | 105% | 100% | 0.0% | 0.0% | 0.1% | 100% | 100% | -0.4% | -0.5% | -0.2% | 106% | 102%
 | (1) EP init in test, but not in references |  |  |  |  |  |  |  |  |  |  |  |  |  | estimated | 
 | (2) EP init in both, test and references |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 7: Subtest 7.1: Comments by Cross Checkers
M. Coban on test 7.1.2:
Includes modification of context modelling for Cr CBF
Interleaving of regular-coded and bypass-coded bin

## Slide 8: Subtest 7.2: Quantization
Test 7.2.1: (HHI) Dependent Quantization
Uses HHI’s transform coefficient coding (test 7.1.2)
Document JVET-K0072
Additional References
Sign data hiding (on top of test 7.1.1, 7.1.2, 7.1.4)
Cross checks
Results and implementations verified by at least one cross checker (for all tests)
Related contributions: Modified entropy coding and state transition
Qualcomm: JVET-K0070 (cross check in JVET-K0424), JVET-K0319
HHI: JVET-K0072 (cross check in JVET-K0428)

## Slide 9: Subtest 7.2: Modifications of Transform Coefficient Coding
 |  | CE7-1.1 |  | CE7-1.2 |  | CE7-1.3 |  | CE7-1.4 |  | CE7-2.1 | 
scan method |  | diagonal |  | diagonal |  | diagonal (scan region) |  | diagonal |  | diagonal | 
sigCGFlag |  | 4 | (2+2) | 4 | (2+2) |  |  | 4 | (2+2) | 4 | (2+2)
lastXY |  | 58 | (2x(25+4)) | 58 | (2x(25+4)) | 58 | (2x(25+4)) | 58 | (2x(25+4)) | 58 | (2x(25+4))
sigLuma |  | 58 | (3x18) | 18 |  | 47 |  | 58 | (3x18) | 36 | (2x18)
sigChroma |  | 12 |  | 12 |  |  |  | 12 |  | 24 | (2x12)
gt1 luma |  | 16 |  | 21 |  | 18 |  | 16 |  | 42 | (2x21)
gtx luma |  |  |  | 21 |  |  |  |  |  | 21 | 
gt1 chroma |  | 6 |  | 11 |  |  |  | 6 |  | 22 | (2x11)
gtx chroma |  |  |  | 11 |  |  |  |  |  | 11 | 
regular bins |  | 16 sig, |  | 16 sig, |  | max(scanR/2,8) GT1, |  | 16 sig, |  | 16 sig, | 
 |  | 8 GT1/CG, |  | up tp GT4 for |  | max(scanR/16,1) GT2 |  | 8 GT1/CG, |  | up tp GT4 for | 
 |  | 1 GT2/CG |  | all coefficients |  |  |  | 1 GT2/CG |  | all coefficients | 
RiceParameter |  | VTM/BMS |  | JVET-K0071 |  | VTM/BMS |  | VTM/BMS |  | JVET-K0071 | 
total # ctx |  | 150 |  | 156 |  | 123 |  | 150 |  | 218 | 

## Slide 10: Subtest 7.2: Average Simulation Results
subtest 7.2 |  | over VTM-1 (BMS in VTM config.) |  |  |  |  | over BMS-1 |  |  |  |  | over BMS-1 with HEVC coeff. coding |  |  |  | 
 |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
AI | test 7.2.1 | -5.0% | -2.0% | -2.0% | 115% | 98% | -2.9% | -2.4% | -0.8% | 113% | 97% | -3.6% | -3.2% | -1.6% | 119% | 99%
 | 7.1.1 + SDH | -2.1% | -2.8% | -2.8% | 109% | 102% | -0.7% | -1.6% | -1.6% | 105% | 102% | -1.5% | -2.4% | -2.5% | 111% | 104%
 | 7.1.2 + SDH | -2.5% | -3.4% | -3.5% | 106% | 100% | -1.1% | -2.6% | -1.7% | 99% | 99% | -1.9% | -3.4% | -2.6% | 105% | 101%
 | 7.1.4 + SDH | -2.1% | -2.7% | -2.8% | 107% | 101% | -0.7% | -1.6% | -1.6% | 101% | 100% | -1.5% | -2.4% | -2.4% | 107% | 102%
RA | test 7.2.1 | -3.4% | -1.8% | -1.7% | 110% | 99% | -2.2% | -1.7% | -0.4% | 113% | 99% | -2.7% | -2.3% | -0.8% | 121% | 100%
 | 7.1.1 + SDH | -1.5% | -1.6% | -1.7% | 107% | 100% | -0.5% | -1.0% | -1.2% | 104% | 100% | -1.1% | -1.6% | -1.6% | 111% | 101%
 | 7.1.2 + SDH | -1.7% | -2.1% | -2.1% | 104% | 99% | -0.8% | -1.7% | -1.1% | 100% | 100% | -1.4% | -2.2% | -1.5% | 107% | 101%
 | 7.1.4 + SDH | -1.4% | -1.6% | -1.8% | 107% | 100% | -0.5% | -1.0% | -1.2% | 102% | 100% | -1.1% | -1.6% | -1.6% | 109% | 101%
LB | test 7.2.1 | -2.7% | -2.3% | -0.7% | 111% | 99% | -1.9% | -2.3% | 0.4% | 112% | 96% | -2.2% | -2.8% | 0.0% | 118% | 98%
 | 7.1.1 + SDH | -1.2% | -1.9% | -1.6% | 108% | 103% | -0.7% | -1.1% | -0.9% | 103% | 99% | -1.0% | -1.6% | -1.2% | 109% | 101%
 | 7.1.2 + SDH | -1.4% | -2.4% | -1.3% | 106% | 102% | -0.9% | -1.8% | -0.3% | 101% | 99% | -1.2% | -2.2% | -0.6% | 107% | 101%
 | 7.1.4 + SDH | -1.2% | -1.7% | -1.4% | 106% | 100% | -0.6% | -1.1% | -1.1% | 102% | 100% | -0.9% | -1.6% | -1.4% | 108% | 102%
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | estimated | 

## Slide 11: Subtest 7.2: Gain by Modified Quantization
subtest 7.2 |  | VTM configuration |  |  |  |  | BMS configuration |  |  |  | 
 |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
AI | DSQ: 7.2.1 | -3.3% | -0.3% | -0.1% | 113% | 98% | -2.5% | -1.5% | -0.7% | 120% | 99%
 | SDH: 7.1.1 | -0.8% | -1.7% | -1.7% | 104% | 101% | -0.7% | -1.6% | -1.6% | 105% | 102%
 | SDH: 7.1.2 | -0.8% | -1.7% | -1.7% | 104% | 101% | -0.7% | -1.6% | -1.6% | 105% | 100%
 | SDH: 7.1.4 | -0.8% | -1.7% | -1.7% | 101% | 100% | -0.7% | -1.6% | -1.6% | 102% | 100%
RA | DSQ: 7.2.1 | -2.3% | -0.8% | -0.7% | 109% | 99% | -1.9% | -1.1% | -0.4% | 118% | 100%
 | SDH: 7.1.1 | -0.6% | -1.0% | -1.1% | 103% | 100% | -0.5% | -1.0% | -1.2% | 104% | 100%
 | SDH: 7.1.2 | -0.6% | -1.0% | -1.1% | 103% | 99% | -0.6% | -1.0% | -1.1% | 105% | 101%
 | SDH: 7.1.4 | -0.6% | -1.1% | -1.2% | 101% | 100% | -0.6% | -1.0% | -1.1% | 101% | 100%
LB | DSQ: 7.2.1 | -1.8% | -0.9% | -0.6% | 110% | 98% | -1.6% | -1.6% | -0.6% | 116% | 99%
 | SDH: 7.1.1 | -0.6% | -1.4% | -1.2% | 103% | 101% | -0.7% | -1.1% | -0.9% | 103% | 99%
 | SDH: 7.1.2 | -0.5% | -0.9% | -1.2% | 105% | 102% | -0.6% | -1.0% | -1.3% | 105% | 102%
 | SDH: 7.1.4 | -0.6% | -1.1% | -1.1% | 101% | 100% | -0.5% | -1.1% | -1.2% | 101% | 100%

## Slide 12: Subtest 7.2: Comments by Cross Checkers
M. Coban on test 7.2.1:
Unified with coefficient coding of test 7.1.2 (additional contexts)
Requires complex RD algorithm for achieving gains (fallback necessary)
A. Karabutov on test 7.2.1
Recommends to study dependent quantization for JEM / BMS coefficient coding
  see CE7-related contributions: JVET-K0070, JVET-K0072, JVET-K0319

## Slide 13: Subtest 7.3: Quantization Step Sizes / QPs
Test 7.3.1: (Huawei) Adaptive Quantization Step Size Scaling
Version 1: Scaling of quantization step size (based on neighboring samples)
Version 2: Scaling of reconstructed residual (same scaling factor)
Document JVET-K0140 / Used MS-SSIM in addition to PSNR
Test 7.3.2: (MediaTek) Extension of Quantization Parameter Value Range
Document JVET-K0251
Tested for random access and QP values 32, 37, 42, 47
Test 7.3.3: (MediaTek) Derivation of Chroma QP from Luma QP
Document JVET-K0252
Cross checks:
Results and implementations verified by at least one cross checker (for all tests)
Resolved some bugs in implementation of test 7.3.1

## Slide 14: Subtest 7.3: Average Results (PSNR)
subtest 7.3 (PNSR) |  | over VTM-1 (BMS in VTM config.) |  |  |  |  | over BMS-1 |  |  |  | 
 |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
AI | test 7.3.1 (AGS v1: qstep) | 2.5% | 0.8% | 0.9% | 103% | 102% | 1.4% | 0.8% | 0.8% | 103% | 103%
 | test 7.3.1 (AGS v2: residual) | 2.5% | 0.8% | 0.9% | 103% | 102% | 1.5% | 0.8% | 0.8% | 103% | 104%
 | test 7.3.2 (QP extension) |  |  |  |  |  |  |  |  |  | 
 | test 7.3.3 (chroma QP) | -0.3% | 1.2% | 1.2% | 100% | 100% | -0.2% | 1.2% | 1.2% | 100% | 101%
RA | test 7.3.1 (AGS v1: qstep) | 2.3% | 0.5% | 0.4% | 101% | 100% | 1.8% | 0.4% | 0.2% | 100% | 101%
 | test 7.3.1 (AGS v2: residual) | 2.4% | 0.5% | 0.5% | 101% | 100% | 1.8% | 0.4% | 0.2% | 99% | 101%
 | test 7.3.2 (QP extension) [*] | -0.7% | -2.2% | -1.9% | 94% | 99% | -0.7% | -2.1% | -1.8% | 95% | 95%
 | test 7.3.3 (chroma QP) | -1.3% | 2.8% | 2.9% | 99% | 100% | -1.3% | 3.0% | 3.0% | 100% | 100%
LB | test 7.3.1 (AGS v1: qstep) | 3.0% | -1.4% | -1.3% | 96% | 98% | 2.1% | -1.7% | -1.7% | 95% | 99%
 | test 7.3.1 (AGS v2: residual) | 2.9% | -1.1% | -1.1% | 96% | 99% | 2.2% | -1.7% | -1.6% | 94% | 100%
 | test 7.3.2 (QP extension) |  |  |  |  |  |  |  |  |  | 
 | test 7.3.3 (chroma QP) | -0.3% | 2.4% | 2.9% | 100% | 100% | -0.3% | 2.5% | 2.9% | 101% | 101%
 | [*] modified QP values: 32, 37, 42, 47 |  |  |  |  |  |  |  |  |  | 

## Slide 15: Subtest 7.3: Average Results MS-SSIM
subtest 7.3 (MS-SSIM) |  | over VTM-1 (BMS in VTM config.) |  |  |  |  | over BMS-1 |  |  |  | 
 |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
AI | test 7.3.1 (AGS v1: qstep) | -4.8% | 0.7% | 0.9% | 103% | 102% | -3.6% | 0.7% | 0.8% | 103% | 103%
 | test 7.3.1 (AGS v2: residual) | -4.7% | 0.8% | 0.8% | 103% | 102% | -3.5% | 0.7% | 0.8% | 103% | 104%
RA | test 7.3.1 (AGS v1: qstep) | -3.8% | 0.4% | 0.5% | 101% | 100% | -3.1% | 0.3% | 0.2% | 100% | 101%
 | test 7.3.1 (AGS v2: residual) | -3.8% | 0.4% | 0.5% | 101% | 100% | -3.1% | 0.4% | 0.0% | 99% | 101%
LB | test 7.3.1 (AGS v1: qstep) | -3.4% | -1.5% | -1.6% | 96% | 98% | -2.7% | -1.8% | -1.3% | 95% | 99%
 | test 7.3.1 (AGS v2: residual) | -3.4% | -1.0% | -1.0% | 96% | 99% | -2.7% | -1.8% | -1.5% | 94% | 100%

## Slide 16: Subtest 7.3: Comments by Cross Checkers
P. de Lagrange on test 7.3.1:
Scaling depends on reconstructed neighborhood (decoder pipeline)
Semantics for additional slice header element could be simpler
Suggests further tests:
  Use same adjustment as encoder-only method
  Same law at encoder, but use current instead of border samples
H. Schwarz on test 7.3.1
Study encoder-only variant of the approach (can use samples of current block instead of border samples)
Compare with approaches for local QP adaptation
Use separate tool for measuring MS-SSIM (we should not rely on encoder output)

## Slide 17: Subtest 7.3: Comments by Cross Checkers
P. de Lagrange on test 7.3.2:
QP range extension is welcome (encoder manufacturers sometimes use quantization matrix scaling to achieve a similar effect)
QP indexed tables in bilateral filter and deblocking filter are extended (by linear extrapolation); may need review
Modification for reading and writing delta-QP values seems incomplete (changes are proposed by cross checker)
Semantics for additional slice header element could be simpler

## Slide 18: Subtest 7.3: Comments by Cross Checkers
P. de Lagrange on test 7.3.3:
Mapping seems useful for local QP adjustment only, since PPS and slice Cb/Cr QP adjustment is already supported
It has been noted that many offsets and adjustments apply to chroma QP, with different rules for deblocking filter (local adjustment ignored), which may need review

## Slide 19: Subtest 7.4: Scanning Order of Transform Coefficients
Test 7.4.1: (KDDI) Block size dependent coefficient scanning
Modifies scanning order for some block sizes
Document JVET-K0398
Test 7.4.2: [WITHDRAWN]
Cross checks:
Results and implementations verified by at least one cross checker (for all tests)

## Slide 20: Subtest 7.4: Average Simulation Results
subtest 7.4 |  | over VTM-1 (BMS in VTM config.) |  |  |  |  | over BMS-1 |  |  |  | 
 |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
AI | test 7.4.1 (MDCS) | -0.3% | -0.1% | -0.1% | 102% | 101% | 0.0% | 0.1% | 0.1% | 101% | 101%
RA | test 7.4.1 (MDCS) | -0.1% | 0.0% | 0.0% | 101% | 100% | 0.0% | 0.1% | 0.0% | 100% | 100%
LB | test 7.4.1 (MDCS) | -0.1% | 0.1% | 0.1% | 101% | 100% | -0.1% | 0.2% | 0.3% | 99% | 100%

## Slide 21: Subtest 7.4: Comments by Cross Checkers
M. Koo on test 7.4.1:
Recommends further study on block shape adaptive scanning patterns

## Slide 22: Subtest 7.5: Sign Prediction
Test 7.5.1: (Huawei) Residual Sign Prediction in Transform Domain
For intra- and inter-picture predicted blocks
Prediction of up to 5 signs per transform blocks (depending on scaled level)
Modified entropy coding of signs
Document JVET-K0044
Test 7.5.2: (Huawei) Residual Sign Prediction in Transform Domain
Same approach, but only for intra-picture predicted blocks
Document JVET-K0044
Cross checks:
Results and implementations verified by at least one cross checker (for all tests)

## Slide 23: Subtest 7.5: Average Simulation Results
subtest 7.5 |  | over VTM-1 (BMS in VTM config.) |  |  |  |  | over BMS-1 |  |  |  | 
 |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
AI | test 7.5.1 (TSP: intra+inter) | -1.3% | -1.0% | -1.1% | 119% | 151% | -0.4% | -0.3% | -0.4% | 109% | 121%
 | test 7.5.1 (TSP: intra only) | -1.3% | -1.0% | -1.1% | 119% | 151% | -0.4% | -0.3% | -0.4% | 109% | 122%
RA | test 7.5.1 (TSP: intra+inter) | -1.0% | -0.7% | -0.8% | 109% | 118% | -0.6% | -0.4% | -0.6% | 107% | 110%
 | test 7.5.1 (TSP: intra only) | -0.6% | -0.4% | -0.5% | 105% | 112% | -0.2% | -0.1% | -0.2% | 104% | 107%
LB | test 7.5.1 (TSP: intra+inter) | -0.7% | -0.4% | -0.3% | 109% | 120% | -0.6% | -0.4% | -0.1% | 107% | 112%
 | test 7.5.1 (TSP: intra only) | -0.1% | -0.1% | 0.0% | 104% | 109% | -0.1% | -0.2% | 0.0% | 103% | 106%

## Slide 24: Subtest 7.5: Comments by Cross Checkers
F. Henry on test 7.5.1:
May obtain similar results with reduced number of reference samples
Makes decoding stage more serial, because it requires neighboring samples for decoding the signs