## Slide 1: JVET-K0141 AHG8: 360°-based inter/intra prediction for cubemap projection
Cheng-Hsuan Shih, Jian-Liang Lin, Hung-Chih Lin, Shen-Kai Chang, and Chi-Cheng Ju

## Slide 2: Overall Summary
Proposes a 360°-based inter/intra prediction for cubemap projection
The experiment conducted on 360Lib-6.0 and BMS-1.0
  An averaged 0.97%/1.26%/1.28% BD-rate reduction on VTM
  An averaged 1.40%/0.60%/0.79% BD-rate reduction on BMS
Subjective quality is significantly improved at frame boundary

## Slide 3: Conventional Padding Method
The padding region is located around the border of each reference frame by extending the boundary pixels
The conventional padding method does not take advantage of the geometric continuity property in 360° video

## Slide 4: Proposed Method
Proposed method using the geometric neighboring pixel data to obtain the benefits of the geometric continuity property in 360° video
  Inter prediction - the inter prediction replaces the replication padding with the geometry padding in padding region
  Intra prediction - the referenced neighboring pixels in the intra prediction are changed to use the geometric neighboring reconstructed pixels

## Slide 5: 360°-based inter prediction for cubemap projection 1/2
Reference pictures for inter prediction
  Constructing the top sub-frame and the bottom sub-frame for each reference frame data
  The pixel data in the padding region are obtained by the geometry padding process
  Padding size is LCU size + 16 pixels (=144)
144
144

## Slide 6: 360°-based inter prediction for cubemap projection 2/2
Geometry padding process
  The video content of padding region for a given face is derived from other faces
  The geometric pixel position is obtained by the projection mapping functions
  Lanczos interpolation filters are applied to fractional positions
    6-taps for luma
    4-taps for chroma

## Slide 7: 360°-based intra prediction for cubemap projection
The reference pixels of intra prediction are derived from geometric neighboring pixels
The geometric neighboring reference pixels are available if these pixels have been coded
Current CU
Geometric neighboring pixels

## Slide 8: Experimental Results 1/2
Code base: BMS-1.0 + 360Lib-6.0
Configuration: VTM
Projection: Modified Cubemap Projection (MCP) in JVET-J0019
Proposed method vs. conventional inter/intra prediction
Face size = 1280
Sequences |  | WS-PSNR (E2E) |  |  | S-PSNR-NN (E2E) |  | 
 |  | Y | U | V | Y | U | V
Class S1 8K | SkateboardInLot | -1.56% | -2.02% | -2.03% | -1.59% | -2.05% | -1.99%
 | ChairLift | -2.15% | -2.06% | -1.83% | -2.14% | -2.04% | -1.84%
 | KiteFlite | -0.05% | 0.09% | 0.06% | -0.03% | 0.08% | 0.07%
 | Harbor | -0.14% | -0.25% | -0.42% | -0.13% | -0.28% | -0.38%
 | Trolley | -0.16% | -0.17% | -0.11% | -0.18% | -0.17% | -0.10%
 | GasLamp | -0.24% | -0.27% | -0.21% | -0.24% | -0.24% | -0.20%
Class S2 6K | Balboa | -1.69% | -2.33% | -2.43% | -1.68% | -2.31% | -2.44%
 | Broadway | -1.32% | -1.82% | -2.07% | -1.32% | -1.80% | -2.06%
 | Landing2 | -0.99% | -1.67% | -1.51% | -0.96% | -1.66% | -1.49%
 | BranCastle2 | -1.39% | -2.09% | -2.25% | -1.41% | -2.08% | -2.24%
Class S1 |  | -0.72% | -0.78% | -0.76% | -0.72% | -0.78% | -0.74%
Class S2 |  | -1.35% | -1.98% | -2.06% | -1.34% | -1.96% | -2.06%
Overall |  | -0.97% | -1.26% | -1.28% | -0.97% | -1.26% | -1.27%

## Slide 9: Experimental Results 2/2
Code base: BMS-1.0 + 360Lib-6.0
Configuration: BMS
Projection: Modified Cubemap Projection (MCP) in JVET-J0019
Proposed method vs. conventional inter/intra prediction
Face size = 1280
Sequences |  | WS-PSNR (E2E) |  |  | S-PSNR-NN (E2E) |  | 
 |  | Y | U | V | Y | U | V
Class S1 8K | SkateboardInLot | -1.92% | -1.00% | -0.25% | -1.99% | -1.03% | -0.27%
 | ChairLift | -2.55% | -1.63% | -1.81% | -2.56% | -1.64% | -1.79%
 | KiteFlite | -0.48% | 0.23% | 0.06% | -0.41% | 0.19% | 0.02%
 | Harbor | -0.07% | 1.15% | 2.26% | 0.04% | 1.33% | 2.46%
 | Trolley | -0.80% | 0.11% | -0.70% | -0.85% | 0.18% | -0.69%
 | GasLamp | -0.72% | 0.85% | 0.25% | -0.80% | 0.94% | 0.34%
Class S2 6K | Balboa | -2.02% | -1.55% | -2.23% | -2.02% | -1.57% | -2.20%
 | Broadway | -1.52% | -1.61% | -2.29% | -1.52% | -1.61% | -2.26%
 | Landing2 | -1.50% | -0.19% | -0.69% | -1.51% | -0.13% | -0.66%
 | BranCastle2 | -2.38% | -2.36% | -2.55% | -2.38% | -2.32% | -2.54%
Class S1 |  | -1.09% | -0.05% | -0.03% | -1.09% | -0.01% | 0.01%
Class S2 |  | -1.86% | -1.43% | -1.94% | -1.86% | -1.41% | -1.92%
Overall |  | -1.40% | -0.60% | -0.79% | -1.40% | -0.57% | -0.76%

## Slide 10: Subjective Quality Evaluation
Reconstructed YUV encoded under VTM-1.0 with QP = 37
Viewport
  Vertex 1 is tested (the one near the frame boundary)

## Slide 11: Anchor: Conventional Inter/Intra Prediction
Cropped viewport of Landing2 (frame 30) under VTM1.0 with QP 37

## Slide 12: Proposed: 360°-based inter/intra prediction
Cropped viewport of Landing2 (frame 30) under VTM1.0 with QP 37

## Slide 13: Anchor: Conventional Inter/Intra Prediction
Cropped viewport of Broadway (frame 299) under VTM1.0 with QP 37

## Slide 14: Proposed: 360°-based inter/intra prediction
Cropped viewport of Broadway (frame 299) under VTM1.0 with QP 37

## Slide 15: Anchor: Conventional Inter/Intra Prediction
Cropped viewport of SkateboardInLot (frame 194) under VTM1.0 with QP 37

## Slide 16: Proposed: 360°-based inter/intra prediction
Cropped viewport of SkateboardInLot (frame 194) under VTM1.0 with QP 37

## Slide 17: Conclusions
The proposed inter/intra predictions maximally utilize face continuity for cubemap projection
In terms of E2E WS-PSNR-Y/U/V :
  0.97%/1.26%/1.28% BD-rate reduction on VTM
  1.40%/0.60%/0.79% BD-rate reduction on BMS
The seam artifacts caused by the frame boundary could also be significantly reduced