## Slide 1: JVET-K0212 Improved Intra Refresh
Jean-Marc Thiesse
Didier Nicholson

## Slide 2: Context: Low latency
Low latency is key for several market use-cases.
  Not only for video conferencing
    e.g. any application with man in the loop (cloud gaming, drones, remote system operation…)
    Contribution market which needs ultra low latency
  Latency is one key marketing feature for selling encoders
Latency (and error resilience) were a mandate of JVET CfP.
JVET-K0212

## Slide 3: Context: Low latency
Latency comes from various parts of a streaming system:
  Encoding configuration such as GOP structure (=>no reordering)
  Encoding/Decoding time itself (=>dependent slices)
  Network handling:
    Intra picture size is significantly higher than Inter to get the quality.
    Intra pictures took the time of several pictures to be sent.
  No normative solution to address specifically this latency issue
JVET-K0212

## Slide 4: Classical solution: Intra Refresh
Intra Refresh (IR) is often used to solve this issue by encoder manufacturers:
  A group of pixels (column, line, pseudo-random…) is periodically forced to Intra instead of sending one big Intra picture (latency ok).
  The position of refreshed pixels moves along the encoding so that a clean region is produced to insure the reconstruction:
JVET-K0212

## Slide 5: Without Intra Refresh
x8!!
JVET-K0212

## Slide 6: Intra Refresh
JVET-K0212

## Slide 7: Intra Refresh drawbacks
This solution is a « trick » at the encoder level.
Needs several modifications that make bitrate losses:
  Constrained Intra Prediction (CIP) to insure clean refresh.
  Motion vector restrictions (do not point to dirty regions).
  Reference picture constraints at re-looping, etc.
Stream connection not well-managed.
This situation can be improved with a clean and appropriate normative syntax.
JVET-K0212

## Slide 8: Proposal: Improved Intra Refresh
Add the signalization for indicating the position of IR CUs.
Exploit this IR CUs positions knowledge to improve the quality for this low latency use-case:
  Do not transmit pred_mode_flag nor cu_skip_flag on IR CU.
  Enable CIP only on IR CU.
  Take care of the IR position for MVs derivation.
  Define two delta QP by slice depending on the position.
JVET-K0212

## Slide 9: New signalization
PPS level:
  intra_refresh_enabled_flag
  intra_refresh_mode
  intra_refresh_size
  intra_refresh_delta_qp
Slice level:
  intra_refresh_direction
  intra_refresh_position
JVET-K0212

## Slide 10: Normative Intra Refresh Summary
JVET-K0212

## Slide 11: Results: Reference Intra Refresh (1)
Early assessment with VTM 1.1, JVET sequences (only class B and E) and Low-DelayB-10 test conditions.
Column Intra Refresh of size 16 and 64 pixels tested.
Significant losses, especially for Class E.
JVET-K0212
 |  | 16 |  |  | 64 |  | 
 |  | Y | U | V | Y | U | V
Class B | MarketPlace | 5.82% | 7.62% | 8.16% | 14.00% | 13.17% | 13.17%
 | RitualDance | 8.37% | 12.77% | 13.67% | 13.56% | 17.01% | 17.82%
 | Cactus | 7.99% | 10.54% | 10.72% | 19.18% | 20.09% | 20.60%
 | BasketBallDrive | 8,95% | 17,37% | 16,92% | 13,36% | 20,22% | 19,47%
 | BQTerrace | 10.12% | 10.90% | 10.86% | 27.97% | 26.50% | 27.51%
 | Average | 8,25% | 11,84% | 12,07% | 17,62% | 19,40% | 19,71%
Class E | FourPeople | 28.61% | 28.40% | 28.79% | 83.90% | 82.79% | 82.85%
 | Johnny | 34.92% | 35.54% | 35.92% | 101.97% | 105.39% | 106.82%
 | KristenAndSara | 25.38% | 25.07% | 24.34% | 78.42% | 76.75% | 76.61%
 | Average | 29,64% | 29,67% | 29,68% | 88,10% | 88,31% | 88,76%

## Slide 12: Results: Reference Intra Refresh (2)
Previous comparison not fair due to « Intra period = -1 »
=>Results against LDB-10 with Intra period=20 to compare against column 64.
Loss are still significant.
JVET-K0212
 |  | 64 |  | 
 |  | Y | U | V
Class E | FourPeople | 25,33% | 38,23% | 37,15%
 | Johnny | 25,77% | 48,09% | 43,10%
 | KristenAndSara | 25,87% | 41,64% | 44,57%
 | Average | 25,66% | 42,66% | 41,61%

## Slide 13: Results: Improved Intra Refresh
Improved Intra Refresh against Reference Intra Refresh.
Modifications: Signalization + Skip and Pred_mode not written + CIP enable on Intra refresh CU only.
Relevant improvement.
JVET-K0212
 |  | 16 |  |  | 64 |  | 
 |  | Y | U | V | Y | U | V
Class B | MarketPlace | -1,31% | -3,27% | -3,79% | -1,50% | -2,75% | -2,94%
 | RitualDance | -5,13% | -8,93% | -9,35% | -5,20% | -8,29% | -8,85%
 | Cactus | -2,91% | -4,99% | -5,20% | -3,00% | -4,58% | -5,11%
 | BasketBallDrive | -5,34% | -11,08% | -11,58% | -5,24% | -9,95% | -10,59%
 | BQTerrace | -1,14% | -2,33% | -1,60% | -1,38% | -1,43% | -1,49%
 | Average | -3,16% | -6,12% | -6,30% | -3,26% | -5,40% | -5,80%
Class E | FourPeople | -2.74% | -2.94% | -3.56% | -2.90% | -2.55% | -2.87%
 | Johnny | -2,42% | -2,67% | -1,75% | -2,70% | -2,34% | -2,42%
 | KristenAndSara | -2,34% | -3,21% | -3,04% | -2,73% | -2,75% | -2,46%
 | Average | -2,50% | -2,94% | -2,78% | -2,78% | -2,55% | -2,58%

## Slide 14: Conclusion
Low latency is classicaly achieved in real life video encoder implementations with Intra Refresh
  at a cost of significant coding efficiency loss.
  the more the sequences are easily inter coded the more losses.
A suitable normative Intra Refresh solution is proposed:
  Minimal signalization at PPS and Slice level.
  Small modification within encoder and decoder to exploit the IR position.
  Results show that the IR losses are reduced while providing all IR advantages for latency reduction (and error robustness improvement).
Recommendation:
  To explore this solution within a Ad Hoc Group dedicated on Low Latency.
    Definition of CTC and appropriate test set
    Explore/cross-check the proposed modifications as well as improvements
  To integrate the proposed modifications within VTM.
JVET-K0212

## Slide 15: Thank you
The research leading to this work has been supported by the FUI23 EFIGI project, BPIFrance and Region Ile de France.

## Slide 16
seq_parameter_set_rbsp( ) { | Descriptor
sps_seq_parameter_set_id | ue(v)
chroma_format_idc | ue(v)
if( chroma_format_idc = = 3 ) | 
separate_colour_plane_flag | u(1)
pic_width_in_luma_samples | ue(v)
pic_height_in_luma_samples | ue(v)
bit_depth_luma_minus8 | ue(v)
bit_depth_chroma_minus8 | ue(v)
log2_ctu_size_minus2 | ue(v)
log2_min_qt_size_intra_slices_minus2 | ue(v)
log2_min_qt_size_inter_slices_minus2 | ue(v)
max_mtt_hierarchy_depth_inter_slices | ue(v)
max_mtt_hierarchy_depth_intra_slices | ue(v)
intra_refresh_enabled_flag | u(1)
if( intra_refresh_enabled_flag ){ | 
intra_refresh_mode | ue(v)
intra_refresh_size | ue(v)
intra_refresh_delta_qp | ue(v)
} | 
rbsp_trailing_bits( ) | 
} | 

## Slide 17
slice_header( ) { | Descriptor
slice_pic_parameter_set_id | ue(v)
slice_address | u(v)
slice_type | ue(v)
if ( slice_type != I ) | 
log2_diff_ctu_max_bt_size | ue(v)
if (intra_refresh_enabled_flag ){ | 
intra_refresh_direction | u(1)
intra_refresh_position | ue(v)
} | 
byte_alignment( ) | 
} | 
coding_unit( x0, y0, cbWidth, cbHeight ) { | Descriptor
if( slice_type != I && !intra_refresh_cu) { | 
pred_mode_flag | ae(v)
} | 
… | 

## Slide 18
CuIntraRefresh[ xNbY ][ yNbY ] is derived at frame level according to intra_refresh_position value. CuIntraRefresh[ xNbY ][ yNbY ] is equal to 1 if the CU belongs to the Intra Refresh area.
….
Each sample p[ x ][ y ] is derived as follows:
– If one or more of the following conditions are true, the sample p[ x ][ y ] is marked as "not available for intra prediction":
– The variable availableN is equal to FALSE.
– CuPredMode[ xNbY ][ yNbY ] is not equal to MODE_INTRA and constrained_intra_pred_flag is equal to 1.
– CuPredMode[ xNbY ][ yNbY ] is not equal to MODE_INTRA and CuIntraRefresh[ xNbY ][ yNbY ] is equal to 1.
– Otherwise, the sample p[ x ][ y ] is marked as "available for intra prediction" and the sample at the location ( xNbCmp, yNbCmp ) is assigned to p[ x ][ y ].