## Slide 1
JVET-M0083
AHG10: Quantization matrices for MTS
T. Toma, K. Abe
Panasonic Corporation

## Slide 2
2
Background
Quantization matrices, which is HEVC based method with extension to support rectangular CU, was proposed in Macao (JVET-L0121).
Necessity of quantization matrices in VVC was agreed in principle. However following aspects became further study.
  Do the different MTS basis function sets require different matrices?
  Is it really necessary to specify default matrices?

## Slide 3
3
Introduction
Necessity of quantization matrices that is customized for MTS is discussed in this contribution.
  Results of transform coefficients analysis between DCT2 and MTS are shown.
  Syntax is proposed to support quantization matrices customized for MTS.
    Similar to DCT2’s design. Only luma is supported since MTS is used only for luma.

## Slide 4
4
Analysis of transform coefficients between DCT2 and MTS
Characteristics of transform coefficients may be one criteria to see if different matrices are needed for DCT2 and MTS.
Evaluation method
  Average and standard deviation of coefficients prior to quantization in a block are compared among DCT2, DST7, and DCT8.
  Encoding conditions
    Intra and Inter, respectively
    QP: 22, CU size: 16x16, RA condition, VTM 3.0rc1
    Class B sequences (only one frame is used for evaluation)

## Slide 5
Characteristics of transform coefficients (intra block)
Overall characteristics are similar between DCT2 and MTS. However, there are some differences in both average and standard deviation.
Each coefficients
Average & standard deviation
DST7 x DCT8
DST7 x DST7
DCT8 x DCT8
DCT8 x DST7
DCT2 x DCT2

## Slide 6
6
Characteristics of transform coefficients (inter block)
Similar observation to intra block. Overall characteristics are similar between DCT2 and MTS, but with some differences.
Each coefficients
Average & standard deviation
DCT8 x DCT8
DCT8 x DST7
DCT2 x DCT2
DST7 x DCT8
DST7 x DST7

## Slide 7
7
Necessity of quantization matrices customized for MTS
Characteristics of coefficients distribution in a CU is similar between DCT2 and MTS basis functions, but with some differences.
It would be an option to support quantization matrices for MTS that is different from DCT2’s matrices.

## Slide 8
8
Support quantization matrices for MTS basis functions
The method to send quantization matrices is the same as DCT2
  Matrices is supported only for luma since MTS is used only for luma.
  4 types of matrices for MTS: (DST7, DST7), (DST7, DCT8) , (DCT8, DST7), (DCT8, DCT8)
Default matrices are shared between DCT2 and MTS
 | DCT2 |  | MTS (DST7, DCT8) | 
Size | Luma | Chroma | Luma | Chroma
2x2 | n/a |  | n/a | n/a
4x4 |  |  |  | n/a
8x8 |  |  |  | n/a
16x16 |  |  |  | n/a
32x32 |  |  |  | n/a
64x64 |  | n/a |  | n/a
[Support of quantization matrices]
seq_parameter_set_rbsp( ) { | Descriptor
. . . | 
scaling_list_enabled_flag | u(1)
if( scaling_list_enabled_flag ) { | 
sps_scaling_list_data_present_flag | u(1)
if( sps_scaling_list_data_present_flag ) { | 
mts_idx = -1 | 
scaling_list_data( ) | 
sps_scaling_list_extension_data_present_flag | u(1)
if( sps_scaling_list_extension_data_present_flag ) | 
for( mts_idx = 0; mts_idx < 4; mts_idx ++) | 
scaling_list_data( ) | 
} | 
} | 
. . . | 
mts_index = 0 : DCT8xDCT8
mts_index = 1 : DCT8xDST7
mts_index = 2 : DST7xDCT8
mts_index = 3 : DST7xDST7

## Slide 9
Proposed syntax modification of scaling_list_data( )
Syntax for quantization matrices of MTS follows that of DCT2.
scaling_list_data( ) {
for( sizeId = 0; sizeId < 6; sizeId++ )
if( mts_idx == -1 )
for( matrixId = 0; matrixId < 6; matrixId += ( sizeId == 5 ) ? 3 : 1 )
if( ! ( ( sizeId == 0 ) && ( matrixId % 3 == 0) ) ) {
matrixIds = (mts_idx+1)*6 + matrixId
scaling_list_pred_mode_flag[ sizeId ][ matrixIds ]
if( !scaling_list_pred_mode_flag[ sizeId ][ matrixIds ] )
scaling_list_pred_matrix_id_delta[ sizeId ][ matrixIds ]
else {
nextCoef = 8
coefNum = Min( 64, ( 1 << ( 4 + ( sizeId << 1 ) ) ) )
if( sizeId > 2 ) {
scaling_list_dc_coef_minus8[ sizeId − 2 ][ matrixIds ]
nextCoef = scaling_list_dc_coef_minus8[ sizeId−2 ][ matrixIds ] + 8
}
for( i = 0; i < coefNum; i++ ) {
scaling_list_delta_coef
nextCoef = ( nextCoef + scaling_list_delta_coef + 256 ) % 256
ScalingList[ sizeId ][ matrixIds ][ i ] = nextCoef
} } }
else
for( matrixId = 0; matrixId < 6; matrixId += 3 )
if( ! (sizeId == 0) ) {
matrixIds = (mts_idx+1)*6 + matrixId
scaling_list_pred_mode_flag[ sizeId ][ matrixIds ]
if( !scaling_list_pred_mode_flag[ sizeId ][ matrixIds ] )
scaling_list_pred_matrix_id_delta[ sizeId ][ matrixIds ]
else {
nextCoef = 8
coefNum = Min( 64, ( 1 << ( 4 + ( sizeId << 1 ) ) ) )
if( sizeId > 2 ) {
scaling_list_dc_coef_minus8[ sizeId − 2 ][ matrixIds ]
nextCoef = scaling_list_dc_coef_minus8[ sizeId−2 ][ matrixIds ] + 8
}
for( i = 0; i < coefNum; i++ ) {
scaling_list_delta_coef
nextCoef = ( nextCoef + scaling_list_delta_coef + 256 ) % 256
ScalingList[ sizeId ][ matrixIds ][ i ] = nextCoef
} } } }
if 2x2 , Chroma Only
if 64x64 Luma Only
Luma Only
DCT2
2x2 is n/a.
Copy Mode
DPCM Mode
Copy Mode
DPCM Mode
MTS

## Slide 10
10
Simulation results
Default matrices that are the same as HEVC are used
BD-rate loss is 1.6% for AI, 0.5% for RA, and 1.1% for LDB
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 1.83% | 0.57% | -1.41% | 104% | 102%
Class A2 | 2.47% | -0.77% | -1.04% | 103% | 104%
Class B | 1.36% | -1.50% | -1.85% | 105% | 101%
Class C | 2.09% | -0.20% | -0.55% | 95% | 107%
Class E | 0.46% | -0.82% | -0.85% | 107% | 102%
Overall | 1.64% | -0.63% | -1.19% | 103% | 103%
Class D | 2.23% | -0.31% | -0.32% | 94% | 115%
Class F | 1.10% | 0.61% | 0.47% | 101% | 104%
 | Random access Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.19% | 1.68% | -1.02% | 106% | 101%
Class A2 | -0.71% | -0.79% | -1.30% | 103% | 102%
Class B | 0.45% | -1.15% | -2.00% | 106% | 101%
Class C | 1.63% | -0.62% | -0.79% | 103% | 111%
Class E |  |  |  |  | 
Overall | 0.48% | -0.37% | -1.34% | 104% | 104%
Class D | 1.86% | -1.54% | -1.43% | 101% | 136%
Class F | 1.02% | 0.86% | 0.54% | 106% | 110%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.59% | -1.76% | -2.68% | 106% | 101%
Class C | 1.91% | -0.85% | -1.02% | 102% | 112%
Class E | 0.83% | 0.90% | -0.78% | 107% | 110%
Overall | 1.09% | -0.79% | -1.65% | 105% | 107%
Class D | 2.06% | -1.76% | -1.31% | 100% | 131%
Class F | 1.26% | -0.01% | -0.26% | 105% | 110%

## Slide 11
11
Conclusions
Characteristics of transform coefficients in a CU is similar between DCT2 and MTS basis functions, but with some differences.
Support of quantization matrices customized for MTS is proposed in case different matrices will be needed for image quality tuning in the future.
Propose to adopt quantization matrices in VTM. It may be considered as a first step to support basic method that matrices are shared between DCT2 and MTS (JVET-L0121).

## Slide 12
12
Thank Sony for cross-checking this proposal !