## Slide 1: JVET-M0103 Deblocking for multi-hypothesis intra inter prediction K. Andersson, J. Enhorn, R. Yu, Z. Zhang, R. Sjöberg (Ericsson)
Kenneth Andersson
Ericsson
2019-01-12

## Slide 2: Summary
Combined intra inter prediction can produce boundaries due to missing deblocking functionality
It is proposed to fix this for next version of VTM by
  deblocking if at least one CU adjacent to a CU boundary uses CIIP,
  also deblock inside the CIIP block at boundaries between sub-blocks with different weights by reusing sub-block functionality already in VVC.
Deblocking is only applied on an 8x8 grid.
Slight improvement in BDR at similar encoding and decoding time.

## Slide 3: Visual artifacts in VTM (LDB Kimono QP=34)

## Slide 4: Application of CIIP deblocking (LDB Kimono QP=34)

## Slide 5: Visual artifacts in VTM (RA Cactus QP=32)

## Slide 6: Application of CIIP deblocking (RA Cactus QP=32)

## Slide 7: Proposed change to VVC
Use sub-block concept to determine boundaries
If CIIP is used on P or Q side
  Set Bs to 1

## Slide 8: WD text
8.3.5 Derivation process for intra prediction mode in combined merge and intra prediction
..
  If IntraPredModeY[ xCb ][ yCb ].is equal to INTRA_ANGULAR50, NumSbY[ xCb ][ yCb ] is set equal to 4 and NumSbX[ xCb ][ yCb ] is set equal to 1,
  Otherwise, if IntraPredModeY[ xCb ][ yCb ] is equal to INTRA_ANGULAR18, , NumSbY[ xCb ][ yCb ] is set equal to 1 and NumSbX[ xCb ][ yCb ] is set equal to 4.
  8.5.2.5 Derivation process of boundary filtering strength
  ..
  Otherwise, if the sample p0 or q0 has ciip_flag equal to 1, bS[ xDi ][ yDj ] is set equal to 1.

## Slide 9: CTC results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,01% | -0,01% | 0,00% | 100% | 100%
Class A2 | -0,01% | -0,05% | 0,09% | 100% | 102%
Class B | -0,02% | -0,02% | 0,02% | 100% | 100%
Class C | -0,01% | 0,00% | 0,04% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0,02% | -0,02% | 0,03% | 100% | 101%
Class D | 0,02% | -0,07% | 0,02% | 100% | 100%
Class F | 0,00% | 0,03% | 0,04% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,02% | -0,20% | 0,04% | 100% | 96%
Class C | 0,02% | 0,19% | 0,01% | 100% | 100%
Class E | -0,06% | 0,04% | -0,44% | 99% | 104%
Overall | 0,00% | -0,01% | -0,09% | 100% | 99%
Class D | -0,02% | 0,38% | -0,02% | 100% | 100%
Class F | 0,00% | 0,31% | -0,14% | 99% | 97%
 | Low delay P Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,03% | 0,05% | -0,05% | 100% | 100%
Class C | -0,02% | 0,04% | -0,09% | 100% | 101%
Class E | -0,12% | -0,41% | -1,15% | 99% | 100%
Overall | -0,05% | -0,07% | -0,34% | 100% | 100%
Class D | 0,01% | -0,28% | -0,24% | 99% | 103%
Class F | 0,08% | -0,50% | -0,26% | 100% | 99%

## Slide 10: Conclusion
It has been shown that deblocking functionality can be used for combined intra inter prediction to remove blocking artifacts.
The proposal set Bs to 1 for a boundary that uses CIIP on at least one side and for boundaries inside a CIIP block that uses different weights by reusing sub-block deblocking functionality already in VVC.
It is proposed to include deblocking for CIIP for next version of VVC
Thanks to Mediatek for cross-check (JVET-M0549)