## Slide 1: JVET-M0105 Non-CE7: Delta QP for Chroma CU
R. Chernyak,
S. Ikonin,
J. Chen

## Slide 2: Background
Current VVC approach:
Delta QP signalling
Delta QP Chroma CU derivation
qPiCb = Clip3( −QpBdOffsetC, 69, QpY + pps_cb_qp_offset + tile_group_cb_qp_offset ) (8‑818) qPiCr = Clip3( −QpBdOffsetC, 69, QpY + pps_cr_qp_offset + tile_group_cr_qp_offset ) (8‑819)

## Slide 3: Proposed solution
Introduce Delta QP signalling for Chroma CU
JVET-L meeting notes on L0428: “On the second aspect: need more time and experts to review. Resubmission to the next meeting was encouraged”.
transform_unit( x0, y0, tbWidth, tbHeight, treeType ) {
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA )
tu_cbf_luma[ x0 ][ y0 ]
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_CHROMA ) {
tu_cbf_cb[ x0 ][ y0 ]
tu_cbf_cr[ x0 ][ y0 ]
}
if( ( tu_cbf_luma[ x0 ][ y0 ] ¦ ¦ tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ] ) && treeType != DUAL_TREE_CHROMA ) {
if( cu_qp_delta_enabled_flag && !IsCuQpDeltaCoded ) {
cu_qp_delta_abs
if( cu_qp_delta_abs )
cu_qp_delta_sign_flag
}
}
CuQpDeltaVal(C) = cu_qp_delta_abs * ( 1 − 2 * *cu_qp_delta_sign_flag )

## Slide 4: Proposed solution (cont’d)
Carry Delta QP between chroma and luma of neighboring block and use as predictor for Chroma CU
qPiCb = Clip3( −QpBdOffsetC, 69, QpY + pps_cb_qp_offset + tile_group_cb_qp_offset + + qPiCb_A – QpY_A_Cb + CuQpDeltaValC)
qPiCr = Clip3( −QpBdOffsetC, 69, QpY + pps_cr_qp_offset + tile_group_cr_qp_offset + + qPiCr_A – QpY_A_Cr + CuQpDeltaValC)
QpY_A_Cb== QpY_A + pps_cb_qp_offset + tile_group_cb_qp_offset QpY_A_Cr== QpY_A + pps_cr_qp_offset + tile_group_cr_qp_offset