## Slide 1: JVET-M0147 Results of Tests 9.2.1, 9.2.2
S. Sethuraman
Ittiam Systems
9 January 2019

## Slide 2: CE9.2.1 – Study items
Primary requirement for DMVR from last meeting
  Restrict internal memory requirements for refinement
    Refinement block size limited to 1024 samples
    Calculate internal memory to avoid accessing pre-fetch cache again for MC
Base method was constrained to not have refinement for CUs with luma sample count greater than 1024 in CE9.2.6 from L-meeting (JVET-L0173)
CE9.2.1 studies the following:
  Impact of the type of interpolation used for refinement
    Nearest rounded integer grid samples (Integer-DMVR)
    Bilinear MC at 1/16th of a pel accuracy with 10-bit accuracy (BiMC-DMVR)
  Impact of cost function
    SAD vs. Block mean removed SAD (B-MR-SAD)
  Impact of using refined MVs for purposes other than current CU’s MC
    CTU-level pipeline
    VPDU-level pipeline
  Impact of force splitting a CU into sub-Pus
    32 width, 32 height vs. 16 width, 16 height

## Slide 3: Recap – Base (CE9.2.1a) Elements
Symmetric bilateral matching that uses equal and opposite delta-MVs in L0 and L1 (JVET-K0041, JVET-K0217)
Final MC restricted to (CU_w + 7)*(CU_h + 7) independent of refinement with use of padded samples – JVET-K0275
Bilinear MC at 1/16th of a pel accuracy for refinement (JVET-K0041, JVET-K0359)
Block mean-removed SAD (MR-SAD) as the cost function (JVET-K0217)
Parametric error surface based on integer distance evaluated cost values (JVET-K0041)
Use of refined MVs for deblocking, TMVP, and spatial prediction of merge/AMVP/affine-MVP from top-left or top CTU neighbor’s refined MV (JVET-K0041, JVET-K0359)
Early exit for DMVR based on MVD w.r.t earlier merge-indices (JVET-K0358)
CU-level early exit for DMVR based on SAD threshold (JVET-K0342)
Computing cost only on every other row (JVET-K0105)
Restricting DMVR for CUs of size less than 64 luma samples (JVET-K0105)
Restrict DMVR for CUs with height=4
Restrict DMVR for CUs of size greater than 1024 luma samples – L Meeting Notes
DMVR was enabled for CUs signaling MMVD and SbTMVP

## Slide 4: Summary of CE9.2.1 Results
S.No | Test case | Description | Y | U | V | EncT | DecT
1 | CE9.2.1a | CE9.2.6 with DMVR disabled for w*h > 1024 | -0.71% | -0.81% | -0.87% | 110.39% | 117.81%
2 | CE9.2.1.b0 | Integer DMVR, SAD, and refined MV used only for MC in Base | -0.30% | -0.39% | -0.44% | 101.40% | 102.58%
3 | CE9.2.1.b | 2 + Enable 32x32 forced split + enabled DMVR for w*h > 1024 also | -0.58% | -0.86% | -0.86% | 101.76% | 106.42%
4 | CE9.2.1.c | 3 + Replace SAD with MR-SAD | -0.66% | -0.88% | -0.92% | 101.73% | 108.31%
5 | CE9.2.1.d | 4 + Replace Integer DMVR with Bilinear MC based | -0.74% | -1.02% | -1.07% | 102.28% | 111.22%
6 | CE9.2.1.e | 5 + use of refined MV for deblocking, TMVP and for spatial MV prediction from top/top-left CTU neighbors | -1.12% | -1.25% | -1.30% | 103.01% | 113.33%
7 | CE9.2.1.f | 6 + use of refined MV also within CTU row from VPDUs that were processed 2 VPDUs behind current VPDU | -1.25% | -1.33% | -1.43% | 102.87% | 113.30%
8 | CE9.2.1.f1 | In 7, MC restricted to use samples within (64+7)*(64+7) for VPDU of CUs larger than 64x64 | -1.25% | -1.33% | -1.42% | 102.75% | 113.40%
9 | CE9.2.1g | In 6, sub-PU size changed from 32x32 to 16x16 | -1.13% | -1.33% | -1.44% | 103.24% | 118.11%

## Slide 5: Comments on the Summary of CE9.2.1 Results
DMVR provides up to 1.25% average luma BDRATE gain (with similar average chroma BDRATE gains) – CE9.2.1f
  Class A1 and A2 have higher gains than other classes
Use of refined MV for purposes other than MC contributes a total of 0.38% out of the 1.13% average BDRATE in CE9.2.1g (significant impact)
  Supplemental results show that using refined MV only for temporal prediction gives 0.26% out of 0.38%
  Using refined MV for deblocking gives ~0.02% out of 0.38%
  Using refined MV for spatial prediction gives ~0.09% out of 0.38%
    VPDU-64 pipeline gives another 0.12% (implying that lower max CTU sizes will benefit more from use of refined MVs spatially)
Use of Bilinear MC gives 0.12% out of 1.13% in CE9.2.1g over integer-DMVR
Use of MR-SAD gives 0.1% over SAD as cost function in CE9.2.1g

## Slide 6: Comments on the Summary of CE9.2.1 Results
Force splitting a CU larger than 1024 luma samples into sub-PUs with independent refinement for each sub-PU improves coding gain
  CE9.2.1b0 vs CE9.2.1b offers 0.28% average luma BDRATE gain
    Gains comes from force splitting Cus larger than 1024 to 32 width, 32 height sub-PUs
  CE9.2.1g force splits to 16 width, 16 height sub-PUs and gives nearly the same gains as CE9.2.1e; preferred because of lower internal memory
DMVR for MMVD and ATMVP are disabled in all tests other than CE9.2.1a
  Reason is the significant increase in EncT % due to MMVD evaluating up to 32 candidates in the SATD stage and all going through DMVR
  Reason is the significant increase in DecT % due to ATMVP DMVR implemented at 8x8 sub-PU level (MC + BDOF happen at 8x8 level)
Forced splitting to sub-Pus significantly increases average decoding time as MC and BDOF now have to happen at a sub-PU level
  32x32 increases DecT % by ~3%
  16x16 increases DecT % by another ~5%

## Slide 7: CE9.2.2
Studies the following 2 aspects
  Replacing block mean removed SAD (B-MR-SAD) with a previous row-mean removed SAD (PR-MR-SAD) to allow a row level pipeline between interpolation and cost evaluation
  Impact of early exit threshold value for SAD
9.2.2c – PR-MR-SAD and SAD threshold of 4 per pixel (for 10-bit)
9.2.2d – In 9.2.2c, increase SAD threshold to 12 per pixel (for 10-bit) for sub-PUs in CUs of size greater than 1024 luma samples
9.2.2f – Study impact of DMVR in the absence of BDOF
9.2.2f1 – Study impact of using refined MVs in 9.2.2c
9.2.2f2 – Study impact of changing cost function to SAD in 9.2.2c

## Slide 8: Summary of CE9.2.2 Results
S.No | Test case | Description | Y | U | V | EncT | DecT
1 | CE9.2.2c | In 9.2.1g, MR-SAD replaced by PR-MR-SAD | -1.07% | -1.27% | -1.36% | 103.20% | 117.69%
2 | CE9.2.2d | In 10, increase early exit threshold for w*h > 1024 to assess DecT impact | -1.04% | -1.27% | -1.36% | 103.20% | 117.27%
3 | CE9.2.2f | Results for 9.2.2(c) when BIO is disabled in both VTM3 and with DMVR + DMVR is enabled for ATMVP and MMVD | -1.51% | -1.58% | -1.59% | 115.98% | 125.70%
4 | CE9.2.2f1 | Disabling refined MV usage for anything other than MC in 9.2.2c | -0.72% | -1.05% | -1.11% | 102.30% | 115.33%
5 | CE9.2.2f2 | Replacing PR-MR-SAD with SAD in 9.2.2c | -1.02% | -1.29% | -1.35% | 102.94% | 115.27%

## Slide 9: Comments on the Summary of CE9.2.2 Results
DMVR in the absence of BDOF provides an average luma BDRATE gain of 1.51% (and similar gains in chroma)
  ATMVP-DMVR and MMVD-DMVR are enabled in this case and offer close to 0.1% out of 1.51%
    Increase both EncT and DecT significantly as explained earlier
  BDOF and DMVR seem to have an overlap of 1.41 – 1.13 = 0.28%
PR-MR-SAD with cost evaluation on alternate rows has a 0.06% average luma BDRATE drop when compared to B-MR-SAD, and a 0.05% gain when compared to SAD
  The drop is very minimal over B-MR-SAD when alternate row cost evaluation is not used
Refined MV usage for purposes other than MC offers 0.35% average luma BDRATE gain (9.2.2f1)
Threshold change from 4 to 12 per pixel for sub-PUs in CUs of size larger than 1024 luma samples had minimal impact of DecT

## Slide 10: Complexity Analysis
To avoid access of data accessed by DMVR from pre-fetch cache from being accessed again, the internal memory requirement is:
  2 x (sub-PU-w + 4 + 7) x (sub-PU-h + 5) 10-bit samples
    For sub-PU-w=16, sub-PU-h=16, this becomes 2 x 27 x 21 10-bit samples
When using SAD or PR-MR-SAD, DMVR requires only 2 x 5 x (sub-PU-w + 4) 10-bit interpolated sample buffers for cost evaluations
Bilinear MC for refinement requires 40% additional multiplications and additions when compared to bi-prediction MC for 8x8 worst-case
  Integer DMVR drops 0.12% over bilinear MC while removing these operations
  JVET-M0148 proposes a simplified method that removes the multiplications with minimal impact to BDRATE (~0.03%)
SAD requires 27% additions over bi-pred MC additions for 8x8 worst-case
PR-MR-SAD and MR-SAD require 52% and 57% additions respectively

## Slide 11: Conclusions
Sub-PU size of 16x16 is proposed that keeps the internal memory requirements very low (1134 10-bit samples) while avoiding repeat access from pre-fetch cache
SAD and PR-MR-SAD require only 200 samples for storing interpolated samples when Integer grid samples are not used
Multiple combinations exist that offer over 1% average BDRATE gain over VTM3 while capping worst-case operations and internal memory requirements
  CE9.2.2c
  CE9.2.2f1
When BIO is disabled in VTM, BDRATE gains are as high as 1.51% with DMVR (CE9.2.2f)
It is requested that CE9.2.2c be considered for adoption into VTM

## Slide 12: THANKS TO ALL CROSS-CHECKERS! Qualcomm, MediaTek, Panasonic, Sharp