## Slide 1: CE3-related: Chroma intra candidates modification based on directional DM (JVET-M0213)
Reporter： MA Yanzhuo, WAN Shuai

## Slide 2: Chroma intra prediction modes in VVC
Chroma mode list in VVC
- DM
- CCLM/LM_L/LM_T
- four default chroma modes
- Planar
- DC
- Vertical
- Horizontal
* Alternative mode (mode 66, to replace the redundant DM mode )
Separate QTBT structures and blocks used by DM

## Slide 3: Proposal
Table 8‑3 – Specification of IntraPredModeC[ xCb ][ yCb ] depending on intra_chroma_pred_mode[ xCb ][ yCb ] and IntraPredModeY[ xCb + cbWidth / 2 ][ yCb + cbHeight / 2 ] when sps_cclm_enabled_flag is equal to 1
intra_chroma_pred_mode[ xCb ][ yCb ] | IntraPredModeY[ xCb + cbWidth / 2 ][ yCb + cbHeight / 2 ] |  |  |  | 
 | 0 | 50 | 18 | 1 | X ( 0 <= X <= 66 )
0 | 66 | 0 | 0 | 0 | 0
1 | 50 | 66 | 50 | 50 | 50
2 | 18 | 18 | 66 | 18 | 18
3 | 1 | 1 | 1 | 66 | 1
4 | 81 | 81 | 81 | 81 | 81
5 | 82 | 82 | 82 | 82 | 82
6 | 83 | 83 | 83 | 83 | 83
7 | 0 | 50 | 18 | 1 | X
intra_chroma_pred_mode[ xCb ][ yCb ] | IntraPredModeY[ xCb + cbWidth / 2 ][ yCb + cbHeight / 2 ] |  | 
 | 0 | 1 | X ( 2 <= X <= 66 )
0 | 66 | 0 | 0
1 | 50 | 50 | X-N
2 | 18 | 18 | X+N
3 | 1 | 66 | 1
4 | 81 | 81 | 81
5 | 82 | 82 | 82
6 | 83 | 83 | 83
7 | 0 | 1 | X

## Slide 4: Obtain modes DM N
If the DM is a directional mode M (2<=M<=66),
the modes M-N and M+N (N>0) are calculated as follows:
M1 = ((M + 62 - N) % 64) + 2;
M2 = (M -2 + N)% 64 + 2;
DM N modes

## Slide 5: Preliminary experiments with different N values
Anchor: VTM3.0
Tested: The proposed DM±N modes method
Condition：AI configurations with 24 frames interval
N=4 is recommended.
BD-rates Performance | Class C |  |  | Class E |  |  | Average |  | 
 | Y | U | V | Y | U | V | Y | U | V
N=2 | -0.02% | -0.61% | -0.86% | -0.04% | -1.12% | -1.00% | -0.03% | -0.86% | -0.93%
N=3 | -0.02% | -0.55% | -0.62% | -0.03% | -0.75% | -0.64% | -0.02% | -0.65% | -0.63%
N=4 | -0.07% | -0.26% | -0.53% | -0.04% | -0.51% | -0.70% | -0.06% | -0.38% | -0.61%
N=5 | -0.05% | -0.31% | -0.57% | -0.02% | -0.33% | -0.33% | -0.03% | -0.32% | -0.45%
N=7 | -0.05% | -0.13% | -0.38% | -0.01% | -0.31% | -0.26% | -0.03% | -0.22% | -0.32%
N=10 | -0.05% | -0.05% | 0.01% | -0.02% | 0.15% | 0.00% | -0.03% | 0.05% | 0.00%

## Slide 6: Results of the proposal
Anchor: VTM3.0
Tested: The proposed method (N = 4)
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.34% | -0.14% |  | 100%
Class A2 | -0.02% | -0.26% | -0.22% |  | 100%
Class B | -0.01% | -0.23% | -0.38% |  | 100%
Class C | -0.03% | -0.31% | -0.58% |  | 101%
Class E | -0.05% | -0.48% | -0.55% |  | 101%
Overall | -0.03% | -0.31% | -0.39% |  | 100%
Class D | -0.04% | -0.33% | -0.47% |  | 101%
Class F | -0.01% | -0.29% | -0.25% |  | 101%

## Slide 7: Results for N=4 in every sequences
 |  | BD-rate (piecewise cubic) |  |  | BD-rate (cubic) |  | 
 |  | Y | U | V | Y | U | V
Class A1 | Tango2 | -0.05% | -0.78% | -0.29% | -0.05% | -0.79% | -0.29%
 | FoodMarket4 | -0.01% | -0.27% | -0.06% | -0.01% | -0.24% | -0.07%
 | Campfire | -0.05% | 0.03% | -0.08% | -0.07% | 0.05% | -0.07%
Class A2 | CatRobot1 | -0.05% | -0.52% | -0.52% | -0.05% | -0.50% | -0.51%
 | DaylightRoad2 | 0.01% | -0.15% | -0.05% | 0.00% | -0.13% | -0.06%
 | ParkRunning3 | -0.03% | -0.13% | -0.12% | -0.03% | -0.13% | -0.13%
Class B | MarketPlace | 0.00% | -0.16% | -0.30% | 0.00% | -0.13% | -0.29%
 | RitualDance | -0.02% | -0.31% | -0.26% | -0.02% | -0.27% | -0.29%
 | Cactus | -0.03% | -0.13% | -0.34% | -0.03% | -0.06% | -0.32%
 | BasketballDrive | -0.01% | -0.25% | -0.51% | -0.02% | -0.25% | -0.48%
 | BQTerrace | 0.00% | -0.28% | -0.50% | -0.01% | -0.27% | -0.47%
Class C | BasketballDrill | -0.03% | -0.67% | -0.93% | -0.03% | -0.74% | -0.95%
 | BQMall | -0.03% | -0.05% | -0.29% | -0.03% | -0.07% | -0.25%
 | PartyScene | 0.00% | -0.16% | -0.28% | 0.00% | -0.12% | -0.27%
 | RaceHorses | -0.06% | -0.36% | -0.85% | -0.06% | -0.39% | -0.88%
Class D | BasketballPass | -0.01% | -0.35% | -0.64% | -0.01% | -0.30% | -0.55%
 | BQSquare | -0.04% | 0.06% | -0.32% | -0.04% | -0.23% | -0.21%
 | BlowingBubbles | -0.02% | -0.76% | -0.20% | -0.02% | -0.66% | -0.23%
 | RaceHorses | -0.08% | -0.28% | -0.71% | -0.08% | -0.18% | -0.73%
ClassE | FourPeople | 0.02% | -0.21% | -0.30% | 0.02% | -0.23% | -0.29%
 | Johnny | -0.10% | -0.74% | -0.95% | -0.10% | -0.73% | -0.98%
 | KristenAndSara | -0.06% | -0.49% | -0.40% | -0.06% | -0.44% | -0.41%
ClassF | BasketballDrillText | 0.00% | -0.57% | -0.74% | 0.00% | -0.52% | -0.74%
 | ArenaOfValor | -0.02% | -0.47% | -0.29% | -0.02% | -0.46% | -0.30%
 | SlideEditing | -0.01% | 0.05% | 0.04% | -0.01% | 0.00% | 0.30%
 | SlideShow | 0.00% | -0.16% | -0.03% | 0.00% | -0.23% | -0.09%

## Slide 8: Thanks