## Slide 1
JVET-M0230
Non-CE4: The Reduction of the Temporal MV Buffer
Yi-Wen Chen, Xianglin Wang

## Slide 2: Introduction
In current VVC, some inter prediction modes such as the affine mode could derive MVs and perform MC at 1/16-pel precision
All MVs are stored at 1/16-pel precision for accurate MV predictions
Temporal MV buffer size in the current VVC is approximately 9Mbits/frame for a 4kx2k video
To reduce the size of temporal MV buffer, it is proposed to store the MVs in 1/4-pel precision instead of 1/16-pel precision

## Slide 3: Results
Anchor: VTM-3.0
Test : Anchor + Proposed Modifications

## Slide 4: Summary
Proposed to store the MVs into temporal MV buffer in 1/4-pel precision instead of 1/16-pel precision
The size of temporal MV buffer could be reduced by 12% with minor coding performance loss
It is recommended to consider adoption of the proposed method into VVC

## Slide 5: Thank you