## Slide 1
JVET-M0232
Non-CE10: Simplification of Intra Mode coding for CIIP
Yi-Wen Chen, Xianglin Wang

## Slide 2: Introduction
An intra prediction mode for CIIP mode is derived from two additional syntax elements: mpm flag and mpm index
The MPM for CIIP is derived as follow.
The left and top neighbouring blocks are set as A and B, respectively
The intra prediction modes of block A and block B, denoted as intraModeA and intraModeB, respectively, are derived as follows:
  Let X be either A or B
  intraModeX is set to DC if 1) block X is not available; or 2) block X is not predicted using the CIIP mode or the intra mode; 3) block B is outside of the current CTU
  otherwise, intraModeX is set to 1) DC or PLANAR if the intra prediction mode of block X is DC or PLANAR; or 2) VERTICAL if the intra prediction mode of block X is a “vertical-like” angular mode (larger than 34), or 3) HORIZONTAL if the intra prediction mode of block X is a “horizontal-like” angular mode (smaller than or equal to 34)
If intraModeA and intraModeB are the same:
  If intraModeA is PLANAR or DC, then the three MPMs are set to {PLANAR, DC, VERTICAL} in that order
  Otherwise, the three MPMs are set to {intraModeA, PLANAR, DC} in that order
Otherwise (intraModeA and intraModeB are different):
  The first two MPMs are set to {intraModeA, intraModeB} in that order
  Uniqueness of PLANAR, DC and VERTICAL is checked in that order against the first two MPM candidate modes; as soon as a unique mode is found, it is added to as the third MPM

## Slide 3: The Proposed Modifications
Remove the MPM process in CIIP
Directly signal the intra modes of CIIP using the truncated unary (TU) codewords as shown in the table below
Modes | General Shape |  |  | Wide Shape |  | Narrow Shape | 
Planar | 1 |  |  | 1 |  | 1 | 
DC | 0 | 1 |  | 0 | 1 | 0 | 1
HOR | 0 | 0 | 1 | - | - | 0 | 0
VER | 0 | 0 | 0 | 0 | 0 | - | -

## Slide 4: Results
Anchor: VTM-3.0
Test : Anchor + Proposed Modifications

## Slide 5: Summary
MPM derivation process is removed from intra mode coding for CIIP
Truncated unary codewords are used to signal the intra modes for CIIP
The results reported show that -0.01% and 0.01% BD-rate increases are incurred with the proposed simplification
It is recommended to adopt the proposed modifications into VVC for CIIP mode.

## Slide 6: Thank you