## Slide 1: CE13: Pre-rotation with Test 1.1a and 1.1b Test 4.2
12 January 2019
Samsung Electronics Co. Ltd

## Slide 2: Introduction
For 360 compression spherical data is projected on to the plane using one of the projection formats eg. Cuebmap, RSP, HCP, ISP etc
Using pre-rotation before the projection content can be made more suitable for the video codecs
It can be seen that there are many edges which are diagonal and more complex region lies in the poles
With pre-rotation it is possible to align these edges to one of the vertical or horizontal angles and complex region can be placed in the equator region
Frame from Gaslamp sequence
Corresponding Gradient Mag. image

## Slide 3: Optimal rotation for Gaslamp sequence
Frame from Gaslamp sequence
Corresponding Gradient Mag. image
Rotated with optimal rotation (140° yaw)
Corresponding Gradient Mag. image

## Slide 4: Proposed algorithm – Pre-processing (No Multipass)
Steps
Downsize the image to 2K size and generate 36 HCP images corresponding to rotation angles multiple of 10 degrees starting from 10 to 360 degrees.
Compute gradient magnitudes and angles for each of these 36 images
Find the image with maximum number of vertical and horizontal gradients from these images. Here we consider gradients between -5 to 5 degrees as horizontal and -85 to 95 degrees as vertical.
After arriving at the best angle at the granularity of 10 degree these steps can be further repeated to reach to 1 degree resolution.
This algorithm can also be applied at RAP level.

## Slide 5: Early termination
Class S2 sequence has very high camera motion (Global motion) for the sequence like Landing2 and Brancastle2
Elementary motion estimation is used to decide to apply rotation
Full sequence
First IRAP

## Slide 6: Results – TEST 13.4.2b vs CE Anchor
 | Sequence | End-to-end WS-PSNR |  | 
 |  | Y | U | V
Class S1 8K | SkateboardInLot | 0.00% | 0.00% | 0.00%
 | ChairLift | -0.37% | -0.42% | -1.16%
 | KiteFlite | 0.12% | -0.43% | 0.17%
 | Harbor | -0.96% | -1.46% | -1.87%
 | Trolley | 0.00% | -0.18% | 0.00%
 | GasLamp | -2.71% | -6.43% | -9.02%
Class S2 6K | Balboa | 0.00% | 0.00% | 0.00%
 | Broadway | 0.00% | 0.00% | 0.00%
 | Landing2 | 0.00% | 0.00% | 0.00%
 | BranCastle2 | 0.00% | 0.00% | 0.00%
 | Class S1 | -0.65% | -1.49% | -1.98%
 | Class S2 | 0.00% | 0.00% | 0.00%
 | All | -0.39% | -0.89% | -1.19%

## Slide 7: Conclusion
For spherical content, rotation can improve the compression gain
For sequences like Gaslamp, with many edges, rotation can help significantly (observed gain ~2.71% for luma component)
Elementary motion estimation is used to decide if rotation need to be applied.
Rotation as a pre-processing method does not need any change in decoder and does not increase decoder complexity
Rotation parameter can be passed to renderer in SEI/VUI information

## Slide 8: Proposed-SEI syntax
spherical_rotation( payloadSize ) { | Descriptor
spherical_rotation_flag | u(1)
if(spherical_rotation_flag) { | 
spherical_rotation_precision | ue(v)
spherical_rotation_yaw | se(v)
spherical_rotation_pitch | se(v)
spherical_rotation_roll | se(v)
} | 
} | 

## Slide 9
Thank you

## Slide 10: RAP level rotation results (CE 13.4.2b vs CE anchor)
Sequence No. | Rap BD-Rate Gain from RAP0 to RAP9 |  |  |  |  |  |  |  |  |  | Rap_Level Bruteforce | Rotation Bruteforce
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | Avg Gain Seq | Avg Gain Seq
SkateboardInLot | -0.68% | -0.29% | -1.02% | -3.28% | -1.46% | -0.92% | -0.78% | -0.53% | -2.28% | -2.06% | -1.33% | -0.60%
ChairliftRide | -0.49% | -0.77% | -0.63% | -0.75% | -0.54% | -0.83% | -0.57% | -0.81% | -0.87% | -0.68% | -0.69% | -0.51%
KiteFlite | -0.16% | -0.02% | -0.02% | -0.04% | -0.06% | -0.06% | 0.00% | -0.03% | -0.04% | -0.03% | -0.05% | -0.02%
Harbor | -1.74% | -1.77% | -1.85% | -1.73% | -1.76% | -1.77% | -2.02% | -1.75% | -1.66% | -2.48% | -1.85% | -1.86%
Trolley | -0.71% | -0.68% | -0.83% | -0.82% | -0.82% | -0.64% | -0.85% | -0.66% | -0.72% | -0.50% | -0.72% | -0.59%
GasLamp | -3.17% | -3.11% | -3.01% | -2.93% | -3.15% | -2.79% | -3.27% | -2.53% | -2.94% | -3.62% | -3.05% | -2.87%
Balboa | -0.52% | -0.30% | -0.30% | -0.69% | -1.77% | -1.82% | -0.64% | -0.25% | -1.25% | -1.19% | -0.87% | -0.67%
Broadway | -0.36% | -0.59% | -0.37% | 0.00% | 0.00% | -0.11% | -0.01% | -0.25% | -0.15% | -0.59% | -0.24% | -0.12%
Landing | -0.37% | 0.00% | -0.47% | -0.36% | -1.67% | -1.53% | -0.79% | -0.57% | -0.48% | -0.14% | -0.64% | -0.45%
BranCastle | -0.38% | -0.34% | -0.31% | -0.26% | -0.39% | -0.77% | -0.79% | -0.71% | -0.85% | -0.77% | -0.56% | -0.38%
Avg Gain | -0.86% | -0.79% | -0.88% | -1.09% | -1.16% | -1.13% | -0.97% | -0.81% | -1.12% | -1.21% | -1.00% | -0.81%
WS-PSNR Luma Component gain

## Slide 11: Results (CE-13.6.2 – L meeting)