## Slide 1: CE10-related: Simplification on combined inter-intra mode prediction （JVET-M0296）
Biao Wang, Semih Esenlik, Anand Meher Kotra,
Han Gao, Jianle Chen

## Slide 2: Problem and Proposed
Problem: complicated MPM list construction for CIIP:
  A 3-MPM list construction based on left and above blocks
  Required rounding operation if left or above is not one of {Planar, DC, Hor, Ver}
  Pruning checks for 3-MPM
  Adjust the 3-MPM list based on block shape:
    When width > 2*height, 3-MPM list excludes Hor, and add one of {Planar, DC, Ver}
    When height> 2* width, 3-MPM list excludes Ver, and add one of {Planar, DC, Hor}
Proposed: a fixed order 3-MPM list without “construction”
  {Planar, Hor, Ver}

## Slide 3: Mpm_flag and mpm_index signaling
 | Val | 3 intra mode candidate list | 4 intra mode candidate list
MPM flag | 0 | (not exist, always 1) | Excluding 3-MPM list from {PLANAR, DC, vertical, horizontal}
 | 1 | use index to indicate intra mode in the 3-MPM list | use index to indicate intra mode in the 3-MPM list
MPM index | 0 | 0 | 0
 | 1 | 10 | 10
 | 2 | 11 | 11
 | Val | Modes | 3-MPM list
MPM flag | 1 |  | Not signaled, always 1
MPM Index | 0 | Planar | 0
 | 1 | Horizonal | 10
 | 2 | Vertical | 11
VTM3.0
Proposed

## Slide 4: Results:
 | Random access Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.03% | 0.02% | 100% | 100%
Class A2 | -0.04% | 0.05% | 0.01% | 100% | 100%
Class B | -0.04% | 0.07% | 0.01% | 100% | 100%
Class C | 0.01% | 0.08% | 0.09% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.02% | 0.05% | 0.03% | 100% | 100%
Class D | -0.02% | -0.08% | 0.00% | 100% | 100%
Class F | -0.01% | -0.02% | -0.04% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.20% | 0.01% | 100% | 101%
Class C | 0.00% | 0.08% | 0.03% | 100% | 99%
Class E | 0.02% | 0.29% | -0.35% | 100% | 100%
Overall | 0.00% | 0.02% | -0.07% | 100% | 100%
Class D | -0.02% | 0.10% | 0.11% | 100% | 100%
Class F | 0.09% | 0.19% | -0.14% | 100% | 99%
Significant simplification with small coding gain:
RA: -0.02%
LDB: 0.00%
LDP: -0.06%
 | Low delay P Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.05% | 0.21% | 0.04% | 100% | 101%
Class C | -0.06% | 0.21% | -0.06% | 100% | 100%
Class E | -0.09% | -0.21% | -0.61% | 100% | 99%
Overall | -0.06% | 0.11% | -0.15% | 100% | 100%
Class D | -0.05% | -0.68% | 0.64% | 100% | 100%
Class F | 0.18% | -0.32% | 0.11% | 100% | 100%

## Slide 5: Summary & Conclusion
A significant simpler MPM list is proposed
  {Planar, Horizontal, Vertical}
  Simpler signaling for mpm_flag and mpm_idx
Significant simplification with small coding gain:
  RA: -0.01%
  LDB: 0.00%
  LDP: -0.06%
Almost the whole corresponding section can be deleted
  JVET-L1001-v9-SpecChange.docx
We suggest to adopt the proposed 3-MPM list for CIIP blocks
Thanks to Tencent for crosschecking

## Slide 6
Thank You
www.huawei.com