## Slide 1
CE7-related:
Joint coding of chrominance residuals
JVET-M0305

## Slide 2: JVET-M0305: Joint coding of chrominance residuals
Proposing a new mode for coding residual chrominance blocks
  A single joint residual for the two chroma blocks in TU
  Add the residual to Cb prediction, deduct from Cr prediction
  Code the joint residual as it was the Cb residual
  One bin indicator to enable the mode (present if Cbfs for Cr and Cb are 1)
Nice coding efficiency improvement
Very little complexity impact
  Encoder needs to check the new mode
  Decoder can bypass Cr transform process when the mode is active
Introduction

## Slide 3: JVET-M0305: Joint coding of chrominance residuals
Example
Encoder
Decoder
Cb
Cr
-Cr
Coded
Cb
Cr = -Cb

## Slide 4: JVET-M0305: Joint coding of chrominance residuals
New function:
void CABACReader::joint_cb_cr( TransformUnit& tu )
{
tu.jointCbCr = m_BinDecoder.decodeBin( Ctx::JointCbCrFlag( 0 ) );
}
Added in CABACReader::residual_coding:
if ( compID == COMPONENT_Cr && TU::getCbf( tu, COMPONENT_Cb ) )
{
joint_cb_cr( tu );
if ( tu.jointCbCr ) // No Cr residual in bitstream in joint Cb-Cr residual mode
return;
}
Added in DecCu::xIntraRecBlk and DecCu::xDecodeInterTU:
if ( tu.jointCbCr && compID == COMPONENT_Cr ) // Cr uses negative of the signaled Cb residual
{
for (int y = 0; y < piResi.height; y++)
for (int x = 0; x < piResi.width; x++)
crResiPel[y*crStride + x] = -cbResiPel[y*cbStride + x];
}
else
Decoder implementation

## Slide 5: JVET-M0305: Joint coding of chrominance residuals
BD-rate savings
Overall | Y | U | V | Ave-UV
AI | -0.29 % | -0.79 % | -2.16 % | -1.48 %
RA | -0.19 % | -1.44 % | -2.00 % | -1.72 %
LD-B | -0.08 % | -2.38 % | -4.83 % | -3.61 %
LD-P | -0.11 % | -2.46 % | -5.08 % | -3.77 %

## Slide 6: JVET-M0305: Joint coding of chrominance residuals
Full results
 |  |  | AI Main10 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.17 % | -1.00 % | 0.15 % | 100 % | 100 %
Class A2 | -0.52 % | -1.71 % | -0.22 % | 104 % | 101 %
Class B | -0.20 % | -0.66 % | -2.84 % | 100 % | 99 %
Class C | -0.30 % | -1.14 % | -3.67 % | 103 % | 100 %
Class E | -0.33 % | 0.57 % | -3.26 % | 101 % | 101 %
Overall | -0.29 % | -0.79 % | -2.16 % | 102 % | 100 %
Class D | -0.25 % | -1.28 % | -3.21 % | 102 % | 100 %
Class F | -0.36 % | -1.84 % | -3.79 % | 103 % | 101 %
 |  |  | RA Main10 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.11 % | -1.74 % | 0.26 % | 104 % | 99 %
Class A2 | -0.33 % | -2.28 % | -0.41 % | 104 % | 98 %
Class B | -0.15 % | -1.06 % | -3.15 % | 102 % | 101 %
Class C | -0.18 % | -1.05 % | -3.47 % | 103 % | 100 %
Class E |  |  |  |  | 
Overall | -0.19 % | -1.44 % | -2.00 % | 103 % | 100 %
Class D | -0.13 % | -1.29 % | -3.03 % | 102 % | 99 %
Class F | -0.43 % | -1.79 % | -3.46 % | 103 % | 99 %

## Slide 7: JVET-M0305: Joint coding of chrominance residuals
Full results
 |  |  | Low delay B Main10 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.14 % | -3.01 % | -4.12 % | 102 % | 94 %
Class C | -0.04 % | -2.97 % | -4.85 % | 102 % | 94 %
Class E | -0.03 % | -0.55 % | -5.98 % | 101 % | 95 %
Overall | -0.08 % | -2.38 % | -4.83 % | 102 % | 94 %
Class D | -0.05 % | -3.73 % | -4.14 % | 102 % | 96 %
Class F | -0.26 % | -3.00 % | -4.05 % | 103 % | 99 %
 |  |  | Low delay P Main10 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.14 % | -2.79 % | -4.24 % | 104 % | 95 %
Class C | -0.07 % | -3.13 % | -5.11 % | 103 % | 94 %
Class E | -0.11 % | -1.01 % | -6.43 % | 103 % | 96 %
Overall | -0.11 % | -2.46 % | -5.08 % | 104 % | 95 %
Class D | -0.06 % | -3.86 % | -4.32 % | 104 % | 95 %
Class F | -0.17 % | -3.85 % | -4.70 % | 106 % | 93 %

## Slide 8: JVET-M0305: Joint coding of chrominance residuals
Very simple new mode with straight-forward implementation
Nice improvements over VTM-3
Summary
Overall | Y | U | V | Ave-UV
AI | -0.29 % | -0.79 % | -2.16 % | -1.48 %
RA | -0.19 % | -1.44 % | -2.00 % | -1.72 %
LD-B | -0.08 % | -2.38 % | -4.83 % | -3.61 %
LD-P | -0.11 % | -2.46 % | -5.08 % | -3.77 %