## Slide 1: JVET-M0333 Non-CE8: Coding on block vector difference
Junghak Nam, Jaehyun Lim, Seung Hwan Kim

## Slide 2: Summary
Proposed schemes
  A coding method for block vector difference in CPR mode
Simulation results (over VTM-3.0 + CPR=1)
  AI: -0.02% (CTC), -0.19% (Class F), -0.41% (SCC)
  RA: 0.00% (CTC), -0.08% (Class F), -0.10% (SCC)
  LD: 0.00% (CTC), -0.09% (Class F), -0.01% (SCC)
Crosscheck: JVET-M0705 (by Tencent)

## Slide 3: Proposed method
For CPR mode, binarization process of abs_mvd_minus2 syntax is coded with Exp-Golomb order K equal to 3 instead of 1
Syntax structure | Syntax element | Binarization | 
 |  | Process | Input parameters
mvd_coding( ) | abs_mvd_greater0_flag[ ] | FL | cMax = 1
 | abs_mvd_greater1_flag[ ] | FL | cMax = 1
 | abs_mvd_minus2[ ] | EGk | CPR? k=3: k=1
 | mvd_sign_flag[ ] | FL | cMax = 1

## Slide 4: Experimental results
 | Over VTM-3.0 |  |  |  |  | Over VTM-3.0 + CPR=1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CTC | 0.08% | -0.04% | 0.07% | 100% | 101% | 0.00% | -0.03% | 0.02% | 101% | 102%
ClassF | -9.94% | -9.92% | -10.08% | 108% | 101% | -0.08% | -0.04% | -0.17% | 101% | 102%
SCC | -22.13% | -21.65% | -22.19% | 104% | 100% | -0.10% | -0.07% | -0.10% | 101% | 104%
 | Over VTM-3.0 |  |  |  |  | Over VTM-3.0 + CPR=1 |  |  |  | 
Test # | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CTC | 0.10% | 0.35% | 0.21% | 108% | 102% | 0.00% | 0.09% | 0.20% | 101% | 102%
ClassF | -5.21% | -5.11% | -4.87% | 109% | 103% | -0.09% | 0.26% | 0.62% | 101% | 103%
SCC | -13.10% | -13.34% | -13.60% | 110% | 101% | -0.01% | 0.08% | 0.03% | 101% | 104%
< Random access >
< Low delay B >
 | Over VTM-3.0 |  |  |  |  | Over VTM-3.0 + CPR=1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CTC | -0.29% | -0.42% | -0.38% | 136% | 103% | -0.02% | -0.02% | -0.05% | 102% | 102%
ClassF | -12.23% | -12.17% | -12.25% | 157% | 103% | -0.19% | -0.18% | -0.20% | 101% | 104%
SCC | -37.20% | -36.34% | -36.60% | 110% | 89% | -0.41% | -0.33% | -0.35% | 101% | 104%
< All intra >