## Slide 1
CE10-related: Simplification of Triangular Partitions
JVET-M0352
The 13th JVET Meeting
Jan. 2019
Dohyeon Park, Yong-Uk Yoon, Jae-Gon Kim (KAU)
Jinho Lee, Jungwon Kang (ETRI)

## Slide 2: Summary
Proposed simplifications to reduce complexity of triangle PU mode
  Test 1: Simplfication of motion vector storage skipping reference picture mapping process
  Test 2: Reduction of the number of motion information combinations
 |  | Over VTM-3.0 |  |  |  | 
 |  | Y | U | V | EncT | DecT
Test 1 | RA | 0.00% | 0.02% | 0.01% | 100% | 100%
 | LB | 0.17% | 0.28% | 0.10% | 100% | 100%
Test 2 | RA | 0.01% | 0.05% | 0.09% | 96% | 100%
 | LB | 0.03% | 0.01% | 0.13% | 94% | 100%

## Slide 3: Background
Triangle prediction mode divides a CU into two triangle prediction units for inter prediction, which makes more flexible inter prediction
In motion vector storage, a bi-prediction MV is stored at the grids located at diagonal areas between triangle PUs
  Reference picture mapping process is performed when the motion vector of each PU has the same reference picture list
The syntax element of a merge_triangle_idx is used to indicate the combinations of the split direction and the motion vectors of two partitions
  split direction(2) index for first PU(5) index for second PU(4)
  The index represents 40 combinations as follows:
    { 0, 1, 0 }, { 1, 0, 1 }, { 1, 0, 2 }, { 0, 0, 1 }, ∙∙∙∙∙∙, { 0, 4, 2 }, { 0, 3, 4 }

## Slide 4: Proposed Simplifications
Proposed simplification 1 – Test 1
  When a bi-directional motion vector is derived, the reference picture mapping process is removed
    If two motion vectors of triangle PUs are from the same list, using the motion vector of the first PU only
Two motion vectors are from L0
Two motion vectors are from L1

## Slide 5: Proposed Simplifications
Proposed simplification 2 – Test 2
  Reduction of the number of motion vector combinations for both partitions
    Restriction to 16 combinations from 40 combinations to be checked
      Size of the LUT is reduced (403 → 163)
    In addition, binarization of the index is modified with fixed length coding and truncated binary coding
IDX | Bins |  |  |  | 
0 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 |  | 
2 | 0 | 1 | 0 |  | 
3 | 0 | 1 | 1 |  | 
4 | 1 | 0 | 0 | 0 | 
5 | 1 | 0 | 0 | 1 | 
6 | 1 | 0 | 1 | 0 | 
7 | 1 | 0 | 1 | 1 | 
8 | 1 | 1 | 0 | 0 | 0
9 | 1 | 1 | 0 | 0 | 1
10 | 1 | 1 | 0 | 1 | 0
11 | 1 | 1 | 0 | 1 | 1
12 | 1 | 1 | 1 | 0 | 0
13 | 1 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1 | 1
      The first bin is regular coded, the remains are bypass coded

## Slide 6: Proposed Simplifications
Specifications using merge_triangle_idx in VTM3.0
Proposed specifications using merge_triangle_idx
merge_triangle_idx[ xCb ][ yCb ] | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
m | 1 | 0 | 0 | 0 | 2 | 0 | 0 | 1 | 3 | 4 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 2
n | 0 | 1 | 2 | 1 | 0 | 3 | 4 | 0 | 0 | 0 | 2 | 2 | 2 | 4 | 3 | 3 | 4 | 4 | 3 | 1
merge_triangle_idx[ xCb ][ yCb ] | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39
m | 2 | 2 | 4 | 3 | 3 | 3 | 4 | 3 | 2 | 4 | 4 | 2 | 4 | 3 | 4 | 3 | 2 | 2 | 4 | 3
n | 0 | 1 | 3 | 0 | 2 | 4 | 0 | 1 | 3 | 1 | 1 | 3 | 2 | 2 | 3 | 1 | 4 | 4 | 2 | 4
merge_triangle_idx[ xCb ][ yCb ] | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
triangleDir | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1
merge_triangle_idx[ xCb ][ yCb ] | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39
triangleDir | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0
merge_triangle_idx[ xCb ][ yCb ] | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
triangleDir | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
merge_triangle_idx[ xCb ][ yCb ] | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
m | 1 | 0 | 0 | 0 | 2 | 0 | 0 | 1 | 3 | 4 | 0 | 1 | 1 | 0 | 0 | 1
n | 0 | 1 | 2 | 1 | 0 | 3 | 4 | 0 | 0 | 0 | 2 | 2 | 2 | 4 | 3 | 3

## Slide 7: Experimental Results
Test 1: Removing the reference picture mapping process
Test 2: Reduction of the number of motion information combinations
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.02% | 0.07% | 100% | 100%
Class A2 | 0.00% | 0.21% | 0.11% | 100% | 100%
Class B | 0.00% | 0.01% | -0.02% | 100% | 100%
Class C | 0.02% | -0.12% | -0.06% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.02% | 0.01% | 100% | 100%
Class D | -0.05% | -0.03% | 0.03% | 100% | 100%
Class F | -0.01% | 0.00% | 0.01% | 100% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.11% | -0.05% | 0.03% | 100% | 100%
0.18% | 0.37% | 0.34% | 100% | 100%
0.26% | 0.71% | -0.09% | 100% | 99%
0.17% | 0.28% | 0.10% | 100% | 100%
0.06% | -0.22% | 0.27% | 100% | 100%
0.08% | 0.13% | 0.19% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.04% | 0.08% | 96% | 100%
Class A2 | 0.01% | 0.08% | 0.10% | 95% | 100%
Class B | 0.01% | 0.02% | 0.01% | 96% | 100%
Class C | 0.03% | 0.14% | 0.17% | 95% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | 0.05% | 0.09% | 96% | 100%
Class D | 0.03% | 0.02% | -0.04% | 95% | 101%
Class F | 0.04% | 0.02% | 0.01% | 94% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.03% | -0.25% | -0.17% | 95% | 100%
0.07% | 0.25% | 0.19% | 95% | 101%
0.00% | 0.12% | -0.48% | 92% | 100%
0.03% | 0.01% | -0.13% | 94% | 100%
0.04% | 0.18% | 0.46% | 94% | 101%
0.09% | 0.31% | 0.21% | 93% | 100%

## Slide 8: Experimental Results
Test 3: Test 1 + Test 2
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.09% | 0.02% | 96% | 100%
Class A2 | 0.00% | 0.06% | 0.16% | 96% | 100%
Class B | 0.03% | 0.05% | 0.07% | 96% | 100%
Class C | 0.05% | 0.14% | 0.13% | 95% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | 0.05% | 0.10% | 96% | 100%
Class D | 0.03% | 0.04% | -0.10% | 95% | 100%
Class F | 0.02% | 0.04% | 0.01% | 94% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.14% | -0.04% | 0.20% | 95% | 100%
0.25% | 0.45% | 0.51% | 95% | 100%
0.26% | 0.80% | 0.26% | 93% | 100%
0.20% | 0.33% | 0.32% | 94% | 100%
0.19% | 0.41% | 0.84% | 94% | 100%
0.19% | 0.43% | 0.20% | 93% | 99%

## Slide 9: Conclusions
Proposed two simplifications
  Skipping the reference picture mapping process (Test 1)
  Reducing the number of motion information combinations (Test 2)
Test 1
  Reference picture mapping process can be removed without loss in RA
  Suggest to study in CE to reduce loss in LDB (0.17%)
Test 2
  Number of cost checks for triangle partitions can be reduced with minor loss
  Encoding time reduction: 4% in RA, 6% in LDB
  Suggest to adopt in the next VTM