## Slide 1: JVET-M0354 CE6-related: MTS with Haar transform for Screen Contents Coding
January 2019
Karam NASER, Franck GALPIN and Tangi POIRIER - Technicolor

## Slide 2: Motivation
  Haar transform is characterized by:
    Smooth basis functions with sharp edges
    Very simple to implement (multiplication free)
    Proved to be good transform for special signal (SCC, Depth maps)
  Proposal:
    Utilize Haar transform in VTM
2D basis of Haar transform (8x8)

## Slide 3: Idea
  VTM transform design:
    (DCT2,DCT2) as core transform
    (DST7, DST7), (DST7, DCT8), (DCT8, DST7) (DCT8, DCT8) as MTS
  Embed Haar in MTS:
    (DCT2,DCT2) as core transform
    (DST7, DST7), (DST7, Haar), (Haar, DST7) (Haar, Haar) as MTS

## Slide 4: Simulation Results
  Results over VTM-3.0 (Class F)
 | Y | U | V | EncT | DecT
BasketballDrillText | 0.08% | -0.26% | -0.13% |  | 
ArenaOfValor | 0.11% | 0.17% | -0.05% |  | 
SlideEditing | -1.23% | -0.66% | -0.57% |  | 
SlideShow | -0.34% | 0.08% | 0.42% |  | 
Average | -0.35% | -0.17% | -0.08% | 101% | 100%
 | Y | U | V | EncT | DecT
BasketballDrillText | -0.03% | -0.02% | -0.15% |  | 
ArenaOfValor | -0.02% | -0.09% | -0.03% |  | 
SlideEditing | -1.30% | -0.62% | -0.64% |  | 
SlideShow | -0.49% | -0.36% | 0.19% |  | 
Average | -0.46% | -0.27% | -0.16% | 102% | 99%
 | Y | U | V | EncT | DecT
BasketballDrillText | 0.12% | -0.26% | 0.02% |  | 
ArenaOfValor | -0.03% | 0.03% | 0.01% |  | 
SlideEditing | -0.94% | -0.23% | -0.51% |  | 
SlideShow | -0.44% | 1.36% | 0.23% |  | 
Average | -0.32% | 0.22% | -0.06% | 101% | 107%
AI 
RA 
LBD 

## Slide 5: Simulation Results
  Results over VTM-3.0 (Class TGM)
 | Y | U | V | EncT | DecT
sc_flyingGraphics | -0.32% | -0.23% | -0.34% |  | 
sc_console | -0.86% | -0.38% | -0.35% |  | 
sc_desktop | -0.75% | -0.31% | -0.30% |  | 
ChineseEditing | -1.40% | -0.69% | -0.69% |  | 
Average | -0.83% | -0.40% | -0.42% | 103% | 101%
 | Y | U | V | EncT | DecT
sc_flyingGraphics | -1.00% | -0.40% | -0.35% |  | 
sc_console | -1.61% | -0.63% | -0.63% |  | 
sc_desktop | -1.06% | -0.48% | -0.37% |  | 
ChineseEditing | -1.67% | -0.73% | -0.76% |  | 
Average | -1.34% | -0.56% | -0.53% | 102% | 103%
 | Y | U | V | EncT | DecT
sc_flyingGraphics | -0.16% | 0.01% | -0.11% |  | 
sc_console | -0.40% | -0.22% | -0.18% |  | 
sc_desktop | -0.32% | -0.34% | -0.07% |  | 
ChineseEditing | -0.18% | -0.39% | -0.38% |  | 
Average | -0.26% | -0.23% | -0.19% | 118% | 112%
AI 
RA 
LBD 

## Slide 6: Simulation Results
  Results over VTM-3.0 (Class F)
    CPR=1
 | Y | U | V | EncT | DecT
BasketballDrillText | 0.01% | -0.52% | -0.25% |  | 
ArenaOfValor | 0.12% | 0.00% | 0.00% |  | 
SlideEditing | -0.55% | -0.18% | -0.23% |  | 
SlideShow | 0.02% | -0.09% | 0.03% |  | 
Average | -0.10% | -0.20% | -0.11% | 102% | 106%
 | Y | U | V | EncT | DecT
BasketballDrillText | -0.05% | -0.13% | -0.17% |  | 
ArenaOfValor | -0.03% | -0.09% | -0.05% |  | 
SlideEditing | -0.59% | -0.19% | -0.23% |  | 
SlideShow | -0.35% | -0.46% | 0.13% |  | 
Average | -0.25% | -0.22% | -0.08% | 103% | 109%
 | Y | U | V | EncT | DecT
BasketballDrillText | 0.08% | -0.43% | 0.00% |  | 
ArenaOfValor | 0.00% | 0.13% | 0.15% |  | 
SlideEditing | -0.86% | -0.44% | -0.36% |  | 
SlideShow | -0.16% | 0.26% | 0.81% |  | 
Average | -0.23% | -0.12% | 0.15% | 117% | 112%
AI 
RA 
LBD 

## Slide 7: Simulation Results
  Results over VTM-3.0 (Class TGM)
    CRP=1
 | Y | U | V | EncT | DecT
sc_flyingGraphics | -0.22% | -0.05% | -0.16% |  | 
sc_console | -0.54% | -0.30% | -0.16% |  | 
sc_desktop | -0.46% | -0.19% | -0.19% |  | 
ChineseEditing | -0.46% | -0.19% | -0.19% |  | 
Average | -0.45% | -0.19% | -0.16% | 104% | 105%
 | Y | U | V | EncT | DecT
sc_flyingGraphics | -0.48% | -0.12% | -0.07% |  | 
sc_console | -1.08% | -0.38% | -0.45% |  | 
sc_desktop | -0.54% | -0.13% | -0.22% |  | 
ChineseEditing | -0.66% | -0.14% | -0.20% |  | 
Average | -0.69% | -0.19% | -0.24% | 108% | 101%
 | Y | U | V | EncT | DecT
sc_flyingGraphics | -0.03% | 0.08% | 0.02% |  | 
sc_console | -0.11% | -0.18% | -0.04% |  | 
sc_desktop | -0.04% | 0.30% | 0.03% |  | 
ChineseEditing | 0.08% | -0.24% | -0.11% |  | 
Average | -0.02% | -0.01% | -0.02% | 118% | 111%
AI 
RA 
LBD 

## Slide 8: Additional Results
  Testing the impact on natural sequences
    RA CTC
 | Random Access Main 10 |  |  |  | 
 | Over VTM 3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.11% | 0.24% | 0.13% | 115% | 107%
Class A2 | 0.13% | 0.02% | 0.11% | 116% | 108%
Class B | 0.14% | 0.17% | -0.08% | 116% | 107%
Class C | 0.08% | -0.26% | 0.05% | 119% | 108%
Class E |  |  |  |  | 
Overall | 0.12% | 0.04% | 0.04% | 117% | 107%
Class D | 0.01% | -0.20% | -0.11% | 120% | 108%

## Slide 9: Summary
  Haar transform:
    Simple + efficient for SCC
    Significant coding gain ( especially for TGM and AI cfg: 1.34%)
    little loss for natural sequences (0.12% on RA CTC)
  Conclusion
    Can be either restricted to screen contents or for all sequences with small loss