## Slide 1: JVET-M0360 Video coding based on Cross Random-access-point Referencing (CRR)
Hualong Yu,
Xiaoding Gao,
Qichao Yuan,
Xinyu Lin,
Lu Yu
Zhejiang University
YuQun Fan,
Yin Zhao,
Haitao Yang,
Ye-Kui Wang,
Jianle Chen
Huawei

## Slide 2: Conventional Video Coding
  Videos are divided into Random Access Segments (RASs) by random access points.
  Picture decoding can only reference to pictures in the same RAS but not pictures in other RASs.
Video
Referenced
Dependent
Random Access Segment
RAP picture

## Slide 3: Temporal Correlation in Video
Temporal correlation between different RASs widely exists in
Movie, drama, conferencing, surveillance, etc.
Similar scenes or subjects appear repeatedly or alternatively.
But temporal correlation between different RASs have not been used since video sequence is isolated into segments to provide the functionality of random access.
[1] Pictures from movie “The Man from Earth”
Presentation Time
Random Access Point
Random Access Segment
Temporal Correlated

## Slide 4: Cross RAP Referencing (CRR) Coding
fully use temporal correlation between RASs
keep the functionality of random access

## Slide 5: Cross RAP Referencing (CRR) Coding
Extract representative pictures from RASs with similar scenes and subjects.
[1] Pictures from movie “The Man from Earth”
Presentation Time
Random Access Point
Random Access Segment
Temporal Correlated

## Slide 6: Cross RAP Referencing (CRR) Coding
The representative pictures are coded as Library Pictures.
Same library picture may be referenced by multiple RASs
  Exploit long-term correlation
  High coding efficiency
[1] Pictures from movie “The Man from Earth”
Presentation Time
Random Access Point
Random Access Segment

## Slide 7: Cross RAP Referencing (CRR) Coding
Library pictures are coded into library stream.
Video segments reference to the library pictures are coded into main stream.
Encoder
Input Video
Output Video
Decoder
Library Encoder
Library Decoder
Main Stream
Library Stream
Pre-analyzer

## Slide 8: Cross RAP Referencing (CRR) Coding
Keep random access function.
Main Stream
Library Stream
Main Stream
Library Stream
Main Stream
Library Stream
Notes: With two separate stream, random access function can be supported. In this example, gray pictures marked as P1~7 in main stream are first pictures in each segments and the main stream reference to two library pictures in library stream, the blue L1 and red L2.

## Slide 9: Cross RAP Referencing (CRR) Coding
Keep random access function.
Main Stream
Library Stream
Main Stream
Library Stream
Main Stream
Library Stream

## Slide 10: Cross RAP Referencing (CRR) Coding
Keep random access function.
Main Stream
Library Stream
Main Stream
Library Stream
Main Stream
Library Stream
Notes: With two separate stream, random access function can be supported. In this example, gray pictures marked as P1~7 in main stream are first pictures in each segments and the main stream reference to two library pictures in library stream, the blue L1 and red L2. If the video plays from beginning, the L1 and L2 is transmitted when they are referenced the first time at P1 and P3. As for other pictures reference to the same library pictures

## Slide 11: Cross RAP Referencing (CRR) Coding
Keep random access function.
Main Stream
Library Stream
Main Stream
Library Stream
Main Stream
Library Stream
Notes: With two separate stream, random access function can be supported. In this example, gray pictures marked as P1~7 in main stream are first pictures in each segments and the main stream reference to two library pictures in library stream, the blue L1 and red L2. If the video plays from beginning, the L1 and L2 is transmitted when they are referenced the first time at P1 and P3. As for other pictures reference to the same library pictures

## Slide 12: What need to be standardized
Coding Layer
  Sequence/Picture Level: extension required
    sequence level indication of whether using CRR
    indication of referencing to Library picture in RPS
    management of DPB
  CTU-level: Current designs remain the same.
System layer:
  ISOBMFF and DASH can handle the association and synchronization of library-stream pictures and main-stream pictures.
  Similar systems operations for other systems environments can be designed.

## Slide 13
Test configuration: RA configuration of VVC CTC.
VTM3.0 with CRR vs. VTM3.0 without CRR.
All Average Gain: -11.21%
Experiment results
 |  | Y | U | V
A1 | Tango2 | -0.51% | 0.56% | -0.51%
 | FoodMarket4 | -0.02% | -1.18% | -1.02%
 | Campfire | -2.81% | -0.61% | -4.83%
A2 | CatRobot1 | -7.70% | -8.21% | -8.27%
 | DaylightRoad2 | -4.88% | -4.69% | -9.21%
 | ParkRunning3 | 0.16% | -0.76% | -0.82%
B | MarketPlace | -2.50% | -2.63% | -2.35%
 | RitualDance | -0.16% | -2.06% | 0.55%
 | Cactus | -15.29% | -15.25% | -14.98%
 | BasketballDrive | -0.92% | -0.56% | -0.59%
 | BQTerrace | -14.06% | -15.04% | -12.28%
C | BasketballDrill | -29.64% | -36.71% | -33.16%
 | BQMall | -4.27% | -4.41% | -4.05%
 | PartyScene | -9.85% | -13.74% | -13.28%
 | RaceHorses | -0.41% | -0.65% | -1.20%
D | BasketballPass | -2.73% | -5.59% | -4.46%
 | BQSquare | -11.43% | -16.62% | -14.29%
 | BlowingBubbles | -6.10% | -6.74% | -7.92%
 | RaceHorses | -0.88% | -2.51% | -2.38%
F | BasketballDrillText | -27.01% | -32.51% | -31.19%
 | ArenaOfValor | -9.73% | -10.16% | -10.01%
 | SlideEditing | -75.20% | -76.73% | -76.31%
 | SlideShow | -31.98% | -32.71% | -32.60%
 | All ABCDF | -11.21% | -12.59% | -12.40%

## Slide 14
Test configuration: RA configuration of HEVC CTC.
HM16.15 with CRR vs. HM16.15 without CRR.
All Average Gain: -19.6%
Experiment results
 | BD-Rate |  | 
 | Y | U | V
Class A | -8.2% | -15.3% | -18.7%
Class B | -10.5% | -23.1% | -25.3%
Class C | -14.8% | -24.7% | -24.0%
Class D | -6.3% | -22.3% | -22.7%
Class E | -44.6% | -69.8% | -69.3%
Class F | -41.7% | -51.6% | -49.3%
Average ABCD | -10.0% | -21.4% | -22.8%
Average All | -19.6% | -32.5% | -33.0%

## Slide 15
5 Drama test sequences with length ranging from 136s to 152s with RA configuration of VVC CTC.
VTM3.0 with CRR vs. VTM3.0 without CRR.
Experiment results
Sequence | Resolution | Fps | Frame | Length (s)
Bigbang | 640x360 | 30 | 4080 | 136
Cards | 640x360 | 30 | 4337 | 144
Earthman | 640x360 | 30 | 4339 | 144
Girls | 640x360 | 30 | 4567 | 152
Sherlock | 640x360 | 30 | 4553 | 151
 | Y | U | V | Enc Time | Dec Time
Bigbang | -20.23% | -20.63% | -20.41% | 115% | 104%
Cards | -33.45% | -32.43% | -33.57% | 131% | 101%
Earthman | -27.23% | -23.41% | -26.26% | 126% | 98%
Girls | -23.03% | -21.41% | -21.97% | 119% | 103%
Sherlock | -25.59% | -24.18% | -25.21% | 123% | 100%
All | -25.91% | -24.41% | -25.48% | 122% | 101%

## Slide 16
5 Drama test sequences with length ranging from 136s to 152s with RA configuration of HEVC CTC.
HM16.15 with CRR vs. HM16.15 without CRR.
Experiment results
 | Y | U | V
Bigbang | -29.5% | -38.4% | -37.5%
Card | -46.2% | -53.4% | -53.1%
Earthman | -36.2% | -45.1% | -43.9%
Girls | -34.9% | -45.7% | -44.1%
Sherlock | -40.1% | -49.7% | -49.2%
All | -37.38% | -46.46% | -45.56%

## Slide 17: Conclusion
Preliminary test results show that CRR in video coding can provide significant coding gain.
High level syntax needs to be extended to support CRR, while current CTU-level design in VVC does not need any change.
We recommend to establish a CE to further study the technology.

## Slide 18: Thanks Thank Bytedance for cross checking (M0855)