## Slide 1: JVET-M0366 Transform Simplification
Christopher Hollmann, Davood Saffar,
Per Wennersten, Jacob Ström
Christopher Hollmann
Ericsson
2019-01-09

## Slide 2: Introduction
MTS tool allows a total of 5 possible combinations of transform:
  DCT-2 horizontal and vertical
  DST-7 horizontal and vertical
  DST-7 horizontal and DCT-8 vertical
  DCT-8 horizontal and DST-7 vertical
  DCT-8 horizontal and vertical
Very uneven usage distribution
mts_cu_flag
mts_tu_idx
DCT-2 hor
DCT-2 ver
DST-7 hor
DCT-8 hor
DCT-8 ver
DST-7 ver
DCT-8 ver
DST-7 ver
20%
60%
10%
10%
2%

## Slide 3: Proposed changes (1)
Remove combination DCT-8 horizontal and vertical
Replace size 32 DCT-8 with existing DCT-2
Replace mts_tu_idx with two flags:
  mts_dst_flag: DST-7 horizontal and vertical
  mts_tu_flag: DST-7 and DCT-8 horizontal and vertical
mts_cu_flag
mts_dst_flag
DCT-2 hor
DCT-2 ver
DST-7 hor+ver
mts_tu_flag
Combination of DCT-X and DST-7

## Slide 4: Proposed changes (2)
Intra mode |  | 0-34 | 35-66
Hor | Ver |  | 
DST-7 | DCT-X | 0 | 1
DCT-X | DST-7 | 1 | 0
mts_tu_flag: 1 context (as in VTM-3.0)
Code more probable mode based on block size (inter) or intra mode (intra)
Hor | Ver | H > W | H <= W
DST-7 | DCT-X | 0 | 1
DCT-X | DST-7 | 1 | 0
Intra Mode |  | 10-22, 46-57 | 0-9, 23-45, 58-66
size | N = |  | 
32xN, Nx32 | 4, 8, 16, 32 | 0 | 1
16xN, Nx16 | 4, 8, 16 | 2 | 3
4xN, 8xN | 4, 8 | 4 | 5
mts_cu_flag: 6 contexts (as in VTM-3.0)
Based on block size (inter + intra) and intra mode (only intra)
 | Nx4 | Nx8 | Nx16 | Nx32
4xN | 5 | 2 | 1 | 0
8xN | 2 | 5 | 3 | 1
16xN | 1 | 3 | 4 | 3
32xN | 0 | 1 | 3 | 4

## Slide 5: Results
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 with MTS Inter On |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | 0,12% | -0,15% | 0,10% | 95% | 100%
Class E | 0,08% | 0,47% | -0,81% | 96% | 99%
Overall |  |  |  |  | 
Class D | 0,11% | -0,51% | -0,34% | 97% | 100%
Class F | -0,07% | 0,16% | -0,34% | 97% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 with MTS Inter On |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,05% | -0,12% | 0,07% | 96% | 99%
Class A2 |  |  |  |  | 
Class B | 0,05% | 0,06% | -0,08% | 97% | 100%
Class C | 0,04% | -0,20% | -0,15% | 96% | 99%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0,04% | -0,73% | -0,18% | 96% | 99%
Class F | -0,03% | 0,02% | 0,05% | 96% | 99%
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,07% | 0,00% | 0,02% | 87% | 98%
Class A2 | -0,05% | 0,07% | -0,01% | 89% | 99%
Class B | -0,05% | -0,09% | -0,04% | 87% | 99%
Class C | -0,02% | -0,07% | -0,18% | 88% | 99%
Class E | -0,09% | 0,03% | -0,01% | 88% | 100%
Overall | -0,05% | -0,03% | -0,05% | 88% | 99%
Class D | -0,02% | 0,02% | -0,09% | 88% | 100%
Class F | -0,01% | -0,08% | 0,02% | 88% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,02% | 0,13% | 0,06% | 98% | 99%
Class A2 | -0,06% | -0,10% | 0,05% | 98% | 101%
Class B | -0,03% | 0,20% | -0,11% | 98% | 101%
Class C | 0,01% | -0,38% | 0,00% | 98% | 100%
Class E |  |  |  |  | 
Overall | -0,02% | -0,03% | -0,01% | 98% | 100%
Class D | 0,00% | -0,64% | -0,06% | 97% | 101%
Class F | -0,03% | 0,11% | 0,04% | 97% | 102%
According to CTC
CTC with MTS enabled for Inter
LDB: 0.00% 0.33% -0.10% 99% 99%

## Slide 6: Summary & Recommendation
Recommendation:
Adopt this proposal into VTM-4.0
4 changes:
No DCT-8 horizontal and vertical
Replace size-32 DCT-8 with DST-7
New flags instead of mts_tu_idx
Change context selection for mts_cu_flag

## Slide 8: Buggy Test Results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 with EMT = 3 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,01% | -0,16% | -0,02% | 100% | 144%
Class A2 | 0,11% | -0,06% | -0,02% | 104% | 139%
Class B | 0,02% | -0,15% | -0,12% | 113% | 156%
Class C | -0,02% | 0,10% | 0,09% | 118% | 155%
Class E |  |  |  |  | 
Overall | 0,03% | -0,07% | -0,02% | 110% | 150%
Class D | 0,03% | -0,16% | -0,11% | 115% | 173%
Class F | -0,04% | -0,02% | 0,09% | 113% | 195%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 with EMT = 3 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,10% | -0,11% | -0,16% | 123% | 176%
Class C | 0,07% | -0,38% | 0,21% | 90% | 137%
Class E | 0,05% | 0,77% | -1,22% | 97% | 191%
Overall | 0,08% | 0,02% | -0,30% | 105% | 165%
Class D | 0,09% | -0,48% | -0,45% | 115% | 161%
Class F | 0,01% | -0,25% | 0,09% | 121% | 221%
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,05% | -0,05% | 0,07% | 87% | 98%
Class A2 | -0,03% | -0,01% | -0,01% | 89% | 99%
Class B | -0,03% | -0,06% | -0,09% | 87% | 99%
Class C | -0,01% | -0,08% | -0,19% | 88% | 99%
Class E | -0,05% | -0,06% | -0,13% | 88% | 100%
Overall | -0,03% | -0,06% | -0,08% | 88% | 99%
Class D | -0,02% | -0,03% | 0,00% | 88% | 100%
Class F | 0,01% | -0,01% | 0,07% | 88% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,02% | 0,05% | 98% | 99%
Class A2 | -0,03% | 0,12% | 0,14% | 98% | 101%
Class B | -0,03% | 0,09% | -0,05% | 98% | 101%
Class C | 0,00% | 0,04% | 0,06% | 98% | 100%
Class E |  |  |  |  | 
Overall | -0,01% | 0,07% | 0,04% | 98% | 100%
Class D | -0,06% | -0,31% | -0,19% | 97% | 101%
Class F | -0,06% | 0,10% | 0,14% | 97% | 102%
LDB: 0,00% 0,19% -0,11% 99% 99%

## Slide 9: Only remove DCT-8 hor + ver
 | Random Access Main 10 |  | 
 | Over VTM-3.0 |  | 
 | Y | U | V
Class A1 | 0,00% | -0,10% | 0,08%
Class A2 | -0,03% | 0,05% | 0,04%
Class B | 0,00% | 0,14% | -0,01%
Class C | 0,00% | -0,20% | 0,00%
Class E |  |  | 
Overall | -0,01% | -0,02% | 0,02%
Class D | 0,01% | -0,32% | -0,07%
Class F | -0,01% | 0,15% | -0,04%
 | All Intra Main10 |  | 
 | Over VTM-3.0 |  | 
 | Y | U | V
Class A1 | 0,03% | -0,08% | 0,01%
Class A2 | 0,04% | -0,02% | -0,02%
Class B | 0,02% | -0,06% | -0,03%
Class C | 0,01% | -0,05% | -0,11%
Class E | 0,02% | 0,01% | -0,06%
Overall | 0,02% | -0,04% | -0,04%
Class D | 0,02% | -0,03% | -0,11%
Class F | -0,02% | -0,04% | 0,12%

## Slide 10: Remove DCT-8 hor + ver Replace size 32 DCT-8 with DCT-2
 | Random Access Main 10 |  | 
 | Over VTM-3.0 |  | 
 | Y | U | V
Class A1 | 0,00% | 0,06% | 0,11%
Class A2 | -0,03% | -0,05% | 0,11%
Class B | -0,02% | 0,08% | -0,19%
Class C | -0,01% | -0,09% | 0,04%
Class E |  |  | 
Overall | -0,02% | 0,01% | -0,01%
Class D | -0,03% | -0,41% | -0,28%
Class F | -0,05% | 0,00% | 0,07%
 | All Intra Main10 |  | 
 | Over VTM-3.0 |  | 
 | Y | U | V
Class A1 | -0,05% | -0,03% | 0,05%
Class A2 | -0,01% | 0,03% | -0,01%
Class B | -0,02% | -0,07% | -0,01%
Class C | 0,00% | -0,07% | -0,10%
Class E | 0,01% | -0,01% | 0,01%
Overall | -0,01% | -0,04% | -0,02%
Class D | -0,01% | -0,07% | -0,13%
Class F | 0,01% | -0,07% | 0,00%

## Slide 11: Remove DCT-8 hor + ver Replace size 32, change mts_cu_flag
 | Random Access Main 10 |  | 
 | Over VTM-3.0 |  | 
 | Y | U | V
Class A1 | -0,03% | -0,13% | 0,06%
Class A2 | -0,04% | -0,07% | 0,02%
Class B | -0,02% | 0,08% | 0,01%
Class C | -0,01% | -0,07% | 0,04%
Class E |  |  | 
Overall | -0,03% | -0,04% | 0,03%
Class D | -0,03% | -0,52% | -0,14%
Class F | -0,01% | 0,06% | 0,01%
 | All Intra Main10 |  | 
 | Over VTM-3.0 |  | 
 | Y | U | V
Class A1 | -0,06% | -0,06% | 0,05%
Class A2 | -0,03% | 0,01% | -0,04%
Class B | -0,04% | -0,03% | -0,05%
Class C | -0,01% | -0,07% | -0,18%
Class E | -0,05% | -0,05% | 0,08%
Overall | -0,04% | -0,04% | -0,04%
Class D | -0,02% | -0,06% | 0,11%
Class F | 0,00% | -0,07% | 0,00%

## Slide 12: Remove DCT-8 hor + ver Replace size 32, change mts_tu_idx
 | Random Access Main 10 |  | 
 | Over VTM-3.0 |  | 
 | Y | U | V
Class A1 | -0,02% | -0,11% | -0,01%
Class A2 | -0,04% | 0,06% | 0,08%
Class B | -0,02% | 0,12% | 0,07%
Class C | 0,04% | -0,06% | 0,08%
Class E |  |  | 
Overall | -0,01% | 0,01% | 0,06%
Class D | 0,00% | -0,42% | 0,04%
Class F | -0,03% | 0,06% | -0,21%
 | All Intra Main10 |  | 
 | Over VTM-3.0 |  | 
 | Y | U | V
Class A1 | -0,06% | -0,10% | -0,02%
Class A2 | -0,02% | -0,02% | -0,04%
Class B | -0,04% | -0,03% | -0,06%
Class C | -0,01% | -0,04% | -0,21%
Class E | -0,05% | -0,14% | -0,07%
Overall | -0,03% | -0,06% | -0,09%
Class D | -0,03% | 0,02% | -0,08%
Class F | 0,01% | -0,11% | 0,00%