## Slide 1: JVET-M0428: Encoder optimization with deblocking filter
Nan Hu, Vadim Seregin, Wei-Jung Chien, Marta Karczewicz

## Slide 2
Distortion calculation during tree traversal in VTM3
……
DeQuant
InvT
Add Pred
SSE
……
DeQuant
InvT
Add Pred
Deblocking
Proposed method
SSE

## Slide 3: Results
Thanks Alibaba for cross-checking
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.78% | -0.71% | -0.50% | 101% | 103%
Class A2 | -0.56% | -1.30% | -1.23% | 102% | 101%
Class B | -0.65% | -1.14% | -1.20% | 102% | 103%
Class C | -0.41% | -1.05% | -1.04% | 101% | 100%
Class E | -0.55% | -0.89% | -0.88% | 101% | 94%
Overall | -0.58% | -1.03% | -1.00% | 101% | 100%
Class D | -0.32% | -1.21% | -1.01% | 101% | 98%
Class F (optional) | -0.30% | -0.69% | -0.49% | 101% | 98%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.78% | -1.66% | -1.22% | 101% | 99%
Class A2 | -0.95% | -1.21% | -1.04% | 101% | 100%
Class B | -0.73% | -1.46% | -1.61% | 103% | 103%
Class C | -0.46% | -1.23% | -1.26% | 102% | 101%
Class E |  |  |  |  | 
Overall | -0.71% | -1.39% | -1.33% | 102% | 101%
Class D | -0.33% | -1.77% | -1.60% | 102% | 102%
Class F (optional) | -0.39% | -0.83% | -0.86% | 102% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.73% | -0.32% | -0.44% | 102% | 103%
Class C | -0.41% | 0.10% | -0.04% | 101% | 101%
Class E | -0.90% | 0.37% | -0.64% | 101% | 103%
Overall | -0.66% | -0.01% | -0.35% | 101% | 102%
Class D | -0.41% | -0.38% | 0.16% | 102% | 98%
Class F (optional) | -0.51% | -0.42% | -0.49% | 101% | 99%