## Slide 1: CE3-related: Simplified look-up table for CCLM mode (JVET-M0493)
L. Zhao, X. Zhao, X. Li , S. Liu ( Tencent )
2019/01

## Slide 2: Introduction
In CCLM, the model parameters and are derived as follows
To avoid division operation, two look-up tables (LUT) with size 512 are employed
  LUT-1: Floor( 232 / diff ) − Floor( 216 / diff ) * 216
  LUT-2: Floor( 216 / diff )

## Slide 3: Proposed method
Firstly, LUT-1 is removed
Secondly, the range of diff is divided into multiple intervals, and further quantized, and the quantized value specifies LUT entry index
  Method 1 (size 120)
  Method 2 (size 88)
  Method 3 (size 64)

## Slide 4: Simulation Results
Anchor: VTM3.0
Method 1
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.26% | 0.02% | 97% | 96% | 0.02% | -0.27% | 0.00% | 94% | 96%
Class A2 | 0.00% | -0.08% | 0.00% | 97% | 97% | 0.01% | 0.12% | 0.13% | 96% | 98%
Class B | 0.01% | -0.06% | -0.10% | 99% | 99% | -0.01% | 0.09% | -0.10% | 95% | 96%
Class C | -0.02% | -0.10% | -0.16% | 98% | 98% | 0.01% | -0.01% | -0.03% | 95% | 95%
Class E | 0.01% | 0.01% | 0.01% | 97% | 97% |  |  |  |  | 
Overall | 0.00% | -0.09% | -0.06% | 98% | 98% | 0.01% | 0.00% | -0.02% | 95% | 96%
Class D | 0.00% | -0.10% | -0.02% | 98% | 98% | -0.02% | -0.09% | -0.11% | 95% | 95%
Class F | 0.00% | -0.06% | 0.04% | 97% | 97% | -0.02% | 0.10% | 0.05% | 93% | 94%

## Slide 5: Simulation Results
Anchor: VTM3.0
Method 2
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.17% | 0.03% | 98% | 98% | 0.05% | -0.22% | 0.05% | 96% | 98%
Class A2 | 0.00% | -0.07% | -0.04% | 98% | 98% | -0.02% | -0.03% | 0.07% | 96% | 100%
Class B | 0.00% | -0.07% | -0.08% | 100% | 102% | 0.00% | 0.03% | -0.16% | 96% | 101%
Class C | 0.00% | -0.06% | -0.16% | 98% | 100% | 0.00% | -0.02% | 0.16% | 95% | 100%
Class E | 0.01% | 0.09% | 0.06% | 99% | 101% |  |  |  |  | 
Overall | 0.00% | -0.06% | -0.05% | 99% | 100% | 0.00% | -0.04% | 0.01% | 96% | 100%
Class D | 0.00% | -0.04% | 0.11% | 100% | 101% | -0.01% | -0.37% | -0.06% | 95% | 99%
Class F | 0.02% | -0.09% | 0.02% | 98% | 100% | -0.01% | 0.04% | 0.02% | 94% | 99%

## Slide 6: Simulation Results
Anchor: VTM3.0
Method 3
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.20% | -0.01% | 99% | 99% | 0.06% | -0.20% | 0.03% | 96% | 96%
Class A2 | 0.00% | -0.04% | -0.05% | 98% | 98% | -0.01% | 0.08% | 0.08% | 97% | 99%
Class B | 0.00% | -0.07% | -0.15% | 99% | 99% | -0.02% | 0.06% | -0.08% | 96% | 97%
Class C | -0.01% | -0.08% | -0.11% | 100% | 96% | 0.00% | 0.03% | 0.13% | 96% | 95%
Class E | 0.02% | -0.04% | 0.10% | 100% | 99% |  |  |  |  | 
Overall | 0.01% | -0.08% | -0.06% | 99% | 98% | 0.00% | 0.00% | 0.03% | 96% | 97%
Class D | -0.01% | -0.09% | 0.05% | 99% | 98% | 0.01% | -0.44% | -0.19% | 96% | 96%
Class F | 0.01% | 0.07% | -0.01% | 98% | 98% | 0.01% | 0.07% | 0.08% | 95% | 94%

## Slide 7: Conclusion
One LUT is removed and the size of the remaining LUT is reduced by 87.5% (from 512 to 64 integers)
Minor BD-rate impact
It is proposed to further study this proposal in CE