## Slide 1: CE10-related: Unidirectional illumination compensation
V. Seregin, W.-J. Chien, T. Hsieh, N. Hu, M. Karczewicz

## Slide 2: Local illumination compensation
LIC parameters derivation as in BMS/CE10
  Neighbor samples for the current and reference blocks are used to derive linear mode a*p+b
To remove the extra stage in the inter processing and lower complexity, LIC is not applied to:
  Bi-directional prediction
  Sub-block based inter prediction (affine, ATMVP)
  Multi hypothesis intra and inter
To simplify merge list derivation process with LIC:
  LIC flag is not used in merge candidate pruning
  LIC flag is set to false for TMVP, average pair-wise and zero MV candidates

## Slide 3: Test results
Two tests are performed:
  Test 1: Proposed uni-directional LIC
  Test 2: Proposed LIC is not applied to 4x4 and 128xN blocks
Random Access Main 10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.75% | -0.42% | -0.51% | 118% | 98%
-0.37% | -0.22% | -0.25% | 111% | 99%
-0.50% | -0.27% | -0.45% | 113% | 98%
-0.38% | -0.46% | -0.35% | 118% | 98%
-0.49% | -0.34% | -0.39 | 115% | 98%
-0.22% | -0.36% | -0.24% | 118% | 98%
-0.87% | -0.61% | -0.55% | 112% | 98%
Low delay B Main10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.53% | -0.58% | -0.43% | 116% | 100%
-0.48% | -0.37% | -0.15% | 124% | 101%
0.02% | 0.10% | -0.37% | 100% | 101%
-0.38% | -0.34% | -0.32% | 114% | 101%
-0.19% | -0.03% | -0.26% | 120% | 102%
-2.46% | -1.93% | -1.53% | 116% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.82% | -0.41% | -0.59% | 120% | 98%
Class A2 | -0.37% | -0.24% | -0.30% | 111% | 99%
Class B | -0.51% | -0.32% | -0.46% | 114% | 96%
Class C | -0.39% | -0.47% | -0.30% | 120% | 96%
Class E |  |  |  |  | 
Overall | -0.51% | -0.36% | -0.41% | 116% | 97%
Class D | -0.24% | -0.24% | -0.35% | 119% | 95%
Class F | -0.90% | -0.64% | -0.57% | 112% | 95%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.58% | -0.43% | -0.43% | 115% | 97%
Class C | -0.46% | -0.40% | -0.52% | 123% | 97%
Class E | 0.08% | 0.07% | -0.03% | 99% | 98%
Overall | -0.38% | -0.29% | -0.36% | 113% | 97%
Class D | -0.18% | 0.01% | -1.01% | 120% | 97%
Class F | -2.53% | -1.79% | -2.13% | 116% | 95%
Test 1
Test 2

## Slide 4: Encoder optimization for Test 2
LIC mode is checked at encoder only if the current best mode is not merge.
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.47% | -0.30% | -0.31% | 102% | 99%
Class A2 | -0.22% | -0.13% | -0.14% | 102% | 101%
Class B | -0.32% | -0.11% | -0.22% | 102% | 98%
Class C | -0.19% | -0.17% | -0.12% | 105% | 100%
Class E |  |  |  |  | 
Overall | -0.30% | -0.17% | -0.20% | 103% | 99%
Class D | -0.08% | -0.12% | -0.15% | 105% | 100%
Class F | -0.54% | -0.41% | -0.38% | 103% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.25% | -0.44% | -0.27% | 101% | 100%
Class C | -0.15% | -0.03% | -0.18% | 104% | 101%
Class E | 0.08% | 0.16% | -0.36% | 99% | 103%
Overall | -0.14% | -0.16% | -0.26% | 102% | 101%
Class D | -0.02% | 0.00% | -0.09% | 104% | 101%
Class F | -1.53% | -0.97% | -0.92% | 103% | 99%