## Slide 1
JVET-M0510
AHG9: CNN-based in-loop filter proposed by USTC
Yuanying Dai, Dong Liu, Yue Li, Feng Wu
University of Science and Technology of China, Hefei, China

## Slide 2
Summary

## Slide 3
Summary
Lightweight deep convolutional neural networks
Locate between DF and SAO
-0.96%, -0.32%, -0.45% BD-rate savings for Y, Cb, and Cr components compared with VTM3.0 under AI configuration

## Slide 4
Proposed Method

## Slide 5
Network structure: test1
1. Residue learning
2. Shared Parameters

## Slide 6
Network structure: test2
1. Residue learning
2. Shared Parameters
3. Depthwise conv

## Slide 7
Training

## Slide 8
EXPERIMENTS

## Slide 9
Experiments
1. BD-rate of Test1
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.01% | -0.03% | 157% | 734%
Class A2 | -0.65% | -0.10% | -0.13% | 128% | 2396%
Class B | -0.63% | -0.02% | -0.02% | 129% | 2169%
Class C | -1.72% | -1.33% | -1.89% | 104% | 4050%
Class E | -1.68% | 0.01% | 0.01% | 119% | 2476%
Overall | -0.96% | -0.32% | -0.45% | 125% | 2162%
Class D | -2.18% | -1.39% | -1.64% | 121% | 3816%
Class F | -1.10% | -0.60% | -0.73% | 112% | 780%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.11% | 0.02% | -0.02% | 134% | 237%
Class A2 | -0.68% | -0.11% | 0.01% | 128% | 308%
Class B | -0.57% | 0.02% | -0.07% | 126% | 466%
Class C | -0.98% | -0.90% | -0.87% | 114% | 1051%
Class E |  |  |  |  | 
Overall | -0.61% | -0.25% | -0.26% | 125% | 465%
Class D | -1.13% | -1.04% | -1.14% | 117% | 960%
Class F | -0.47% | -0.22% | -0.22% | 135% | 231%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.81% | -0.91% | -0.77% | 113% | 331%
Class C | -0.61% | -0.69% | -1.04% | 117% | 1391%
Class E | -0.87% | 0.19% | -0.07% | 124% | 153%
Overall | -0.76% | -0.56% | -0.69% | 117% | 440%
Class D | -1.10% | -1.41% | -1.58% | 106% | 1502%
Class F | -0.17% | -0.22% | -0.05% | 140% | 205%

## Slide 10
Experiments
1. BD-rate of Test2
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | 0.00% | -0.01% | 153% | 596%
Class A2 | -0.49% | 0.00% | -0.01% | 138% | 1509%
Class B | -0.52% | -0.01% | -0.02% | 128% | 1370%
Class C | -1.51% | -0.76% | -1.03% | 98% | 1724%
Class E | -1.36% | 0.02% | 0.02% | 121% | 1677%
Overall | -0.79% | -0.17% | -0.23% | 124% | 1319%
Class D | -1.95% | -1.12% | -1.25% | 119% | 1676%
Class F | -1.06% | -0.20% | -0.24% | 112% | 477%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.76% | -0.90% | -0.62% | 92% | 253%
Class C | -0.45% | -0.38% | -0.50% | 101% | 933%
Class E | -0.67% | 0.02% | 0.46% | 115% | 126%
Overall | -0.64% | -0.50% | -0.31% | 100% | 329%
Class D | -0.87% | -0.48% | -1.05% | 101% | 994%
Class F | -0.15% | -0.45% | -0.56% | 121% | 183%

## Slide 11
Experiments Summary

## Slide 12
CONCLUSION

## Slide 13
Conclusion
1. Good balance between coding performance and complexity
2. Thank Hikvision for cross-check

## Slide 14
THANK YOU!