## Slide 1: JVET-M0517 Non-CE9: Methods for BDOF complexity reduction
S. Sethuraman
Ittiam Systems
9 January 2019

## Slide 2: Overview
2 simplifications proposed for BDOF
  Decimated set of positions used while computing the optical flow vector for a 4x4 block of samples
    Multiple patterns were studied
    Minimal impact on coding efficiency
  Reducing the bit-depth of the per-position multiplications from 11-bit x 11-bit to 8-bit x 8-bit
    2 alternative methods were studied
    One of them had a negligible impact on impact efficiency

## Slide 3: Positions currently used for flow vector estimation
Every 4x4 block of samples use a set of (6x6) = 36 positions centered on the 4x4 block
  Sample differences DI = (I1 – I0) from 6x6 positions
  Sum of horizontal gradients of L0 (Gx0) and L1 (Gx1) and Sum of vertical gradients of L0 (Gy0) and L1 (Gy1) – computed for 6x6 positions using 8x8 samples in each reference
Product terms
  sGx*sGx
  sGy*sGy
  sGx* DI
  sGy* DI
  sGx*sGy
Accumulated over 36 positions for each 4x4 to solve for flow vector (vx, vy)
  Least squares solution of 36 equations in (vx, vy)
Significant part of BDOF’s complexity comes from these multiplications and accumulations

## Slide 4: Decimating the positions
The 6x6 positions are decimated by a factor of 2 in the following manner:
  Alternate rows
  Alternate columns
  Quincunx (alternating in both horizontal and vertical directions)
Though the positions are decimated, it should be noted that the predicted sample values at all 36 positions are still accessed for computing the gradients
Per-position multiplications reduce by a factor of 2
Accumulations reduce by a factor of 2
18 equations are solved to compute the optical flow vector
No change to the process of applying the correction

## Slide 5: Results for decimated positions
Results are presented against VTM3.0 that includes BDOF
Downsampling vertically by a factor of 2 has 0.05% BD-RATE drop
Quincunx downsampling by a factor of 2 has negligible impact on coding efficiency
Alternate rows
Quincunx

## Slide 6: Bit-depths used in current BDOF
As proposed in JVET-L0256, the bit-depths during the flow vector estimation were restricted as follows:
  Predicted samples were right shifted by 6 bits
  Predicted sample difference is in 11-bits
  Gradient computed from 16-bit predicted samples were right shifted by 4 bits
  The gradient sums were further right shifted by 3 bits to be in 11-bits
  The product terms require 11-bit x 11-bit multiplications
  Accumulators require 22+6 = 28 bits
11-bit x 11-bit multiplication adds substantial hardware complexity
  Equivalent to 11 shifted additions with progressively increasing bit depth
11-bit x 11-bit multiplications are not efficient for SIMD
In this proposal, 2 methods for simplifying these multiplications to 8-bit x 8-bit multiplications are studied

## Slide 7: Method-1
The predicted sample difference at 11-bit depth is further right shifted by 3 bits to make it 8-bits
The sum of gradients at 11-bit depth is further right shifted by 3 bits to make it 8-bits
Perform all multiplications as 8-bit x 8-bit multiplications before accumulating the terms

## Slide 8: Method - 2
Predicted samples are right shifted by 6 bits
Predicted sample difference between the corresponding positions of L0 and L1 is computed and is sign-saturated to 8-bit (i.e. clipped between -128 and +127)
The gradients are computed from the predicted sample already right shifted by 6 bits to result in 11-bit gradients
  Eliminates the sub-optimal step in current process of going to 17-bits and then down-shifting it by 4 which is not SIMD friendly; in this, the gradient and the sum of gradients stay within 16-bits and hence is more SIMD friendly
The sum of gradients are computed, right shifted by 1 bit, and then sign saturated to 8-bit
The product terms are computed using 8-bit x 8-bit multiplications
The accumulators need to be only 16 + 6 = 22 bits wide
Each 4x4 block of samples require 5 accumulators
Multiple 4x4 blocks will need to be processed in parallel

## Slide 9: Results for bit-depth restriction
Results are shown against VTM3.0
Method-1 has a significant BD-RATE drop of 0.25%
Method-2 has negligible impact on BD-RATE (0.01% gain)

## Slide 10: Conclusions
2 simplifications to BDOF are proposed
First simplification relates to halving the multiplications and additions required for 4x4 flow vector estimation by using only 50% of the 6x6 positions used earlier
  Using alternate row of positions has a 0.05% BD-RATE drop, but is the simplest from an implementation point of view
  Using Quincunx sampling has a 0.01% BD-RATE drop
Second simplification relates to reducing the multiplications during flow vector estimation from 11-bit x 11-bit to 8-bit x 8-bit
  Two methods were studied
    First method did a straight-forward right shifting by 3-bits of the 11-bit quantities. This shows a BD-RATE drop of 0.25%
    Second method loses 6 bits of LSBs in the predicted sample first and then uses signed saturation to clip the values to 8-bit. This shows negligible impact on coding efficiency (0.01% gain)
Together these two simplifications reduce the hardware requirements for BDOF significantly and hence it is requested that these be adopted as part of BDOF

## Slide 11: THANKS TO QUALCOMM FOR CROSS-CHECKING THE RESULTS!