## Slide 1
JVET-M0541: Combination of MMVD and CPR mode
Yiming Li, Zhenzhong Chen (Wuhan University)
Xiaozhong Xu, Shan Liu (Tencent)

## Slide 2
Current implementation
In a MMVD candidate list, it only consists default merge type (MRG_TYPE_DEFAULT_N) . It excludes the CPR merge type when generating the MMVD candidate list.
MMVD cannot combined with CPR merge mode

## Slide 3: Proposed Method
Propose to unify the CPR mode operation with MMVD
merge candidates with default merge type (MRG_TYPE_DEFAULT_N) and CPR merge type (MRG_TYPE_CPR) may both exist in the MMVD candidate list.
Thus we can have a uniform decoder implementation for CPR merge and non-CPR merge mode.
Based on the uniform implementation, 3methods are provided (the difference are encoder only)

## Slide 4
Proposed method
Method#1
in encoder side, CPR merge mode with MVD is not searched for time saving.

## Slide 5
Simulation Results
Proposed Method1 vs. VTM3.0 off/onCPR

## Slide 6
Proposed method
Method#2
In encoder side, CPR merge mode with MVD is compared with common CPR merge type by RD search. Since MMVD may generate non-integer MVD, the derived block vector will be clipped into integer. Thus all the possible distance index of MMVD is allowed in the decoder.

## Slide 7
Simulation Results
Proposed Method2 vs. VTM3.0 off/onCPR

## Slide 8
Proposed method
Method#3
In encoder side, CPR merge mode with MVD is compared with common CPR merge type by RD search. Since MMVD may generate non-integer MVD, the corresponding candidates in MMVD is skipped. A bitstream conformance check is required such that non-integer motion vector is not allowed when current picture is the reference picture.

## Slide 9
Simulation Results
Proposed Method3 vs. VTM3.0 off/onCPR

## Slide 10
THANKS!