## Slide 1: JVET-M0581
CE10-related: Bi-directional motion vector storage for triangular prediction
Max Bläser
RWTH Aachen University
blaeser@ient.rwth-aachen.de

## Slide 2: Introduction
In JVET-K0144 [1], triangular inter-prediction method with bi-prediction is presented. Coding gains of approximately 1% for RA and 1.7% for LB are reported
In JVET-L0124 [2], triangular partitioning is restricted to uni-directional prediction. The coding gain drops to approximately 0.6% compared to the VTM 2.0 anchor
Bi-directional merge vectors are split into uni-directional components for prediction an MV storage
Additional bi-directional vector constructed for boundary 4x4 blocks
Figure 1: Motion Vector Storage for Triangular Partitions in VTM 3.0 [JVET-L0124]

## Slide 3: Proposed method
Investigate bi-directional motion vector storage, while keeping uni-directional prediction.
Uniquely assign 4x4 border blocks to first or second triangle for MV storage
Figure 2: Handling of bi-prediction motion vectors for triangular / geometric prediction units.
Merge List Generation
Merge Candidate Selection
Motion Compensation
Uni-Prediction Candidate Derivation
Motion Vector Storage
bi-prediction MV
uni-prediction MV
Figure 3: Examples of motion vector storage based on a hard decision for the 4x4 blocks on the partition boundary.
Boundary blocks are assigned to first or second partition
Criterion used is based on motion vectors MV1 and MV2 (closest POC distance preferred)

## Slide 4: Experimental results (RA)
Experiments conducted using the VTM-3.0 software [3] with the VTM configuration and according to the JVET common test conditions JVET-L1010 [4], bandwidth measurements according to JVET-K0451 [5]
 | Random Access Main 10 |  |  |  |  |  |  | Random Access Main10 | 
 | Over VTM-3.0 |  |  |  |  |  |  | Tool off | 
 | Y | U | V | EncT | DecT | ave mem BW | max mem BW | Impacted Pixels | Adj DecT
Class A1 | 0.07% | 0.08% | 0.10% | 101% | 98% | 101% | 102% | 1.51% | 
Class A2 | 0.03% | 0.11% | -0.02% | 101% | 101% | 100% | 101% | 1.39% | 
Class B | 0.05% | 0.08% | 0.22% | 101% | 98% | 101% | 103% | 1.71% | 
Class C | 0.15% | 0.13% | 0.15% | 102% | 100% | 101% | 103% | 3.64% | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.08% | 0.10% | 0.13% | 101% | 99% | 101% | 103% | 2.12% | 
Class D | 0.06% | 0.10% | 0.03% | 102% | 101% | 101% | 108% | 2.91% | 
Class F | 0.08% | 0.01% | 0.05% | 101% | 99% | 102% | 106% | 2.56% | 

## Slide 5: Experimental results (LB)
 | Low delay B Main10 |  |  |  |  |  |  | Low delay B Main10 | 
 | Over VTM-3.0 |  |  |  |  |  |  | Tool off | 
 | Y | U | V | EncT | DecT | ave mem BW | max mem BW | Impacted Pixels | Adj DecT
Class A1 |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  | 
Class B | 0.12% | 0.28% | 0.33% | 115% | 109% | 100% | 101% | 3.71% | 
Class C | 0.18% | 0.07% | 0.41% | 133% | 95% | 101% | 104% | 6.09% | 
Class E | 0.16% | 0.03% | 0.48% | 132% | 100% | 100% | 100% | 3.90% | 
Overall | 0.16% | 0.20% | 0.19% | 128% | 102% | 100% | 104% | 4.55% | 
Class D | 0.16% | 0.03% | 0.48% | 132% | 100% | 100% | 100% | 7.56% | 
Class F | -0.14% | -0.54% | 0.46% | 94% | 100% | 101% | 103% | 2.88% | 

## Slide 6: Conclusion
Slight coding loss reported of 0.08% for RA and 0.16% for LB, with marginal increase in encoder complexity for RA, and 128% increase in encoder complexity for LB
No significant increase in decoder complexity is reported
Further study is recommended on how the motion vector storage for triangular partitions can be improved

## Slide 7: References
[1] R.-L. Liao, C. S. Lim, "CE10: Triangular prediction unit mode (CE10.3.1 and CE10.3.2)", Joint Video Exploration Team of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JVET-K0144, 11th Meeting, Ljubljana, SI, July 2018
[2] R.-L. Liao, C. S. Lim, "CE10.3.1.b: Triangular prediction unit mode", Joint Video Exploration Team of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JVET-L0124, 12th Meeting, Macao, CN, October 2018
[3] VVC Reference Software, https://vcgit.hhi.fraunhofer.de/jvet/VVCSoftware_VTM
[4] F. Bossen, J. Boyce, K. Suehring, X. Li, V. Seregin, “JVET common test conditions and software reference configurations”, Joint Video Exploration Team of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JVET- L1010, 12th Meeting, Macao, CN, October 2018.
[5] R. Hashimoto, S. Mochizuki, "AHG5: How to use the software to evaluate memory bandwidth", Joint Video Exploration Team of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JVET-K0451 11th Meeting, Ljubljana, SI, July 2018