## Slide 1: Jarosław Samelak, Marek Domański
MPEG M46332 = JVET-M0765, MPEG M46343
Unified Screen Content and Multiview Video Coding - Experimental results
Poznań University of Technology
Chair of Multimedia Telecommunications and Microelectronics Poznań, Poland
Marrakech, January 2018

## Slide 2: Multiview video coding: MV-HEVC: (still no VVC implementation for multiview) - The state-of-the-art multiview video coding technology, - Multi-layer codecs (complicated structure) – layered bitream syntax, - Applications still limited, Similarly as for all standards (MPEG2, AVC i.e. MVC).
Two technologies considered

## Slide 3: Screen Content Coding (SCC): – Single-layer codecs. – Only limited upgrade from Main Profile, – Implemented for both HEVC and VVC. - Chance to be popular in consumer devices.
The second technology considered

## Slide 4: Preliminary remarks
Frame-packing is probably the mostly used technique for stereoscopic video transmission.
Intra Block Copy (VVC: Current Picture Reference) in Screen Content Coding may be used for interview prediction:

## Slide 5: Development
Macao Meeting, October 2017
Doc.: JVET-H0044
For All Intra Mode, for HEVC multiview coding : HEVC Screen Content Coding with quarter-pel accuracy of translation vectors provides virtually the same compression performance as MV-HEVCC.
The results were obtained for rectified muliview video acquired using cameras with parallel optical axes (as MVC and MV-HEVC assume).

## Slide 6: Unified Screen Content and Multiview Coding
Codec built on top of HEVC SCC (potentially on VVC)
Translation vectors
are represented using the same format as
motion vectors with ¼-pel accuracy
Views are encoded as tiles of a frame
SAO and deblocking filter after compression of each tile

## Slide 7: Unified Screen Content and Multiview Coding
Screen Content Coding tools configuration enabled Intra Boundary Filter,
disabled Hash-Based Motion Estimation,
disabled Palette Mode,
disabled Colour Transform. Configuration used in experiments, no need to remove these tools.
QP in tiles set independently (for experiments: like in CTC for Multiview Coding).

## Slide 8: Unified Screen Content and Multiview Coding
Reference tile border extension

## Slide 9: Experimental comparison USCCMC versus MV-HEVC
USCCMC: HM-16.9+SCM-8.0 + authors’ improvements
MV-HEVC: HTM-16.2 Conditions like in CTC MV-HEVC Results for Random Access
Sequence | Bitrate increase [%] |  | Encoding time increase [%] | 
 | HEVC-SCC | USCMC | HEVC-SCC | USCMC
Poznan Hall 2 | 25.43 | -0.63 | +80 | +0
Poznan Street | 30.82 | 0.51 | +99 | +2
Kendo | 18.39 | 0.37 | +56 | +1
Balloons | 16.19 | 0.33 | +92 | -1
Newspaper | 17.74 | 0.46 | +94 | +0
Average | 21.72 | 0.21 | +84 | +0

## Slide 10: Experimental comparison USCCMC versus MV-HEVC
USCCMC: HM-16.9+SCM-8.0 + authors’ improvements
MV-HEVC: HTM-16.2 Conditions like in CTC MV-HEVC Results for All Intra
Sequence | Bitrate increase [%] |  | Encoding time increase [%] | 
 | HEVC-SCC | USCMC | HEVC-SCC | USCMC
Poznan Hall 2 | 27.36 | -1.67 | +32 | -5
Poznan Street | 29.05 | -0.55 | +67 | -12
Kendo | 22.34 | 0.06 | +11 | -4
Balloons | 18.27 | 0.00 | +24 | -1
Newspaper | 18.56 | -0.35 | +37 | -3
Average | 23.12 | -0.50 | +34 | -5

## Slide 11: Experimental comparison USCCMC versus HEVC SCC
USCCMC: HM-16.9+SCM-8.0 + authors’ improvements
HEVC SCC: HM-16.9+SCM-8.0 Conditions like in CTC HEVC SCC Results for Random Access, quarter-pel
Sequence | Bitrate increase [%] | Encoding time increase [%]
Basketball_Screen | 2.60 | +10
ChinaSpeed | 0.32 | +23
ChineseEditing | 3.50 | +12
MissionControlClip2 | 0.42 | +10
MissionControlClip3 | 2.38 | +10
sc_console | 8.34 | +15
sc_desktop | 8.82 | +13
sc_flyingGraphics | 5.38 | +31
sc_map | 1.42 | +10
sc_programming | 1.89 | +13
sc_robot | 0.10 | +20
sc_web_browsing | 11.27 | +18
SlideShow | -0.77 | +33
Basketball_Screen | 2.60 | +10
ChinaSpeed | 0.32 | +23
ChineseEditing | 3.50 | +12
MissionControlClip2 | 0.42 | +10

## Slide 12: Consequences for VVC development
Unified Screen Content and Multiview Coding for HEVC can be efficiently used for both Screen Coding and Multiview. USCMC replaces MV-HEVC.
Proposal for JVET: While developing SCC for VVC, check if the modifications ensure also high efficiency of frame-compatible multiview coding. Multiview VVC might not be needed.

## Slide 13: Thank you