## Slide 1: CE3-3.2: Simplified and robust CCLM parameter derivation (JVET-O0095)
A. Filippov, V. Rufitskiy, E. Alshina (Huawei)

## Slide 2: CCLM in VTM-5.0
# | Template processing | Inner block (CB) processing
1 | Downsampling using 6-tap filter | Downsampling using 6-tap filter
2 | Parameter deriving using min / max method | NOP
3 | NOP | Getting a predictor by applying the derived CCLM parameters to an inner block
Proposed CCLM processing of small blocks
# | Template processing | Inner block (CB) processing
1 | Parameter deriving using min / max method | Downsampling using 6-tap filter
2 | NOP | Getting a CCLM-based predictor by applying the derived parameters to an inner block

## Slide 3: Quantitative analysis
Template filter operations
  4 positions x (6 add ops)
Inner samples filter operations
  16 positions (in the case of a 4x4 chroma block) x (6 add ops)
Min/max operations
  4 comparison ops
  3 LUT fetches
  Several (<4..5) add ops
  2 mult ops
int diffC = maxLuma[1] - minLuma[1];
int x = floorLog2( diff );
int normDiff = (diff << 4 >> x) & 15;
int v = DivSigTable[normDiff] | 8;
x += normDiff != 0;
int y = floorLog2( abs( diffC ) ) + 1;
int add = 1 << y >> 1;
a = (diffC * v + add) >> y;
iShift = 3 + x - y;
if ( iShift < 1 ) {
iShift = 1;
a = ( (a == 0)? 0: (a < 0)? -15 : 15 ); // a=Sign(a)*15
}
b = minLuma[1] - ((a * minLuma[0]) >> iShift);