## Slide 1
JVET-O0126
CE8-related: IBC modifications
LI JINGYA, LIM CHONG SOON

## Slide 2
Problem
In VTM5.0, conformance check is performed that requires IBC block vector to be within a valid reference area
X
Curr
X
X
Curr
X
X
X
X
Curr
X
X
Curr
X
X
X
Curr
X
X
X
Curr
current CTU processing order and its available reference samples in current and left CTU when first level vertical binary-tree split is applied.
current CTU processing order and its available reference samples in current and left CTU (when quad-tree split is enforced at 128x128 level)
It is desirable to add block vector check to decoder to avoid undefined decoder behavior

## Slide 3
Problem
JVET-N0201/N0316 moves same conformance checks to decoder side:
An IBC block vector is determined as invalid if any of the following conditions are met. (same as VTM5.0)
If any reference sample exceed picture boundary
If any reference sample’s horizontal and vertical position is greater than or equal to top left sample position of current block area
If any reference sample is in above CTU row
If any reference sample is in below CTU row
If any reference sample exceeds current CTU boundary or left N’s (N =1 for 128x128 sized CTU) CTU boundary
If any reference sample exceeds 3 VPDU reference area
If any reference sample is not available when reference area is in current VPDU
It is desirable to reduce complexity of condition checks

## Slide 4
Proposal
In the proposed method, an IBC block vector is determined as invalid if any of the following conditions are met:
If the refPosTL_y + IBC block height > IBCBufferHeight.
If any reference sample is not decoded in prediction block in IBC buffer.

## Slide 5
Proposal
Explanation of IBC buffer:
A dedicated 128x128 sized buffer is used for decoding current VPDU and storing 3 (when CTU size = 128x128) previously decoded VPDU.
Location of the prediction sample (refPos_x, refPos_y) in IBC buffer for predicted sample located in (currPos_x, currPos_y) with block vector (bv_x, bv_y) is derived as below:
refPos_x = (currPos_x + bv_x) & (IBCBufferWidth - 1)
refPos_y = (currPos_y + bv_y) & (IBCBufferHeight -1)

## Slide 6
Proposal
Buffer updating: The reconstructed samples before in-loop filtering are stored in the buffer as prediction samples for IBC referencing

## Slide 7
Proposal
Summary of buffer updating and validation check process
Initialize isDecoded buffer (256 bytes) at beginning of each CTU row
Assign buffer to current VPDU
When Decoding VPDU
  When start decoding, set isDecoded buffer to zero
  If current block is not IBC mode, go to d, otherwise go to c
  Check if a block vector is valid, if yes, use prediction samples from IBC buffer, otherwise, set all prediction values to a default value; go to d
  Perform reconstruction and stored samples before in-loop filtering in IBC reference buffer
‘isDecoded’ is used that stores the decoding status of all sub-blocks in IBC buffer

## Slide 8
Proposal
VTM5.0/JVET-N0201/JVET-N0316 | Proposed method
17 comparison 24 addition 3 multiplication | 5 comparison 11 addition 6 bitwise AND

## Slide 9
Simulation results
Proposed method (encoder block vector search no change)
Proposed method (encoder block vector search uses proposed validation check)
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 (enable IBC) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.01% | -0.01% | 100% | 102%
Class A2 | 0.01% | -0.04% | 0.02% | 107% | 103%
Class B | 0.00% | 0.03% | -0.01% | 104% | 110%
Class C | -0.01% | -0.01% | 0.02% | 101% | 104%
Class E | -0.01% | -0.01% | 0.06% | 104% | 100%
Overall | -0.01% | 0.00% | 0.01% | 103% | 104%
Class D | -0.02% | -0.07% | 0.03% | 96% | 100%
Class F | -0.03% | 0.07% | 0.03% | 101% | 100%
TGM | -0.18% | -0.11% | -0.12% | 101% | 98%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 (enable IBC) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.05% | 0.07% | 98% | 100%
Class A2 | 0.00% | 0.26% | 0.02% | 100% | 101%
Class B | -0.03% | 0.10% | 0.00% | 102% | 102%
Class C | 0.02% | -0.01% | -0.08% | 105% | 103%
Class E |  |  |  |  | 
Overall | 0.00% | 0.09% | 0.00% | 101% | 102%
Class D | 0.02% | -0.16% | -0.17% | 102% | 105%
Class F | -0.02% | -0.09% | 0.16% | 98% | 102%
TGM | -0.18% | -0.13% | -0.10% | 98% | 96%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 (enable IBC) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.02% | -0.11% | 0.11% | 101% | 100%
Class C | 0.01% | 0.29% | 0.17% | 104% | 100%
Class E | 0.08% | 1.22% | 0.26% | 98% | 103%
Overall | 0.01% | 0.36% | 0.17% | 101% | 101%
Class D | 0.05% | -0.02% | 0.12% | 103% | 100%
Class F | 0.01% | -0.18% | 0.46% | 94% | 91%
TGM | -0.02% | -0.12% | -0.09% | 98% | 101%
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 (enable IBC) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 95% | 100%
Class A2 | 0.00% | 0.00% | 0.00% | 102% | 98%
Class B | 0.00% | 0.00% | 0.00% | 103% | 99%
Class C | 0.00% | 0.00% | 0.00% | 100% | 94%
Class E | 0.00% | 0.00% | 0.00% | 105% | 101%
Overall | 0.00% | 0.00% | 0.00% | 101% | 98%
Class D | 0.00% | 0.00% | 0.00% | 97% | 108%
Class F | 0.00% | 0.00% | 0.00% | 98% | 100%
TGM | 0.00% | 0.00% | 0.00% | 99% | 102%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 (enable IBC) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 98% | 102%
Class A2 | 0.00% | 0.00% | 0.00% | 99% | 101%
Class B | 0.00% | 0.00% | 0.00% | 102% | 103%
Class C | 0.00% | 0.00% | 0.00% | 102% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 101% | 102%
Class D | 0.00% | 0.00% | 0.00% | 105% | 100%
Class F | 0.00% | 0.00% | 0.00% | 98% | 98%
TGM | 0.00% | 0.00% | 0.00% | 97% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 (enable IBC) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 100% | 102%
Class C | 0.00% | 0.00% | 0.00% | 99% | 101%
Class E | 0.00% | 0.00% | 0.00% | 104% | 105%
Overall | 0.00% | 0.00% | 0.00% | 101% | 102%
Class D | 0.00% | 0.00% | 0.00% | 99% | 102%
Class F | 0.00% | 0.00% | 0.00% | 102% | 103%
TGM | 0.00% | 0.00% | 0.00% | 104% | 103%

## Slide 10
10
Conclusion
This contribution further reduces complexity of JVET-N0201/N0316 by introducing dedicated IBC reference buffer. Complexity is greatly reduced. Coding impact is negligible

## Slide 11
11
Thank Bytedance for cross-check