## Slide 1
Non-CE2: CCLM with Chroma Separate Tree
Che-Wei Kuo, Jingya Li, Chong Soon Lim

## Slide 2: Introduction
CE2-3.1: Enable CCLM only in 32x32 luma grid and 16x16 chroma grid to limit the latency within 32x32 luma samples.
Different scan order may lead to even worse latency.
  luma VPDU: QT, chroma VPDU: QT
  luma VPDU: QT, chroma VPDU: BT_V then BT_H on both blocks
In case 2, the chroma prediction latency of the bottom left block is 2x32x32 luma samples.
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU

## Slide 3: Proposed Method
Propose to use VPDU level partitioning information for CCLM enabling condition checks.
Propose 3 methods for trade-off between gain and complexity.
  Method 1: 0.26/2.94/2.97 Y/U/V in AI
  Method 2: 0.08/1.29/1.25 Y/U/V in AI
  Method 3: 0.07/1.04/1.02 Y/U/V in AI
All methods are applied to all CTU size settings and reduce the prediction latency to ¼ luma VPDU reconstruction process.
 |  |  |  | AI |  |  | 
Abbreviation | BDR-Y | BDR-U | BDR-V | Tester EncTime | Tester DecTime | XChecker EncTime | XChecker DecTime
CST | 0.41% | 12.73% | 13.50% | 170% | 103% | 172% | 103%
CCLM | 1.85% | 17.20% | 17.54% | 99% | 100% | 98% | 98%

## Slide 4: Method 1: Luma & Chroma Both NoSplit or QT
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU
Luma VPDU | Chroma VPDU
No split | No split
QT | QT

## Slide 5: Method 2: Allow Chroma Subpart Processing
Luma VPDU | Chroma VPDU
No split | No split
QT | No split QT BT_H (no further split or followed by BT_V)
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU

## Slide 6: Method 2: Allow Chroma Subpart Processing
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU

## Slide 7: Method 3: Allow Luma Subpart Processing
Luma VPDU | Chroma VPDU
No split | No split QT BT_H (the BT that contains the chroma block is followed by no split or BT_V) BT_V (the BT that contains the chroma block is followed by no split or BT_H)
QT | No split QT BT_H (the BT that contains the chroma block is followed by no split or BT_V)
BT_H (the BT(s) that contains the chroma block’s collocated luma block(s) is followed by no split or BT_V) | No split QT BT_H (the BT that contains the chroma block is followed by no split or BT_V)
BT_V (the BT(s) that contains the chroma block’s collocated luma block(s) is followed by no split or BT_H) | No split BT_V (the BT that contains the chroma block is followed by no split or BT_H)

## Slide 8: Method 3: Allow Luma Subpart Processing
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU

## Slide 9: Method 3: Allow Luma Subpart Processing
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU
Luma VPDU
Chroma VPDU

## Slide 10: Complexity: Number of Comparisons
Negligible for VPDU level check instead of CU level.
Worst-case comparisons: By counting checks in 1 VPDU
  split_cu_flag
  split_qt_flag
  mtt_split_cu_vertical_flag
  mtt_split_cu_binary_flag
Method 3 comparisons can be the same as Method 2.
  64x64 BT can be restricted without harming performance.
 | Luma VPDU | Chroma VPDU
Method 1 | 2 (QT) | 2 (QT)
Method 2 | 2 (QT) | 4+4*2=12 (BT_H then BT_V on both blocks)
Method 3 | 4+4*2=12 (BT_H then BT_V on both blocks) | 4+4*2=12 (BT_H then BT_V on both blocks)

## Slide 11: Complexity: Implementation
Method 2
  Need subpart processing for chroma CCLM prediction module.
Method 3
  Luma transform must be separated from reconstruction stage.
  Need subpart processing for luma prediction modules.
    Angular/DC/Planar/PDPC/MIP/ISP/IBC
  Need subpart processing for luma reconstruction.

## Slide 12: Simulation Results: Method 1, 2, 3
 |  | All Intra Main10 |  | 
 |  | Over VTM-5.0 |  | 
Y | U | V | EncT | DecT
0.19% | 2.65% | 2.51% | 100% | 102%
0.14% | 1.74% | 0.90% | 98% | 102%
0.06% | 1.30% | 1.63% | 101% | 102%
0.04% | 0.26% | 0.36% | 104% | 102%
0.02% | 0.82% | 0.89% | 102% | 102%
0.08% | 1.29% | 1.25% | 101% | 102%
0.01% | 0.37% | 0.15% | 102% | 101%
0.05% | 0.60% | 0.60% | 108% | 102%
 |  | Random access Main10 |  | 
 |  | Over VTM-5.0 |  | 
Y | U | V | EncT | DecT
0.04% | 0.55% | 0.74% | 104% | 104%
0.05% | 0.88% | 0.31% | 106% | 104%
0.03% | 0.79% | 0.68% | 104% | 104%
-0.04% | 0.05% | -0.07% | 104% | 103%
0.02% | 0.56% | 0.42% | 105% | 104%
0.04% | 0.21% | 0.08% | 104% | 103%
0.03% | 0.22% | 0.33% | 104% | 103%
 |  | Low delay B Main10 |  | 
 |  | Over VTM-5.0 |  | 
Y | U | V | EncT | DecT
0.01% | 0.50% | 0.46% | 114% | 103%
0.04% | 0.40% | -0.10% | 103% | 103%
0.14% | -0.15% | 1.75% | 104% | 104%
0.05% | 0.30% | 0.60% | 108% | 103%
0.05% | -0.20% | 0.27% | 105% | 102%
-0.08% | 0.22% | -0.28% | 101% | 103%
 |  | All Intra Main10 |  | 
 |  | Over VTM-5.0 |  | 
Y | U | V | EncT | DecT
0.15% | 2.09% | 1.94% | 98% | 102%
0.08% | 1.36% | 0.55% | 101% | 103%
0.06% | 1.06% | 1.42% | 102% | 103%
0.04% | 0.25% | 0.31% | 106% | 103%
0.02% | 0.68% | 0.83% | 105% | 103%
0.07% | 1.04% | 1.02% | 102% | 103%
0.01% | 0.35% | 0.14% | 103% | 102%
0.05% | 0.59% | 0.61% | 103% | 103%
 |  | Random access Main10 |  | 
 |  | Over VTM-5.0 |  | 
Y | U | V | EncT | DecT
0.04% | 0.39% | 0.49% | 105% | 105%
0.05% | 0.85% | 0.20% | 104% | 104%
0.03% | 0.52% | 0.49% | 104% | 104%
-0.04% | -0.04% | -0.05% | 106% | 104%
0.02% | 0.41% | 0.29% | 105% | 104%
0.03% | 0.20% | 0.05% | 106% | 103%
0.03% | 0.23% | 0.29% | 104% | 104%
 |  | Low delay B Main10 |  | 
 |  | Over VTM-5.0 |  | 
Y | U | V | EncT | DecT
0.01% | 0.54% | 0.33% | 108% | 103%
0.04% | 0.38% | -0.11% | 105% | 104%
-0.02% | -0.56% | 2.88% | 100% | 104%
0.01% | 0.21% | 0.82% | 105% | 103%
0.05% | -0.20% | 0.27% | 103% | 102%
-0.06% | 0.05% | -0.60% | 101% | 103%
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.78% | 7.94% | 6.81% | 95% | 103%
Class A2 | 0.27% | 3.12% | 1.38% | 101% | 102%
Class B | 0.18% | 2.74% | 4.23% | 102% | 102%
Class C | 0.08% | 0.58% | 0.69% | 104% | 102%
Class E | 0.10% | 1.27% | 1.65% | 101% | 102%
Overall | 0.26% | 2.94% | 2.97% | 101% | 102%
Class D | 0.04% | 0.44% | 0.19% | 106% | 101%
Class F | 0.22% | 1.37% | 1.31% | 105% | 102%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.13% | 1.99% | 1.63% | 104% | 104%
Class A2 | 0.08% | 1.41% | 0.72% | 104% | 104%
Class B | 0.04% | 1.37% | 1.96% | 104% | 104%
Class C | -0.02% | 0.32% | 0.24% | 105% | 103%
Class E |  |  |  |  | 
Overall | 0.05% | 1.22% | 1.19% | 104% | 104%
Class D | 0.03% | 0.38% | 0.15% | 104% | 103%
Class F | 0.07% | 0.76% | 0.85% | 104% | 103%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | 0.41% | 0.42% | 112% | 103%
Class C | 0.00% | 0.00% | -0.16% | 104% | 103%
Class E | 0.00% | -0.16% | 1.50% | 104% | 103%
Overall | 0.01% | 0.13% | 0.50% | 107% | 103%
Class D | 0.00% | -0.04% | 1.33% | 103% | 102%
Class F | 0.02% | 0.32% | -0.23% | 103% | 103%

## Slide 13: Conclusion
Reduce CCLM with CST latency to ¼ luma VPDU reconstruction process for all CTU size settings.
Propose 3 methods for trade-off between gain and complexity.
  Method 3: 0.07/1.04/1.02 Y/U/V in AI
Negligible complexity for VPDU level check instead of CU level.

## Slide 14: Acknowledgment
Thanks InterDigital for cross-checking