## Slide 1: AHG15: Signalling of chroma Qp mapping table
Sergey Ikonin
Roman Chernyak
Elena Alshina

## Slide 2
Introduction
qPi | < 30 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | > 43
QpC | = qPi | 29 | 30 | 31 | 32 | 33 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | = qPi − 6
In the current VVC v5 chroma QP (QpC) is derived based on QP index (qPi) using luma-to-chroma mapping table:
The table was inherited from HEVC and was mostly designed for SDR content. In Geneva meeting several proposals were addressed to modify this table and to adapt it to HDR content. During meeting discussion in Geneva it was suggested to consider if it might be possible to signal such a table at some higher level.
This contribution proposes signaling mechanism for chroma Qp mapping table. It is also reported that usage of adjusted mapping table provides additional benefits in terms of coding performance and coding gain balancing across luma and chroma components.

## Slide 3
Current VTM mapping function
It can be seen that at points: 30, 35, 37, 39, 41 and 43 function is not increasing, i.e. f(x) – f(x-1) = 0.
At the rest points function has increase of 1 i, i.e. f(x) – f(x-1) = 1.
For example, to reproduce current VVC mapping function following points need to be signalled: 30, 35, 37, 39, 41 and 43.
Chart: Chroma Qp mapping function
28 | 28 | 1
29 | 29 | 1
30 | 29 | 0
31 | 30 | 1
32 | 31 | 1
33 | 32 | 1
34 | 33 | 1
35 | 33 | 0
36 | 34 | 1
37 | 34 | 0
38 | 35 | 1
39 | 35 | 0
40 | 36 | 1
41 | 36 | 0
42 | 37 | 1
43 | 37 | 0
44 | 38 | 1
45 | 39 | 1
qPi | QPc | QPc[i] – QPc[-1]

## Slide 4
HDR specific mapping functions (from N0221)
For HDR specific functions the behavior is the same
20 | 20 | 20 | 20 | 20 | 1 | 1 | 1 | 1
21 | 21 | 20 | 21 | 20 | 1 | 0 | 1 | 0
22 | 21 | 20 | 21 | 21 | 0 | 0 | 0 | 1
23 | 21 | 21 | 22 | 21 | 0 | 1 | 1 | 0
24 | 22 | 21 | 22 | 22 | 1 | 0 | 0 | 1
25 | 22 | 21 | 23 | 22 | 0 | 0 | 1 | 0
26 | 23 | 21 | 23 | 22 | 1 | 0 | 0 | 0
27 | 23 | 21 | 24 | 23 | 0 | 0 | 1 | 1
28 | 24 | 22 | 24 | 23 | 1 | 1 | 0 | 0
29 | 24 | 22 | 25 | 23 | 0 | 0 | 1 | 0
30 | 25 | 22 | 25 | 24 | 1 | 0 | 0 | 1
31 | 25 | 22 | 26 | 24 | 0 | 0 | 1 | 0
32 | 26 | 22 | 26 | 24 | 1 | 0 | 0 | 0
33 | 26 | 22 | 27 | 25 | 0 | 0 | 1 | 1
34 | 27 | 23 | 27 | 25 | 1 | 1 | 0 | 0
35 | 27 | 23 | 28 | 25 | 0 | 0 | 1 | 0
36 | 28 | 24 | 28 | 26 | 1 | 1 | 0 | 1
37 | 28 | 25 | 29 | 26 | 0 | 1 | 1 | 0
38 | 29 | 26 | 29 | 27 | 1 | 1 | 0 | 1
39 | 29 | 27 | 29 | 27 | 0 | 1 | 0 | 0
40 | 29 | 28 | 29 | 28 | 0 | 1 | 0 | 1
41 | 29 | 29 | 30 | 29 | 0 | 1 | 1 | 1
42 | 30 | 29 | 31 | 29 | 1 | 0 | 1 | 0
43 | 30 | 30 | 31 | 30 | 0 | 1 | 0 | 1
44 | 31 | 31 | 32 | 31 | 1 | 1 | 1 | 1
45 | 32 | 32 | 32 | 32 | 1 | 1 | 0 | 1
46 | 33 | 33 | 33 | 33 | 1 | 1 | 1 | 1
47 | 33 | 33 | 33 | 33 | 0 | 0 | 0 | 0
48 | 34 | 34 | 34 | 34 | 1 | 1 | 1 | 1
49 | 34 | 34 | 34 | 34 | 0 | 0 | 0 | 0
50 | 35 | 35 | 35 | 35 | 1 | 1 | 1 | 1
51 | 35 | 35 | 35 | 35 | 0 | 0 | 0 | 0
52 | 36 | 36 | 36 | 36 | 1 | 1 | 1 | 1
53 | 36 | 36 | 36 | 36 | 0 | 0 | 0 | 0
54 | 37 | 37 | 37 | 37 | 1 | 1 | 1 | 1
55 | 37 | 37 | 37 | 37 | 0 | 0 | 0 | 0
56 | 38 | 38 | 38 | 38 | 1 | 1 | 1 | 1
qPi | QpC(709) Cb Cr | QpC(P3) Cb Cr | Deltas QPc[i]-QPc[i-1] | 

## Slide 5
Proposed syntax
seq_parameter_set_rbsp( ) { | Descriptor
sps_decoding_parameter_set_id | u(4)
… | 
chroma_qp_mapping_flag | u(1)
if( chroma_qp_mapping_flag ) | 
cqp_flat_points_minus1 | ue(v)
cqp_fp0 | ue(v)
for ( i = 1; i <= cqp_flat_points_minus1; i++ ) { | 
cqp_delta_fp_minus1[ i ] | u(v)
… | 
} | 

## Slide 6
chroma_qp_mapping_flag equal to 1 specifies that chroma Qp mapping table is signalled and overrides Table 8‑15 by cqpMappingTable which is used to derive QpC. chroma_qp_mapping_flag equal to 0 specifies that default chroma Qp mapping table specified in is used to derive QpC. When chroma_qp_mapping_flag is not present, it is inferred to be equal to 0.
cqp_flat_points_minus1 plus 1 specifies the number of points of where mapping function is non-increasing.
cqp_fp0 specifies the fist element of set of points where mapping function is non-increasing
cqp_delta_fp_minus1[ i ] plus 1 specifies the delta value between i-th and (i-1)-th element of set of points where mapping function is non-increasing.
The variable cQpFlat[] is derived as follows:
cQpFlat[ 0 ] = cqp_fp0; for( i = 1; i <= cqp_flat_points_minus1; i++ ) { cQpFlat[ i ] = cqp_delta_fp_minus1[ i ] + 1 + cQpFlat[ i - 1 ] }
The chroma QP mapping table cqpMappingTable[] is derived as follows:
cqpMappingTable [ 0 ] = 0; for( i = 1; i <= maxQP; i++ ) { incStep = 1 for ( j = 0; j <= cqp_flat_points_minus1 ; j++){ if ( i = = cQpFlat[ j ] ) incStep = 0 } cqpMappingTable [ i ] = cqpMappingTable [ i – 1 ] + incStep; }
Proposed semantics

## Slide 7
Adjusted mapping function
As a second aspect of the proposal we evaluated an adjusted mapping function having non-increasing regions at point 35, 39, 43.
The adjustment of mapping table can be enabled in cfg files by specifying non-increasing points:
CQPMap : 1
CQPMapPoints : 35, 39, 43
The mapping table was adjusted using test configuration files using proposed signalling mechanism.
In this experiment we keep chroma QP Offset equal to 1 for AI configuration only. For configurations RA, LDB and LDP the chroma QP Offset is set to 0.
Chart: Chroma Qp mapping function

## Slide 8
Simulation results: over VTM5.0
 | All Intra Main10 |  |  |  | 
 | Proposal Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.17% | 6.17% | 4.96% | 98% | 100%
Class A2 | -1.69% | 5.20% | 5.14% | 97% | 99%
Class B | -0.63% | 6.05% | 6.77% | 99% | 101%
Class C | -0.69% | 5.78% | 6.00% | 99% | 101%
Class E | -0.62% | 5.87% | 6.34% | 100% | 101%
Overall | -0.91% | 5.84% | 5.95% | 99% | 100%
Class D | -0.67% | 5.78% | 6.16% | 99% | 99%
Class F (optional) | -0.75% | 4.22% | 4.24% | 100% | 100%
 | Random Access Main 10 |  |  |  | 
 | Proposal Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -2.34% | 2.56% | -0.45% | 98% | 100%
Class A2 | -1.18% | -2.76% | -2.97% | 98% | 100%
Class B | -0.21% | -3.75% | -3.11% | 99% | 100%
Class C | -0.38% | -1.69% | -0.76% | 99% | 101%
Class E |  |  |  |  | 
Overall | -0.88% | -1.74% | -1.92% | 99% | 101%
Class D | -0.23% | -2.44% | -1.47% | 100% | 101%
Class F (optional) | -0.20% | -2.26% | -1.65% | 99% | 100%
 | Low delay B Main10 |  |  |  | 
 | Proposal Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.06% | -8.04% | -7.29% | 100% | 101%
Class C | 0.03% | -4.25% | -3.66% | 100% | 99%
Class E | 0.16% | -7.41% | -6.86% | 99% | 101%
Overall | 0.07% | -6.62% | -5.97% | 100% | 100%
Class D | 0.05% | -6.00% | -4.16% | 101% | 104%
Class F (optional) | -0.04% | -3.20% | -2.48% | 99% | 100%
 | Low delay P Main10 |  |  |  | 
 | Proposal Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.06% | -8.18% | -7.40% | 99% | 100%
Class C | -0.07% | -4.69% | -3.63% | 99% | 100%
Class E | 0.08% | -7.54% | -8.13% | 100% | 101%
Overall | 0.02% | -6.86% | -6.33% | 99% | 100%
Class D | 0.13% | -6.53% | -5.06% | 100% | 101%
Class F (optional) | 0.01% | -2.69% | -2.81% | 100% | 100%

## Slide 9
Simulation results: over HM
Delta: Proposal - VTM5.0 Proposal VTM5.0
 | All Intra Main10 |  |  |  |  |  |  |  | 
 | Delta Over VTM-5.0 |  |  | Proposal Over HM16.20 |  |  | VTM5.0 Over HM16.20 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A1 | -0.92% | 4.72% | 3.72% | -27.55% | -35.08% | -33.54% | -26.64% | -39.80% | -37.26%
Class A2 | -1.47% | 3.29% | 4.35% | -26.45% | -22.54% | -15.17% | -24.98% | -25.83% | -19.52%
Class B | -0.53% | 4.75% | 5.38% | -20.97% | -20.13% | -27.59% | -20.45% | -24.88% | -32.98%
Class C | -0.58% | 4.25% | 4.48% | -21.93% | -17.92% | -22.77% | -21.35% | -22.17% | -27.25%
Class E | -0.51% | 5.87% | 6.34% | -25.20% | -19.51% | -24.69% | -24.70% | -24.59% | -29.92%
Overall | -0.76% | 4.45% | 4.71% | -23.90% | -22.43% | -24.96% | -23.14% | -26.88% | -29.67%
Class D | -0.58% | 5.16% | 5.70% | -18.04% | -13.77% | -15.95% | -17.46% | -18.93% | -21.66%
Class F (optional) | -0.54% | 2.50% | 2.37% | -38.69% | -37.15% | -39.71% | -38.15% | -39.65% | -42.08%
 | Random Access Main 10 |  |  |  |  |  |  |  | 
 | Delta Over VTM-5.0 |  |  | Proposal Over HM16.20 |  |  | VTM5.0 Over HM16.20 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A1 | -1.80% | 3.34% | 1.33% | -36.71% | -36.50% | -41.69% | -34.92% | -39.81% | -43.03%
Class A2 | -1.09% | -0.83% | -1.26% | -40.12% | -37.86% | -31.98% | -39.04% | -37.01% | -30.74%
Class B | -0.20% | -1.04% | -0.45% | -32.97% | -38.92% | -40.65% | -32.76% | -37.86% | -40.19%
Class C | -0.36% | -1.06% | -0.11% | -28.21% | -28.14% | -31.23% | -27.86% | -27.10% | -31.11%
Class E |  |  |  |  |  |  |  |  | 
Overall | -0.74% | -0.13% | -0.16% | -33.88% | -35.35% | -36.61% | -33.14% | -35.21% | -36.45%
Class D | -0.23% | -1.35% | -0.09% | -26.31% | -26.11% | -28.32% | -26.07% | -24.83% | -28.17%
Class F (optional) | -0.30% | -1.31% | -0.89% | -40.11% | -41.99% | -43.80% | -39.81% | -40.67% | -42.91%

## Slide 10
Simulation results: over HM
 | Low delay B Main10 |  |  |  |  |  |  |  | 
 | Delta Over VTM-5.0 |  |  | Proposal Over HM16.20 |  |  | VTM5.0 Over HM16.20 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A1 |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  | 
Class B | -0.01% | -4.66% | -3.77% | -25.95% | -26.41% | -27.21% | -25.94% | -21.75% | -23.44%
Class C | -0.04% | -2.31% | -1.44% | -22.51% | -21.31% | -23.43% | -22.47% | -18.99% | -21.99%
Class E | 0.10% | -7.41% | -6.86% | -25.48% | -28.30% | -31.92% | -25.58% | -23.94% | -28.23%
Overall | 0.01% | -3.80% | -2.98% | -24.69% | -25.18% | -27.13% | -24.69% | -21.38% | -24.15%
Class D | -0.01% | -4.10% | -1.93% | -21.24% | -17.86% | -19.42% | -21.22% | -13.76% | -17.49%
Class F (optional) | -0.16% | -1.67% | -1.24% | -36.47% | -37.86% | -39.29% | -36.30% | -36.19% | -38.05%
 | Low delay P Main10 |  |  |  |  |  |  |  | 
 | Delta Over VTM-5.0 |  |  | Proposal Over HM16.20 |  |  | VTM5.0 Over HM16.20 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A1 |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  | 
Class B | -0.03% | -4.60% | -3.55% | -30.44% | -29.55% | -30.15% | -30.41% | -24.95% | -26.60%
Class C | -0.12% | -2.54% | -1.42% | -24.69% | -22.33% | -24.25% | -24.57% | -19.79% | -22.83%
Class E | 0.04% | -3.84% | -3.99% | -29.13% | -32.44% | -36.22% | -29.16% | -28.61% | -32.22%
Overall | -0.04% | -3.72% | -2.95% | -28.19% | -27.87% | -29.70% | -28.15% | -24.15% | -26.75%
Class D | 0.04% | -4.34% | -2.93% | -22.94% | -19.34% | -20.46% | -22.98% | -15.00% | -17.53%
Class F (optional) | -0.16% | -1.34% | -1.38% | -36.27% | -37.56% | -39.27% | -36.11% | -36.22% | -37.88%
Delta: Proposal - VTM5.0 Proposal VTM5.0

## Slide 11
Subjective examples
a) source | b) VTM5.0 | c) test

## Slide 12
Subjective examples
a) source | b) VTM5.0 | c) test

## Slide 13
It is proposed:
Add signaling mechanism for chroma QP mapping table
Enable usage of adjusted chroma QP mapping table
Keep chroma QP offset in CTC for AI configuration only
Conclusion
Thanks Samsung for cross-check!
 | All Intra Main10 |  |  | All Intra Main10 |  |  |  |  |  |  |  | 
 | Proposal Over VTM-5.0 |  |  | Delta Over VTM-5.0 |  |  | Proposal Over HM16.20 |  |  | VTM5.0 Over HM16.20 |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
AI | -0.91% | 5.84% | 5.95% | -0.76% | 4.45% | 4.71% | -23.90% | -22.43% | -24.96% | -23.14% | -26.88% | -29.67%
RA | -0.88% | 0.00% | 0.00% | -0.74% | -0.13% | -0.16% | -33.88% | -35.35% | -36.61% | -33.14% | -35.21% | -36.45%
LDB | 0.07% | -6.62% | -5.97% | 0.01% | -3.80% | -2.98% | -24.69% | -25.18% | -27.13% | -24.69% | -21.38% | -24.15%
LDP | 0.02% | -6.86% | -6.33% | -0.04% | -3.72% | -2.95% | -28.19% | -27.87% | -29.70% | -28.15% | -24.15% | -26.75%