## Slide 1
Non-CE3: MIP Modifications
Yong-Uk Yoon, Do-Hyeon Park, Jae-Gon Kim (KAU)
Jinho Lee, Jungwon Kang (ETRI)
15th JVET meeting
JVET-O0202

## Slide 2: Contents
Introduction
Proposed Modifications
  Change the positions deriving MIP-MPM candidates
  Remove the inverse mapping table
Experimental Results
Conclusions
Related Contributions

## Slide 3: I. Introduction
Matrix-weighted intra prediction (MIP)
  At the last meeting, MIP was adopted as a new intra coding tool
  If the MIP mode is applied
    The index of the MIP mode is signaled using 3 MPMs
  The positions of deriving MIP-MPM is different from the positions of deriving the regular MPM
    MIP-MPM: from top-left corner
    Regular MPM: from top-right and bottom-left corner

## Slide 4: Introduction
  The derivation of the MPMs is harmonized with regular intra modes by performing mode mapping (regular intra modes ↔ MIP modes)
    Based on the predefined mapping tables
      The forward mapping table
        Regular modes to MIP modes
      The inverse mapping table
        MIP modes to regular modes
        Used for the derivation of regular MPM modes and a chroma DM mode

## Slide 5: II. Proposed Modification 1
Modification 1: Change the positions deriving MIP-MPM candidates
  To keep the consistency of the reference positions deriving MPM
    Change the positions of deriving MIP-MPM to the same positions which derive regular MPM
      The top-left neighboring positions are changed to top-right and left-bottom neighboring positions

## Slide 6: Proposed Modification 2
Modification 2: Remove the inverse mapping table
  To simplify the MPM-list derivation process
    Remove the inverse mapping table by mapping the modes that require MIP mode to regular intra mode conversion to planar mode
    When deriving regular MPM or a chroma DM mode,
      If the referenced block is a MIP mode
      → The mode of the reference block is considered as planar mode

## Slide 7: III. Experimental Results
Experimental results of modification 1
  Change the positions deriving MIP-MPM candidates
  Over VTM5.0 in CTC
  AI: 0.00%/-0.05%/0.00% (Y/U/V) with 101%/100% (EncT/DecT)
  RA: -0.01%/-0.06%/-0.02% (Y/U/V) with 99%/100% (EncT/DecT)
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.03% | 0.11% | 104% | 101%
Class A2 | 0.01% | -0.02% | -0.08% | 102% | 100%
Class B | 0.00% | -0.02% | 0.03% | 101% | 101%
Class C | 0.01% | -0.12% | -0.01% | 98% | 100%
Class E | 0.01% | -0.11% | -0.06% | 101% | 100%
Overall | 0.00% | -0.05% | 0.00% | 101% | 100%
Class D | -0.01% | 0.02% | 0.00% | 99% | 102%
Class F | -0.01% | 0.02% | -0.02% | 102% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.15% | 0.04% | 100% | 100%
Class A2 | 0.01% | -0.10% | 0.04% | 100% | 100%
Class B | -0.01% | 0.06% | -0.11% | 97% | 100%
Class C | -0.04% | -0.10% | 0.00% | 98% | 100%
Class E |  |  |  |  | 
Overall | -0.01% | -0.06% | -0.02% | 99% | 100%
Class D | 0.00% | -0.12% | 0.44% | 98% | 100%
Class F | 0.02% | 0.11% | 0.04% | 102% | 100%

## Slide 8: Experimental Results
Experimental results of modification 2
  Remove the inverse mapping table
  Over VTM5.0 in CTC
  AI: 0.01%/-0.02%/0.04% (Y/U/V) with 99%/100% (EncT/DecT)
  RA: 0.01%/0.09%/0.06% (Y/U/V) with 97%/99% (EncT/DecT)
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.06% | 0.04% | 101% | 100%
Class A2 | 0.03% | 0.02% | -0.02% | 94% | 100%
Class B | 0.01% | -0.04% | 0.09% | 100% | 100%
Class C | 0.00% | -0.12% | 0.05% | 99% | 101%
Class E | 0.03% | 0.01% | 0.03% | 101% | 100%
Overall | 0.01% | -0.02% | 0.04% | 99% | 100%
Class D | -0.03% | 0.19% | 0.00% | 100% | 104%
Class F | -0.02% | -0.02% | 0.08% | 102% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.02% | 0.22% | 100% | 100%
Class A2 | 0.07% | 0.22% | 0.06% | 101% | 100%
Class B | 0.01% | 0.04% | 0.01% | 92% | 99%
Class C | -0.02% | 0.15% | 0.01% | 98% | 98%
Class E |  |  |  |  | 
Overall | 0.01% | 0.09% | 0.06% | 97% | 99%
Class D | 0.00% | 0.07% | 0.00% | 97% | 95%
Class F | 0.00% | 0.13% | 0.16% | 99% | 97%

## Slide 9: IV. Conclusions
MIP modifications
  Two modifications are proposed
    Change the positions deriving MIP-MPM candidates
    Remove the inverse mapping table
  Each modification shows almost unchanged coding performances
    Modification 1
      AI: 0.00%/-0.05%/0.00% (Y/U/V)
      RA: -0.01%/-0.06%/-0.02% (Y/U/V)
    Modification 2
      AI: 0.01%/-0.02%/0.04% (Y/U/V)
      RA: 0.01%/0.09%/0.06% (Y/U/V)
Suggest to adopt the proposed modifications to VTM6.0
Thanks “MediaTek” for cross-checking (JVET-O1024)

## Slide 10: V. Related contributions
Related contributions
  Related to modification 1
    JVET-O0464
  Related to modification 2
    JVET-O0170/JVET-O0171/JVET-O0187/JVET-O0255/ JVET-O0312/JVET-O0321/JVET-O0401/JVET-O0464/ JVET-O0469/JVET-O0598