## Slide 1: AHG8: On Adaptive Resolution Change (ARC) High-Level Syntax (HLS)
J. Samuelsson, S. Deshpande, A. Segall

## Slide 2: Proposal summary
Introduce PicSizeUnit to be used as unit for signalling all syntax elements that express picture width and height
Introduce conformance window for “reduced resolution pictures”
Use output resolution for calculating scaling factor between current picture and reference pictures

## Slide 3: Design goals
Allow the same flexibility for signaling width and height of reduced picture resolution as for full picture resolutions.
Minimize signaling overhead, both when ARC is used and when it is not used.
The exact width and height of different reduced resolution pictures should not have to be decided at the start of the CVS.

## Slide 4: SPS
The variable PicSizeUnit is derived as follows:
PicSizeUnit = ( pic_size_unit_minus1 + 1 )

## Slide 5: PPS

## Slide 6: Scale factor
The variables PicOutputWidthL and PicOutputHeightL are derived as follows:
PicOutputWidthL = pic_width_in_pic_size_units * PicSizeUnit − SubWidthC * ( pps_conf_win_right_offset + pps_conf_win_left_offset )
PicOutputHeightL = pic_height_in_pic_size_units * PicSizeUnit − SubHeightC * ( pps_conf_win_bottom_offset + pps_conf_win_top_offset )
The variables HoriScaleFp and VertScaleFp are derived as follows:
HoriScaleFp = ( RefPicOutputWidthL << 14 ) / PicOutputWidthL
VertScaleFp = ( RefPicOutputHeightL << 14 ) / PicOutputHeightL
where RefPicOutputWidthL and RefPicOutputHeightL are the PicOutputWidthL and the PicOutputHeightL of the picture used for reference, respectively.

## Slide 7: Impact on non-ARC use cases
Cost: 1 bit in the PPS
Gain: PicSizeUnit will generally make it possible to reduce the number of bits for signalling width and height. Example 3840x2160 can be signalled with 15 + 9 + 7 = 31 bits instead of 23 + 23 = 46 bits

## Slide 8: Proposal summary
Introduce PicSizeUnit to be used as unit for signalling all syntax elements that express picture width and height
Introduce conformance window for “reduced resolution pictures”
Use output resolution for calculating scaling factor between current picture and reference pictures

## Slide 10: Example
With MinCbSizeY equal to 8 all coded resolutions must be integer multiples of 8.
1920
1080
540
544
960

## Slide 11: Example
With MinCbSizeY equal to 8 all coded resolutions must be integer multiples of 8.
1920
1080
540
544
960
Actual scaling factor 2x
Derived scaling factor 1.985x