## Slide 1: Non-CE4: Simplified motion field storage for TPM
Na Zhang, Hongbin Liu, Li Zhang,
Kai Zhang, Yue Wang

## Slide 2: Summary
Motivation
  Motion field storage for TPM is a little complex.
Proposed solution
  In method #1, the mapping process is removed for the storage of motion information in the weighted area.
  In method #2, bi-prediction motion is always stored in the weighted area.
  In method #3, the changes of method #1 and method #2 are combined under the low delay check.
  No overall coding performance change for method #3.
Thanks LG for crosschecking (JVET-)

## Slide 3: Proposed Method
Method #1
The motion information to be stored in the weighted area is derived from (Mv1,refIdx1) and (Mv2,refIdx2) according to the following process:
If Mv1 and Mv2 are from different reference picture lists, then (Mv1,refIdx1) and (Mv2,refIdx2) are simply combined to form the bi-prediction motion.
Otherwise, if Mv1 and Mv2 are from the same list, uni-prediction motion (Mv2,refIdx2) is stored.
Three motion storage areas of 135 degree partition type for a 32x32 block

## Slide 4: Proposed Method
Method #2
The bi-prediction motion in the weighted area is derived from (Mv1,refIdx1) and (Mv2,refIdx2) according to the following process:
(Mv1,refIdx1) and (Mv2,refIdx2) are combined to form the bi-prediction motion with the reference picture list of partition 2 changed from LX to LY with Y = 1-X, if reference picture list of partition 1 is equal to LX.

## Slide 5: Proposed Method
Method #3
The motion information to be stored in the weighted area is derived from (Mv1,refIdx1) and (Mv2,refIdx2) according to the following process:
If Mv1 and Mv2 are from different reference picture lists, then (Mv1,refIdx1) and (Mv2,refIdx2) are simply combined to form the bi-prediction motion.
Otherwise, if Mv1 and Mv2 are from the same list LX,
  If all reference pictures are with POC values no greater than that of the current picture, Mv2 is converted to a LY (Y is 1-X) motion vector ( the same MV and refence picture index as that in LX). Then (Mv1,refIdx1) and (Mv2,refIdx2) are combined to form the bi-prediction motion;
  Otherwise, uni-prediction motion (Mv2,refIdx2) is stored.

## Slide 6: Simulation results
Anchor: VTM-5.0
Coding performance of the proposed method 1.
 | RA |  |  |  |  | LB |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.15% | 0.07% | 100% | 99% |  |  |  |  | 
Class A2 | 0.02% | 0.06% | 0.05% | 102% | 102% |  |  |  |  | 
Class B | 0.02% | -0.06% | 0.00% | 101% | 102% | 0.08% | 0.39% | 0.06% | 101% | 104%
Class C | -0.03% | -0.02% | -0.16% | 101% | 103% | 0.09% | 0.09% | 0.21% | 101% | 106%
Class E |  |  |  |  |  | 0.03% | 0.28% | -0.19% | 101% | 106%
Overall | 0.00% | -0.05% | -0.02% | 101% | 102% | 0.07% | 0.26% | 0.05% | 101% | 105%
Class D | -0.02% | 0.07% | 0.08% | 100% | 103% | 0.12% | -0.02% | 1.33% | 102% | 104%
Class F | 0.00% | 0.03% | 0.00% | 100% | 101% | 0.09% | 0.02% | -0.38% | 99% | 97%
Class SCC | -0.02% | -0.02% | -0.05% | 98% | 98% | -0.06% | -0.01% | -0.05% | 101% | 101%

## Slide 7: Simulation results
Anchor: VTM-5.0
 | RA |  |  |  |  | LB |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.18% | 0.04% | 100% | 99% |  |  |  |  | 
Class A2 | 0.06% | 0.09% | 0.07% | 101% | 101% |  |  |  |  | 
Class B | 0.07% | 0.11% | 0.04% | 101% | 102% | 0.00% | 0.00% | 0.00% | 100% | 99%
Class C | 0.07% | 0.12% | 0.00% | 101% | 105% | 0.00% | 0.00% | 0.00% | 101% | 108%
Class E |  |  |  |  |  | 0.00% | 0.00% | 0.00% | 101% | 103%
Overall | 0.06% | 0.05% | 0.03% | 101% | 102% | 0.00% | 0.00% | 0.00% | 101% | 103%
Class D | 0.06% | 0.01% | 0.08% | 101% | 105% | 0.00% | 0.00% | 0.00% | 101% | 105%
Class F | 0.06% | 0.07% | 0.00% | 100% | 102% | 0.00% | 0.00% | 0.00% | 98% | 96%
Class SCC | 0.03% | 0.06% | 0.02% | 99% | 98% | 0.00% | 0.00% | 0.00% | 100% | 97%
Coding performance of the proposed method 2.

## Slide 8: Simulation results
Anchor: VTM-5.0
Coding performance of the proposed method 3.
 | RA |  |  |  |  | LB |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.12% | -0.02% | 98% | 98% |  |  |  |  | 
Class A2 | 0.01% | -0.01% | 0.02% | 102% | 102% |  |  |  |  | 
Class B | 0.01% | 0.04% | -0.02% | 99% | 99% | 0.00% | 0.00% | 0.00% | 100% | 101%
Class C | -0.01% | -0.01% | -0.04% | 100% | 100% | 0.00% | 0.00% | 0.00% | 101% | 101%
Class E |  |  |  |  |  | 0.00% | 0.00% | 0.00% | 103% | 102%
Overall | 0.00% | -0.02% | -0.02% | 100% | 99% | 0.00% | 0.00% | 0.00% | 101% | 101%
Class D | -0.01% | -0.07% | 0.09% | 99% | 100% | 0.00% | 0.00% | 0.00% | 101% | 99%
Class F | -0.01% | 0.03% | 0.00% | 99% | 98% | 0.00% | 0.00% | 0.00% | 97% | 91%
Class SCC | -0.01% | -0.02% | -0.05% | 98% | 96% | 0.00% | 0.00% | 0.00% | 100% | 99%

## Slide 9: Conclusions
Three simplified motion field storage methods for TPM is proposed.
There is no overall coding performance change for method #3 compared to VTM5.0 after performing simplification.
It is recommended to adopt method #3 into VVC.

## Slide 10
Thanks！