## Slide 1: CE3-related: Simplification on CCLM process
Dae-Yeon Kim (Chips&Media)
Ju-Ock Lee (Chips&Media)
Sung-Chang Lim (ETRI)
Jinho Lee (ETRI)
Jungwon Kang (ETRI)

## Slide 2: Introduction
Coding gain of CCLM in VTM5.0
  1.9% / 17.2% / 17.5% on Y/Cb/Cr in AI (AHG13 report)
Current CCLM is not desirable in implementation-wise
  Many conditional branches
  Many down-sampling filter shapes
Fig 1. various down-sampling filter shapes for inner samples in the CCLM of WD5

## Slide 3: Proposed Methods
Motivation
  If it is assumed that all neighbor samples are available, CCLM process could be simplified.”
Method #1
  Before CCLM process, make all neighbor samples of Luma available by using “Reference sample construction” already defined in WD5
    General Intra modes (angular intra modes and CCLM)
  Usage of “Reference sample construction” without change
    Reference sample available marking process
    Reference sample substitution process
  By doing so, “Luma down-sampling” can be significantly simplified.

## Slide 4: Proposed Method #1

## Slide 5: Luma down-sampling in WD5
Inner samples (C, TI, LI, and I) of the corresponding luma area

## Slide 6: Simplified luma down-sampling
Inner samples of the corresponding luma area

## Slide 7: Luma down-sampling in WD5
Top neighbor (TN) samples of the corresponding luma area

## Slide 8: Simplified luma down-sampling
Top neighbor (TN) samples of the corresponding luma area

## Slide 9: Luma down-sampling in WD5
Left neighbor samples (LN) of the corresponding luma area

## Slide 10: Simplified luma down-sampling
Left neighbor samples (LN) of the corresponding luma area

## Slide 11: Proposed methods
Method #2
  Before CCLM process, make all neighbor samples of Luma & Chroma available by using “Reference sample construction”
  By doing so, “Luma down-sampling” as well as “Neighbor sample position derivation” and “Linear parameter derivation” can be simplified.
    “Reference sample construction” of chroma blocks is already invoked for CCLM in VTM and WD5.

## Slide 12: Simplified neighboring sample position derivation
If predModeIntra = = INTRA_LT_CCLM startPosT = (nTbW >> 2) startPosL = (nTbH >> 2) pickStepT = (nTbW) >> 1 pickStepL = (nTbH) >> 1 cntT = cntL = 2 else if predModeIntra = = INTRA_L_CCLM startPosL = (nTbH + Min(nTbW, nTbH)) >> 3 pickStepL = (nTbH + Min(nTbW, nTbH)) >> 2 cntL = 4 else if predModeIntra = = INTRA_T_CCLM startPosT = (nTbW + Min(nTbW, nTbH)) >> 3 pickStepT = (nTbW + Min(nTbW, nTbH)) >> 2 cntT = 4 pickPosL[ pos ] = (startPosL + pos * pickStepL), with pos = 0..cntL − 1. pickPosT[ pos ] = (startPosT + pos * pickStepT), with pos = 0..cntT − 1.
If predModeIntra = = INTRA_LT_CCLM numSampT = availT ? nTbW : 0 numSampL = availL ? nTbH : 0 else numSampT = ( availT && predModeIntra = = INTRA_T_CCLM ) ? ( nTbW + Min( numTopRight, nTbH ) ) : 0 numSampL = ( availL && predModeIntra = = INTRA_L_CCLM ) ? ( nTbH + Min( numLeftBelow, nTbW ) ) : 0 numIs4N = ( ( availT && availL && predModeIntra = = INTRA_LT_CCLM ) ? 0 : 1) startPosL = numSampL >> ( 2 + numIs4N ) startPosT = numSampT >> ( 2 + numIs4N ) pickStepL = Max( 1, numSampL >> ( 1 + numIs4N ) ) pickStepT = Max( 1, numSampT >> ( 1 + numIs4N ) ) cntL = cntT = 0 If availL = = TRUE cntL = Min( numSampL, ( 1 + numIs4N ) << 1 ) if availT = = TRUE cntT = Min( numSampT, ( 1 + numIs4N ) << 1 ) pickPosL[ pos ] = (startPosL + pos * pickStepL), with pos = 0.. cntL − 1. pickPosT[ pos ] = (startPosT + pos * pickStepT), with pos = 0.. cntT − 1.
Current WD5
Proposed
Simplified neighbor sample position derivation

## Slide 13: Simplified neighboring sample position derivation
Comparison of lengths of top and left neighboring samples
 | INTRA_LT_CCLM |  | INTRA_T_CCLM | INTRA_L_CCLM
 | Length of top neighboring samples | Length of left neighboring samples | Length of top neighboring samples | Length of left neighboring samples
WD 5.0 | 0 / tuWidth | 0 / tuHeight | tuWidth ~ tuWidth + Min(numAvailTR*, tuHeight) | tuHeight ~ tuHeight + Min(numAvailLB*, tuWidth)
Proposed | tuWidth | tuHeight | tuWidth + Min(tuWidth, tuHeight) | tuHeight + Min(tuWidth, tuHeight)
( * : variable numbers depending on neighboring sample availability)

## Slide 14: Simplified neighboring sample position derivation
Comparison of selected sample positions (gray-colored) for INTRA_T_CCLM
Comparison of selected sample positions (gray-colored) for INTRA_L_CCLM

## Slide 15: Simplified linear parameter derivation
In the current VTM, the number of selected neighbor samples
  2 or 4
    In case of 2, additional copy operation is needed to derive 4 samples.
By the prospoed method, the number of selected neighbor samples
  Always 4
Therefore, the additional copy operation can be removed in WD and VTM.

## Slide 16: Proposed method #1
“Luma down-sampling” is simplified by the proposed method #1
Luma down-sampling
Neighbor sample position derivation
Linear model parameter derivation
Chroma prediction sample generation
Luma neighbor sample construction
Luma down-sampling
Neighbor sample position derivation
Linear model parameter derivation
Chroma prediction sample generation
1.
2.
3.
4.
1.
2.
3.
4.
Simplified
CCLM in VTM 5.0
Proposed method #1
0.

## Slide 17: Proposed method #2
Three CCLM stages are simplified by the proposed method #2
  Neighbor sample position derivation
  Luma down-sampling
  Linear model parameter derivation
Luma down-sampling
Neighbor sample position derivation
Linear model parameter derivation
Chroma prediction sample generation
Luma neighbor sample construction
Luma down-sampling
Neighbor sample position derivation
Linear model parameter derivation
Chroma prediction sample generation
Chroma neighbor sample construction
1.
2.
3.
4.
1.
2.
3.
4.
Simplified
Simplified
Simplified
CCLM in VTM 5.0
Proposed method #2
0.

## Slide 18: Experimental results
Proposed method #1
 | All Intra |  |  |  | 
 | Over VTM 5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.04% | 0.01% | 100% | 101%
Class A2 | 0.00% | 0.01% | -0.01% | 99% | 101%
Class B | 0.00% | 0.00% | 0.01% | 100% | 101%
Class C | 0.00% | 0.00% | 0.05% | 100% | 101%
Class E | 0.00% | -0.03% | -0.04% | 100% | 101%
Overall | 0.00% | 0.00% | 0.01% | 100% | 101%
Class D | -0.01% | 0.10% | 0.06% | 100% | 101%
Class F | 0.00% | -0.01% | -0.02% | 101% | 101%
 | Random access |  |  |  | 
 | Over VTM 5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.27% | 0.06% | 100% | 101%
Class A2 | 0.01% | -0.01% | 0.03% | 100% | 100%
Class B | 0.01% | -0.13% | 0.02% | 100% | 100%
Class C | -0.03% | -0.09% | -0.13% | 100% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | -0.12% | -0.01% | 100% | 100%
Class D | 0.04% | -0.03% | 0.41% | 100% | 100%
Class F | -0.01% | -0.01% | -0.02% | 100% | 101%
The proposed method has potential complexity reduction because it is more SIMD-friendly.

## Slide 19: Experimental results
Proposed method #2
 | Random access |  |  |  | 
 | Over VTM 5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.03% | 0.27% | 100% | 100%
Class A2 | 0.05% | 0.04% | -0.02% | 100% | 100%
Class B | 0.02% | 0.15% | 0.14% | 100% | 100%
Class C | -0.03% | -0.11% | 0.05% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | 0.02% | 0.11% | 100% | 100%
Class D | 0.03% | 0.19% | 0.16% | 100% | 100%
Class F | 0.01% | 0.21% | 0.21% | 100% | 100%
 | All Intra |  |  |  | 
 | Over VTM 5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.16% | 0.20% | 100% | 100%
Class A2 | 0.01% | 0.00% | 0.01% | 99% | 100%
Class B | 0.00% | -0.04% | 0.04% | 100% | 100%
Class C | 0.01% | 0.03% | 0.12% | 101% | 100%
Class E | -0.01% | -0.03% | 0.00% | 100% | 100%
Overall | 0.00% | 0.02% | 0.08% | 100% | 100%
Class D | 0.00% | 0.07% | -0.13% | 100% | 100%
Class F | 0.01% | 0.19% | 0.27% | 101% | 100%
The proposed method has potential complexity reduction because it is more SIMD-friendly.

## Slide 20: Conclusion
Two simplifications are proposed for CCLM
  Simplified luma down-sampling by using reference sample construction
  Simplified fixed neighbor sample position derivation
  Simplified linear parameter derivation
Negligible coding efficiency impact
  Method #1 = AI : 0.00%/0.00%/0.01% , RA : 0.00%/-0.12%/-0.01%
  Method #2 = AI : 0.00%/0.02%/0.08% , RA : 0.01%/0.02%/0.11%
Benefits
  Parallel processing & SIMD friendly
  CCLM-related draft text reduction (8 page to 4.5 page)
It is suggested that this proposal is adopted to the next version of VTM.

## Slide 21
CCLM-related text of the current WD (8 pages)
CCLM-related text of the proposed method #2 (4.5 pages)

## Slide 22
Thanks Sony for cross-checking.
Any comments or questions?