## Slide 1: JVET-N0408 On rounding shift of MIP
K. Kondo, M. Ikeda, T. Suzuki (Sony)
Notes: 1

## Slide 2: Summary
Introduce the proposal
Report experiment results
Conclusion

## Slide 3: Simplification in matrix multiplication of MIP
Fix rounding shift to 8.
Change weight and bias parameters to fix an adaptive shift.

## Slide 4: Experiment results
For BD-rate and runtime, the impacts are negligible.
 | All Intra Main10 |  |  |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.02% | 0.01% | 100% | 100%
Class A2 | 0.00% | 0.01% | -0.03% | 102% | 100%
Class B | 0.01% | -0.08% | 0.01% | 100% | 100%
Class C | 0.01% | -0.01% | -0.03% | 99% | 100%
Class E | -0.01% | -0.04% | -0.03% | 100% | 100%
Overall | 0.00% | -0.03% | -0.01% | 100% | 100%
Class D | -0.01% | 0.05% | -0.14% | 100% | 100%
Class F | 0.00% | 0.06% | 0.07% | 100% | 100%
 | Random access Main10 |  |  |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.23% | 0.10% | 101% | 100%
Class A2 | 0.00% | 0.15% | 0.09% | 103% | 100%
Class B | 0.00% | -0.01% | -0.11% | 100% | 100%
Class C | 0.01% | -0.09% | 0.09% | 99% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | -0.04% | 0.03% | 101% | 100%
Class D | 0.07% | 0.11% | 0.01% | 100% | 100%
Class F | 0.01% | 0.05% | 0.12% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.35% | -0.21% | 99% | 100%
Class C | 0.03% | 0.20% | -0.17% | 98% | 100%
Class E | 0.10% | 0.16% | 0.41% | 99% | 100%
Overall | 0.03% | 0.25% | -0.04% | 99% | 100%
Class D | 0.04% | -0.03% | 0.84% | 99% | 100%
Thank HHI for this cross-check!

## Slide 5: Conclusions
Introduced the proposal
  Fix a rounding shift.
  Simplify specification text
    Can remove a table and 2 lines in text.
Reported experiment results
Recommendation
  This simplification is studied in CE.