## Slide 1: JVET-O0410 CE6-related: Signalling of Low Frequency Non-Separable Transform
Y. Kidani, K. Unno, K. Kawamura and S. Naito
KDDI Corp. (KDDI Research)

## Slide 2: Overview
In the previous meeting, LFNST was adopted to improve coding gain.
In current design, LFNST has two problems in terms of hardware complexity.
  Two counters for non-zero coeff. are required only to determine necessity of decoding lfnst_idx and it causes an additional function block as coefficient counting.
  VPDU constraint is violated because since the lfnst_idx decoding is located in CU.
Modifications of LFNST signalling are proposed to reduce the hardware complexity as follows:
  Removal of the two counters completely by using the existing sytanx elements.
  Block size restriction to meet VPDU constraints.
Results show almost no coding loss comparing CE6-2.1a.

## Slide 3: Problem Statement
In CE-6.2.1a, two counters for non-zero coeff. are required only to determine necessity of decoding lfnst_idx.
  numSigCoeff: use for checking the existence of non-zero coeff. in whole area.
  numZeroOutSigCoeff: use for checking the existence of non-zero coeff. in zeroing area.
With the two counters, lfnst_idx decoding is restricted when non-zero coeff. occur at only DC position or zeroing area.
However, it causes an additional function block as coeff. counting
  The worst case for coeff. scanning in each TU is 4,096 steps when TU size 64x64.
Therefore, these counters should be removed in terms of reducing hardware complexity.

## Slide 4: Problem Statement (cont.)
In addition, current decoding process of lfnst_idx violates the VPDU constraints in case that larger CU since the lfnst_idx is located not in the TU but in the CU.

## Slide 5: Proposal
Two modifications of LFNST signalling are proposed to reduce the hardware complexity as follows:
  Block size restriction, i.e., allowing the lfnst_idx deocing only when both width and height of CU ≤ 64x64. Noted that it doesn’t affect the experiment results under CTC.
  Removal of the two counters by using the existing sytanx elements.
 | VTM 5 | CE6-2.1a | Proposal
How to check existence of non-zero coeff. in non-DC position | NumSigCoeff | NumZeroOutSigCoeff | cbf & last_sig_coeff
How to check existence of non-zero coeff. in zeroing area | NumZeroOutSigCoeff | NumZeroOutSigCoeff | last_sig_coeff & coded_sub_block_flag

## Slide 6: Proposal (cont.)
If all of the following condition are true, lfnst_idx is decoded.
  Both last_sig_coeff and coded_sub_block_flag indicate the no existence of non-zero coeff. in the zeroing area which is variable depended on coding block size.
  cbf and last_sig_coeff satisfy one or more of the following conditions:
    The block tree type is dual tree, cbf in luma block is not equal to 0 and last_sig_coeff of luma block indicates the non-DC position.
    The block tree type is dual tree, one of the cbf in chroma block is not equal to 0 and last_sig_coeff of chroma blocks indicates the non-DC position.
    The block tree type is single tree, one of the cbf in luma/chroma blocks and one of the last_sig_coeff in luma/chroma blocks indicates the non-DC position.
Yellow area indicates where lastScanPos can be exists when LFNST is enabled.
White area indicates no existence of non-zero coeff. When LFNST is enabled.
CE6-2.1a
VTM5

## Slide 7: Results
Proposal is implemented on top of CE6-2.1a in JVET-O0094 and simulation is conducted under CTC of JVET-N1010.
Results shows that BD-rates and runtime are almost same as CE6-2.1a.
 | All Intra Main 10 over VTM5 |  |  |  |  | Random Access Main 10 over VTM5 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.04% | -0.03% | -0.21% | 90% | 99% | -0.02% | -0.13% | 0.09% | 97% | 99%
Class A2 | 0.02% | 0.05% | -0.04% | 88% | 99% | 0.00% | 0.10% | 0.07% | 98% | 100%
Class B | 0.10% | -0.22% | -0.08% | 89% | 99% | 0.04% | 0.04% | -0.14% | 98% | 100%
Class C | 0.12% | -0.17% | -0.10% | 87% | 100% | 0.02% | -0.09% | -0.03% | 97% | 99%
Class E | 0.11% | -0.18% | -0.06% | 90% | 99% |  |  |  |  | 
Overall | 0.08% | -0.12% | -0.09% | 89% | 99% | 0.01% | -0.02% | -0.02% | 97% | 99%
Class D | 0.12% | 0.07% | -0.12% | 88% | 102% | 0.06% | 0.38% | -0.02% | 98% | 98%
Class F | 0.04% | -0.03% | 0.06% | 92% | 99% | 0.03% | -0.03% | 0.09% | 97% | 100%
 | All Intra Main 10 over VTM5 |  |  |  |  | Random Access Main 10 over VTM5 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.11% | 0.01% | 91% | 97% | 0.03% | 0.04% | 0.08% | 97% | 100%
Class A2 | 0.00% | 0.10% | 0.11% | 88% | 99% | -0.01% | 0.08% | 0.05% | 98% | 98%
Class B | 0.08% | -0.06% | 0.04% | 90% | 100% | 0.03% | 0.03% | -0.13% | 98% | 102%
Class C | 0.10% | -0.12% | 0.05% | 88% | 100% | 0.03% | -0.09% | 0.03% | 98% | 99%
Class E | 0.10% | -0.06% | 0.03% | 91% | 101% |  |  |  |  | 
Overall | 0.06% | -0.02% | 0.05% | 90% | 99% | 0.02% | 0.01% | -0.01% | 97% | 100%
Class D | 0.10% | 0.14% | -0.12% | 89% | 101% | 0.06% | 0.23% | 0.11% | 98% | 101%
Class F | 0.02% | 0.09% | 0.09% | 94% | 99% | 0.06% | 0.10% | 0.05% | 97% | 100%
CE6-2.1a + proposal (Anchor is VTM5)
CE6-2.1a (Anchor is VTM5)

## Slide 8: Conclusion
Modification of LFNST signalling is proposed.
  Block size restriction to meet VPDU constraints.
  Removal of the two counters by using the existing sytanx elements.
Proposed signaling can remove coeff. counting steps completely.
Results show BD-rates and runtime are almost same as CE6-.2.1a
  CE6-2.1 + proposal:
    AI: 0.08% luma -0.12%/-0.09% chroma with 89%/99% coding runtime
    RA: 0.01% luma -0.02%/-0.02% chroma with 97%/99% coding runtime
  CE6-2.1:
    AI: 0.06% luma -0.02%/0.05% chroma with 90%/99% coding runtime
    RA: 0.02% luma 0.01%/-0.01% chroma with 97%/100% coding runtime
Suggest to adopt the proposal to WD/VTM in terms of reducing HW complexity.
Thanks for LGE cross checking.

## Slide 9: Appendix
The results of proposal implemented on top of VTM5
The results where only following condition is changed vs. above results.
  The block tree type is single tree, the cbf in luma blocks and the last_sig_coeff in luma block indicates the non-DC position.
 | All Intra Main 10 over VTM5 |  |  |  |  | Random Access Main 10 over VTM5 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.11% | -0.24% | 100% | 100% | 0.01% | -0.20% | 0.04% | 100% | 100%
Class A2 | 0.03% | -0.10% | -0.17% | 99% | 99% | 0.01% | 0.13% | -0.03% | 100% | 99%
Class B | 0.02% | -0.18% | -0.13% | 100% | 100% | 0.03% | -0.11% | -0.06% | 100% | 100%
Class C | 0.02% | -0.15% | -0.04% | 99% | 99% | -0.04% | -0.30% | -0.05% | 100% | 100%
Class E | 0.02% | -0.12% | -0.11% | 99% | 99% |  |  |  |  | 
Overall | 0.02% | -0.14% | -0.13% | 99% | 100% | 0.00% | -0.13% | -0.03% | 100% | 100%
Class D | 0.01% | 0.07% | -0.05% | 100% | 100% | 0.02% | -0.01% | 0.03% | 100% | 100%
Class F | 0.00% | -0.05% | 0.05% | 99% | 99% | -0.01% | -0.01% | -0.01% | 100% | 99%
 | All Intra Main 10 over VTM5 |  |  |  |  | Random Access Main 10 over VTM5 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.11% | -0.24% | 100% | 100% | 0.00% | -0.09% | 0.04% | 100% | 100%
Class A2 | 0.03% | -0.10% | -0.17% | 99% | 99% | 0.01% | 0.06% | -0.09% | 100% | 99%
Class B | 0.02% | -0.18% | -0.13% | 100% | 100% | 0.02% | -0.14% | 0.02% | 100% | 100%
Class C | 0.02% | -0.15% | -0.04% | 99% | 99% | -0.07% | -0.21% | 0.05% | 100% | 100%
Class E | 0.02% | -0.12% | -0.11% | 99% | 99% |  |  |  |  | 
Overall | 0.02% | -0.14% | -0.13% | 99% | 100% | -0.01% | -0.11% | 0.01% | 100% | 100%
Class D | 0.01% | 0.07% | -0.05% | 100% | 100% | 0.02% | 0.05% | 0.06% | 100% | 100%
Class F | 0.00% | -0.05% | 0.05% | 99% | 99% | -0.01% | 0.02% | 0.04% | 100% | 100%

## Slide 10: Appendix (cont.)
Analyze the number of LFNST applied blocks between VTM5 and VTM5+proposal to investigate the effect of modified signalling.
It is confirmed that the proportion of occurrence in LFNST applied is almost same among VTM5 and VTM5+proposal.
Size | 4 |  | 8 |  | 16 |  | 32 |  | 64 | 
4 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 2 | 0 | 0
8 | 0 | 0 | 1 | 4 | 20 | 29 | 24 | 22 | 0 | 0
16 | 0 | 1 | 8 | 16 | 68 | 66 | 198 | 52 | 0 | 0
32 | 0 | 1 | 23 | 14 | 158 | 41 | 1122 | 393 | 0 | 0
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 683 | 0
Size | 4 |  | 8 |  | 16 |  | 32 |  | 64 | 
4 | 0 | 0 | 0 | 0 | 0 | 3 | 1 | 0 | 0 | 0
8 | 0 | 0 | 2 | 7 | 25 | 32 | 20 | 27 | 0 | 0
16 | 0 | 0 | 10 | 11 | 65 | 53 | 216 | 58 | 0 | 0
32 | 0 | 0 | 23 | 15 | 185 | 40 | 1128 | 421 | 0 | 0
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 676 | 0
Size | 4 |  | 8 |  | 16 |  | 32 |  | 64 | 
4 | 0 | 23 | 5 | 40 | 16 | 53 | 6 | 44 | 0 | 0
8 | 5 | 30 | 59 | 101 | 269 | 285 | 153 | 125 | 0 | 0
16 | 6 | 18 | 230 | 241 | 929 | 517 | 774 | 301 | 0 | 0
32 | 4 | 13 | 178 | 143 | 882 | 370 | 1373 | 477 | 0 | 0
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 45 | 0
Size | 4 |  | 8 |  | 16 |  | 32 |  | 64 | 
4 | 0 | 68 | 4 | 109 | 13 | 166 | 11 | 67 | 0 | 0
8 | 3 | 64 | 63 | 285 | 270 | 607 | 180 | 310 | 0 | 0
16 | 11 | 99 | 235 | 574 | 955 | 1061 | 829 | 559 | 0 | 0
32 | 7 | 30 | 159 | 252 | 887 | 568 | 1327 | 854 | 0 | 0
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 50 | 0
FoodMarket @VTM5, AI10/QP22, POC=0
FoodMarket @VTM5+Prop., AI0/QP22, POC=0
FoodMarket @VTM5, AI10/QP37, POC=0
FoodMarket @VTM5+Prop. AI10/QP37, POC=0
Note that left/right columns indicates the number of luma/chroma blocks, respectively.

## Slide 11: Appendix (cont.)
Analyze the number of LFNST applied blocks between VTM5 and VTM5+proposal to investigate the effect of modified signalling.
It is confirmed that the proportion of occurrence in LFNST applied is almost same among VTM5 and VTM5+proposal.
Size | 4 |  | 8 |  | 16 |  | 32 |  | 64 | 
4 | 76 | 14 | 71 | 20 | 22 | 9 | 9 | 8 | 0 | 0
8 | 107 | 8 | 43 | 22 | 47 | 4 | 11 | 4 | 0 | 0
16 | 20 | 1 | 48 | 14 | 71 | 7 | 25 | 1 | 0 | 0
32 | 0 | 0 | 5 | 1 | 36 | 0 | 35 | 1 | 0 | 0
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Size | 4 |  | 8 |  | 16 |  | 32 |  | 64 | 
4 | 78 | 5 | 60 | 32 | 13 | 7 | 9 | 5 | 0 | 0
8 | 105 | 13 | 42 | 13 | 43 | 5 | 15 | 1 | 0 | 0
16 | 22 | 3 | 48 | 7 | 64 | 7 | 29 | 2 | 0 | 0
32 | 0 | 1 | 6 | 0 | 26 | 0 | 35 | 0 | 0 | 0
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Size | 4 |  | 8 |  | 16 |  | 32 |  | 64 | 
4 | 815 | 185 | 633 | 128 | 78 | 7 | 1 | 2 | 0 | 0
8 | 713 | 78 | 422 | 32 | 70 | 11 | 0 | 0 | 0 | 0
16 | 55 | 4 | 75 | 11 | 33 | 12 | 1 | 2 | 0 | 0
32 | 0 | 0 | 1 | 0 | 1 | 2 | 0 | 1 | 0 | 0
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Size | 4 |  | 8 |  | 16 |  | 32 |  | 64 | 
4 | 907 | 153 | 663 | 121 | 71 | 4 | 2 | 5 | 0 | 0
8 | 758 | 90 | 457 | 32 | 81 | 13 | 2 | 0 | 0 | 0
16 | 49 | 6 | 80 | 16 | 34 | 16 | 1 | 2 | 0 | 0
32 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 3 | 0 | 0
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
BasketballDrillText @VTM5, AI10/QP22, POC=0
BasketballDrillText @VTM5+Prop., AI0/QP22, POC=0
BasketballDrillText @VTM5, AI10/QP37, POC=0
BasketballDrillText @VTM5+Prop. AI10/QP37, POC=0
Note that left/right columns indicates the number of luma/chroma blocks, respectively.