## Slide 1: JVET-O0503 Non-CE9: Modifications to MMVD for CUs eligible for DMVR
S. Sethuraman
Ittiam Systems

## Slide 2: Enabling DMVR for MMVD
Currently DMVR is disabled for MMVD CUs
  Due to high EncT reported in JVET-M0147
CE9-2 studies this
  CE9-2.1a – JVET-N0145/O-0077 – Only perform DMVR for MVD magnitudes 2 and above
  Offers 0.1% coding gain, but has higher EncT
  CE9-2.1b – Non-normative optimizations proposed, brings EncT to 102%

## Slide 3: Proposed solution
Studies the MVD magnitudes where refinement on top of signaled MVD helps the most
Normative changes to MMVD CUs that are also eligible to perform DMVR
  Test-2: Restrict refinements to be performed only for MVD magnitudes 4 and 8 (i.e. not do it for MVD magnitudes 16 and 32 in class A when compared to CE9-2.1)
  Test-3: In addition to Test-2, MVD magnitude 1 is removed from the list of MVD magnitudes used by MMVD (one less bin for MVD magnitudes of 2 and above)
  Test-4: In addition to Test-3, MVD magnitude 2 is also removed from the lsit of MVD magnitudes used by MMVD (two less bins for MVD magnitudes of 4 and above)
Non-normative changes
  Test-1:
    No chroma MC during the SATD stage
    Re-use of luma MC from SATD stage to the RDO stage (if MC has no change)
  Test-5:
    Apply CE9-1.2b like early termination (based on not having 20% reduction for a given MVD magnitude over a preceding MVD magnitude in a direction) on top of Test-3

## Slide 4: Benefits
Additional reduction of encoding time over CE9-2.1b
  Test-2, 3, 4: Normatively
  Test-1: Non-normatively
Normative restriction enables practical encoders to reduce their search complexity related to finding the best MVD direction and distance

## Slide 5: Test-1
Bit-exact (non-normative) change
EncT reduces by ~1% relative to VTM5 with proposed Test-1 changes

## Slide 6: Test-2
On top of Test-1
Most of the BDRATE gain of CE9-2.1 are centered at MVD distances 4 and 8
  Only class A is affected (as others do only up to MVD distance 8)
EncT increases by 3%

## Slide 7: Test-3
On top of Test-2
Removal of MVD magnitude 1 from the list improves both BDRATE and encoder complexity

## Slide 8: Test-4
On top of Test-3
Removal of MVD magnitude 2 from the list introduces a small BDRATE drop (0.01% relative to CE9-2.1a)
EncT at similar levels as Test-3

## Slide 9: Test-5
CE9-2.1b non-normative optimization on top of Test-3
Due to removal of MVD distance 1, unconditional evaluation for MVD distances 2 and 4 are incurred
BDRATE gains similar to Test-3 (a small improvement over CE9-2.1.b) and has EncT on part with VTM5.0 (due to non-normative changes of Test-1 and CE9-2.1b)

## Slide 10: Conclusions
MVD distances of 1 and 2 occur infrequently when a current MMVD CU is also eligible for DMVR
Most of the benefit of DMVR on top of MMVD is localized on MVD distances 4 and 8
Normative change
  Proposes to perform DMVR only for MVD distances 4 and 8
  Proposes to remove MVD distance of 1 from the list when current CU is also eligible for DMVR
With the non-normative changes, EncT is brought to VTM5.0 levels while enabling DMVR for MMVD
Removal of MVD distances improves coding gain by reducing the number of bins for the remaining MVD distances.
It is requested that proposed normative and non-normative changes be considered for adoption

## Slide 11: Thanks to Sharp for Cross-checking!