## Slide 1: JVET-O0506 Non-CE9: An improvement to extended predicted sample value derivation in BDOF
S. Sethuraman
Ittiam Systems

## Slide 2: Extended predicted sample values for sub-block boundary gradients
Sub-block boundary sample gradients require extended predicted sample values to the left/top/right/bottom of the sub-block
  (M x N) sub-block requires (M + 2) x (N + 2) sample values to compute the horizontal and vertical gradients
Current method
  Uses integer grid reference samples with truncation of fractional part
  Adopted to reduce the complexity of performing 8-tap interpolation filtering for the extended samples
    0.05% BDRATE drop was there at the time of adoption from JVET-M0487
Drawbacks
  Sample value can be from a position that is up to 15/16th of a pixel distance in both horizontal and vertical directions

## Slide 3: Proposed Solution
Instead of truncating the fractional sample offset completely, it is proposed to round the fractional sample offset in the horizontal and vertical directions while selecting the integer grid sample position from which the extended predicted sample value is obtained
  (x_pos_L0, y_pos_L0) = ((x_spel_pos_L0 + 8) >> 4, (y_spel_pos_L0 + 8) >> 4)
  (x_pos_L1, y_pos_L1) = ((x_spel_pos_L1 + 8) >> 4, (y_spel_pos_L1 + 8) >> 4)
  where
  (x_spel_pos_L0, y_ spel_pos _L0) = (xSb + dx + MVLx0, ySb + dy + MVLy0)
  (x_ spel_pos _L1, y_ spel_pos _L1) = (xSb + dx + MVLx1, ySb + dy + MVLy1)
  (dx, dy) – position offset from the top-left position of sub-block to the extended sample position
  (MVLx0, MVLy0) – L0 motion vector for the sub-block
  (MVLx1, MVLy1) – L1 motion vector for the sub-block
Benefit
  Maximum distance from the sub-pixel accurate position is each direction to the integer grid sample position is 8/16 (instead of 15/16 earlier)

## Slide 4: Results
The fix closes the BDRATE gap compared to the option of using 8-tap interpolation filter to obtain the extended samples
No impact to EncT/Dect

## Slide 5: Conclusions
The extended predicted sample for sub-block boundary gradient computations are obtained through a rounding process instead of truncation to obtain the nearest integer grid reference sample value
A BDRATE gain of 0.04% with no impact on EncT/DecT is observed
A similar proposal is made in JVET-N0615 as well
  There was a small implementation bug identified, after fixing which, the results of this proposal are identical to JVET-N0615
It is requested that this fix be adopted into the next VTM

## Slide 6: Thanks to Qualcomm for Cross-checking!