## Slide 1
JVET-0516
non-CE4: BCW for pairwise

## Slide 2
Motivation
In both merge and affine merge lists
  All candidates can inherit BCW
  Except temporal candidates and zeros (BCW not temporally saved)
  Pairwise candidate has no BCW (only candidate without BCW inheritance)
JVET-O0516 proposes 3 methods of BCW inheritance for pairwise
© 2019 InterDigital, Inc. All Rights Reserved.
Merge | Affine Merge
5x spatial | 1x SbTMVP
1x temporal | 2x inherited affine
5x HMVP | 6x constructed affine
1x pairwise | Zeros
zeros | 
With BCW ( last meeting adoption)
Without BCW (but possible)
N/A (BCW not temporally saved)

## Slide 3
Pairwise construction in VTM-5.0
Pairwise candidate in VTM-5.0
  Based on 2 first merge candidates
  Both use reference picture list Lx
    Average MVs and use reference picture of 1st candidate
  Only one uses reference picture list Lx
    Use MV and reference picture of this candidate for Lx
Some BCW index can be derived if:
  At least one bi-directional candidate is used
  A bi-directional pairwise candidate is being computed
© 2019 InterDigital, Inc. All Rights Reserved.
 | Cand0 |  | Cand1 |  | Pairwise | 
 | L0 | L1 | L0 | L1 | L0 | L1
Reference frames | a0 | a1 | b0 | b1 | a0 | a1
 | a0 | a1 | b0 | / | a0 | a1
 | a0 | a1 | / | b1 | a0 | a1
 | a0 | / | b0 | b1 | a0 | b1
 | / | a1 | b0 | b1 | b0 | a1
 | a0 | / | b0 | / | a0 | /
 | a0 | / | / | b1 | a0 | b1
 | / | a1 | b0 | / | b0 | a1
 | / | a1 | / | b1 | / | a1
Darker for bi-directional candidates

## Slide 4
JVET-O0516 BCW for pairwise Proposed method 1
BCW for pairwise candidate
  When 1st candidate is bi-directional (3 first lines)
    Pairwise inherits BCW from 1st candidate
  When 2nd candidate is bi-directional (2 following lines) with same reference picture on common list (b0=a0 or b1=a1)
    Pairwise inherits BCW from 2nd candidate
© 2019 InterDigital, Inc. All Rights Reserved.
 | Cand0 |  | Cand1 |  | Pairwise | 
 | L0 | L1 | L0 | L1 | L0 | L1
Reference frames | a0 | a1 | b0 | b1 | a0 | a1
 | a0 | a1 | b0 | / | a0 | a1
 | a0 | a1 | / | b1 | a0 | a1
 | a0 | / | b0 | b1 | a0 | b1
 | / | a1 | b0 | b1 | b0 | a1
 | a0 | / | b0 | / | a0 | /
 | a0 | / | / | b1 | a0 | b1
 | / | a1 | b0 | / | b0 | a1
 | / | a1 | / | b1 | / | a1
Darker for bi-directional candidates

## Slide 5
BCW for pairwise candidate
  Same as method 1 without reference picture indices comparisons
  When 1st candidate is bi-directional (3 first lines)
    Pairwise inherits BCW from 1st candidate
Same method as method 2 of JVET-O0367
© 2019 InterDigital, Inc. All Rights Reserved.
 | Cand0 |  | Cand1 |  | Pairwise | 
 | L0 | L1 | L0 | L1 | L0 | L1
Reference frames | a0 | a1 | b0 | b1 | a0 | a1
 | a0 | a1 | b0 | / | a0 | a1
 | a0 | a1 | / | b1 | a0 | a1
 | a0 | / | b0 | b1 | a0 | b1
 | / | a1 | b0 | b1 | b0 | a1
 | a0 | / | b0 | / | a0 | /
 | a0 | / | / | b1 | a0 | b1
 | / | a1 | b0 | / | b0 | a1
 | / | a1 | / | b1 | / | a1
Darker for bi-directional candidates
JVET-O0516 BCW for pairwise Proposed method 2

## Slide 6
BCW for pairwise candidate
  Even more restricted method
  When both candidates are bi-directional (first line) and have same BCW weights
    Pairwise inherits BCW from 1st candidate
Same method as method 1 of JVET-O0367
© 2019 InterDigital, Inc. All Rights Reserved.
 | Cand0 |  | Cand1 |  | Pairwise | 
 | L0 | L1 | L0 | L1 | L0 | L1
Reference frames | a0 | a1 | b0 | b1 | a0 | a1
 | a0 | a1 | b0 | / | a0 | a1
 | a0 | a1 | / | b1 | a0 | a1
 | a0 | / | b0 | b1 | a0 | b1
 | / | a1 | b0 | b1 | b0 | a1
 | a0 | / | b0 | / | a0 | /
 | a0 | / | / | b1 | a0 | b1
 | / | a1 | b0 | / | b0 | a1
 | / | a1 | / | b1 | / | a1
Darker for bi-directional candidates
JVET-O0516 BCW for pairwise Proposed method 3

## Slide 7
Experimental results Method 1
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.19% | 0.15% | 101% | 101%
Class A2 | 0.05% | 0.04% | 0.05% | 100% | 101%
Class B | 0.04% | 0.04% | -0.07% | 99% | 99%
Class C | 0.00% | 0.07% | -0.15% | 99% | 97%
Overall | 0.03% | 0.00% | -0.03% | 100% | 99%
Class D | 0.03% | 0.05% | 0.11% | 99% | 98%
Class F (optional) | 0.00% | 0.08% | 0.04% | 100% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.02% | 0.20% | -0.17% | 101% | 101%
Class C | 0.00% | -0.20% | -0.05% | 100% | 101%
Class E | -0.03% | -0.44% | -0.65% | 100% | 100%
Overall | -0.01% | -0.09% | -0.25% | 101% | 101%
Class D | 0.01% | -0.10% | 0.69% | 100% | 99%
Class F (optional) | -0.12% | -0.17% | -0.34% | 101% | 102%

## Slide 8
Experimental results Method 2
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.13% | 0.12% | 101% | 101%
Class A2 | 0.05% | 0.07% | 0.06% | 100% | 100%
Class B | 0.02% | 0.00% | -0.03% | 100% | 100%
Class C | -0.01% | 0.01% | -0.05% | 101% | 101%
Overall | 0.02% | -0.01% | 0.01% | 100% | 101%
Class D | 0.02% | 0.11% | -0.04% | 101% | 100%
Class F (optional) | 0.00% | 0.06% | -0.01% | 99% | 96%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.03% | 0.05% | -0.18% | 100% | 99%
Class C | 0.01% | 0.16% | -0.14% | 100% | 100%
Class E | -0.07% | -0.22% | -0.64% | 100% | 100%
Overall | -0.02% | 0.02% | -0.28% | 100% | 99%
Class D | -0.03% | 0.11% | 0.49% | 99% | 99%
Class F (optional) | -0.04% | -0.13% | -0.50% | 100% | 99%

## Slide 9
Experimental results Method 3
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.09% | 0.09% | 101% | 101%
Class A2 | 0.03% | -0.02% | 0.03% | 100% | 101%
Class B | 0.01% | -0.02% | -0.10% | 100% | 100%
Class C | -0.02% | -0.06% | 0.01% | 101% | 101%
Overall | 0.00% | -0.04% | -0.01% | 100% | 101%
Class D | 0.00% | 0.09% | -0.03% | 101% | 100%
Class F (optional) | -0.02% | 0.07% | 0.01% | 99% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.01% | 0.36% | -0.09% | 100% | 98%
Class C | 0.04% | 0.08% | -0.04% | 100% | 101%
Class E | -0.03% | -0.03% | -0.30% | 100% | 101%
Overall | 0.00% | 0.17% | -0.13% | 100% | 100%
Class D | 0.01% | -0.31% | 0.28% | 99% | 97%
Class F (optional) | 0.05% | -0.25% | 0.20% | 99% | 99%

## Slide 10
Ticket#312 bug fix
  Fix initialization problem in BCW inheritance for constructed affine
Perfectly match method 1results of JVET-O0367
Partial results Method 3 with Ticket#312 bug fix
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 with Ticket#312 bug-fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.02% | -0.08% | 101% | 100%
Class C | 0.00% | -0.05% | 0.09% | 101% | 99%
Overall |  |  |  |  | 
Class D | 0.01% | 0.08% | -0.02% | 101% | 101%
Class F (optional) |  |  |  |  | 
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 with Ticket#312 bug-fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class B |  |  |  |  | 
Class C | 0.01% | 0.08% | -0.19% | 101% | 100%
Class E | -0.04% | -0.39% | -0.20% | 101% | 101%
Overall |  |  |  |  | 
Class D | -0.04% | 0.07% | -0.31% | 101% | 100%
Class F (optional) |  |  |  |  | 

## Slide 11: JVET-O0516 BCW for pairwise Conclusion
Proposed 3 methods for BCW inheritance for pairwise candidate
  2 first methods
    Address most bi-directional pairwise candidates
    Give small losses in RA and small gains in LDB
  Method 3
    Address bi-directional pairwise candidate created from bi-directional candidates
    Keep same performances as VTM-5.0
    (Give small gains in LDB with Ticket#312 bug fix)
Recommended adoption of method 3 (or method 2)
  Seems to be the best from coding efficiency viewpoint.
Similar to JVET-O0367
Thanks to LGE for crosscheck

## Slide 12: Thank you