## Slide 1: GT1 flag coding
JVET-O0520
Advanced Technology Team
European Professional Engineering
Sony Europe BV.
Adrian Browne / Steve Keating / Karl Sharman
Sony Corp.

## Slide 2: Introduction
For some sequences in CTC and low QP it was observed that cabac_zero_words were being added in the following situation:
  An unusually high number of GT1 flags have been coded
    Sometimes up to 30% of the total CABAC coded bins
  The value of these flags is mostly 0
    For some clips at some QPs this is true for > 95% GT1 flags
    Coded very efficiently
  For any sequence in the test set this only occurs at a limited number of QP levels
  Mostly seen in random access, but also seen in intra and low delay sequences
    DaylightRoad2 at QP=17 RA ~2% of output stream was cabac_zero_word
Possible causes
  Highly predictable regions may leave only low levels of quantized noise
  Dependent quantization
    Shown experimentally but may be RDO effect rather than DepQuant

## Slide 3: Introduction
Example: DaylightRoad2 (RA)
At QP=17
  23.5% of the total CABAC bins coded are GT1 Flags
  95.9% of these have a value of 0
  22.5% of the total CABAC bins are GT1 Flags with value 0

## Slide 4: Proposal
Introduce a GT1 group flag similar to coefficient group flag
  Indicates a group contains no values with magnitude > 1
  GT1 flags could be skipped for such blocks
    Reduces number of flags
    Reduces coding efficiency
    Reduces / removes need for cabac_zero_word padding
Only code the flag when it is statistically likely
  High probability that no coefficient has magnitude > 1
  No change for sequences that don’t exhibit excessive GT1 usage

## Slide 5: Implementation
Modified CABAC context to support two functions
  Read of current state
  Update without producing an output to bitstream
Two implementations developed
  First: TU based
    Pre-condition based on (x, y) position of last significant coefficient
    Always codes top-left coefficients with GT1 flags
      Most likely to be > 1
      Excluded for computation of GT1 group flag
  Second: sub-TU based
    Only code GT1 group flag if at least 8 possible coefficients exist in TU

## Slide 6: Results – TU based implementation
Elimination of cabac_zero_word in:
  DaylightRoad2, random access at QP=17
  BasketballDrill, low delay B at QP=7
  Cactus, random access at QP=12
 |  |  | RA |  | 
 |  |  | Over VTM |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.03% | -0.06% | 101% | 101%
Class A2 | 0.02% | 0.01% | 0.08% | 101% | 101%
Class B | 0.02% | 0.05% | -0.08% | 101% | 101%
Class C | -0.01% | -0.13% | -0.13% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.01% | -0.02% | -0.06% | 101% | 101%
Class D | 0.01% | -0.04% | 0.02% | 101% | 102%
Class F | 0.00% | 0.02% | 0.02% | 102% | 101%
 |  |  | RA(LowQP) |  | 
 |  |  | Over VTM |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.05% | 0.05% | 101% | 101%
Class A2 | -0.09% | -0.02% | -0.04% | 100% | 100%
Class B | 0.01% | 0.06% | 0.07% | 102% | 102%
Class C | 0.00% | 0.03% | 0.09% | 105% | 103%
Class E |  |  |  |  | 
Overall | -0.02% | 0.03% | 0.05% | 102% | 102%
Class D | 0.00% | 0.03% | 0.00% | 104% | 103%
Class F | 0.00% | 0.03% | 0.00% | 102% | 100%

## Slide 7: Results – sub-TU implementation
Additionally, elimination of cabac_zero_word in:
  DaylightRoad2, random access at QP=22
 |  |  | RA |  | 
 |  |  | Over VTM |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.10% | -0.01% | 100% | 100%
Class A2 | 0.02% | -0.03% | 0.01% | 99% | 98%
Class B | 0.01% | 0.07% | -0.06% | 100% | 100%
Class C | -0.01% | -0.04% | 0.02% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | -0.01% | -0.02% | 100% | 100%
Class D | 0.01% | 0.01% | 0.06% | 100% | 100%
Class F (optional) | 0.00% | -0.02% | -0.01% | 100% | 100%

## Slide 8: Results – DaylightRoad2
TU Implementation
Sub-TU Implementation

## Slide 9: Results – CatRobot
TU Implementation
Sub-TU Implementation

## Slide 10: Results – BQTerrace
TU Implementation
Sub-TU Implementation

## Slide 11: Conclusion
Identified conditions in which cabac_zero_word padding is required
  Larger than average number of GT1 flags
  Most GT1 flags have value 0
Proposed a new GT1 group flag
  Signals if all coefficients in a group have a magnitude of at most 1
  Remove need to code large number of GT1 flags for some sequences
  Reduces need for cabac_zero_word padding