## Slide 1: Non-CE4: CIIP using triangular partitions
Saverio Blasi, Gosala Kulupana, André Seixas Dias,
15th JVET Meeting, Gothenburg
JVET O0522

## Slide 2
General idea
Straightforward combination of existing VVC blocks: CIIP and TPM
CIIP combines an intra and inter predictions for a block
TPM performs combination of two inter-predictions using a triangular partitioning
We propose to perform CIIP but using the TPM partitioning scheme and blending
This is basically just a different weighting scheme for the CIIP combination
Three CIIP triangle options are proposed:

## Slide 3
Proposed method
CIIP triangle is signalled as an alternative to conventional CIIP. In this initial implementation no new ctx variables are introduced
If CIIP triangle is used, then one of 3 CIIP triangle modes is signalled
At decoder processing stage, two neighbouring blocks are checked to see if they are intra-coded (exactly as in CIIP), to sort the three CIIP triangle modes
Mode | Binarization
Mode 1 | 0
Mode 2 | 10
Mode 3 | 11

## Slide 4
Proposed method
Two methods are proposed to compute the intra-mode to use for the intra partition:
Method 1: Intra-mode is always PLANAR (as in CIIP)
Method II: Intra-mode is inferred from two neighbouring blocks using simple process:
If both neighbouring CUs are intra-coded using the same mode intraDir0, then TriangleIntraDir = intraDir0
Else if N0 is intra-coded and N1 is not, then TriangleIntraDir = intraDir0
Else if N1 is intra-coded and N0 is not, then TriangleIntraDir = intraDir1
Else TriangleIntraDir = PLANAR
Intra-mode is also inferred from neighbouring blocks

## Slide 5
Performance results
 |  |  | RA |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.26% | 0.04% | 102% | 101%
Class A2 | -0.04% | -0.01% | 0.01% | 102% | 101%
Class B | -0.05% | 0.03% | -0.05% | 102% | 100%
Class C | -0.19% | -0.24% | -0.19% | 101% | 101%
Class E |  |  |  |  | 
Overall | -0.08% | -0.11% | -0.06% | 102% | 101%
Class D | -0.06% | -0.08% | 0.35% | 101% | 100%
Class F | -0.04% | 0.01% | -0.03% | 101% | 103%
 |  |  | LD |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.18% | -0.46% | -0.28% | 100% | 95%
Class E | 0.01% | -0.13% | -0.37% | 101% | 94%
Overall |  |  |  |  | 
Class D | -0.11% | -0.45% | 0.59% | 102% | 92%
Class F |  |  |  |  | 
Method 1
Encoder complexity will probably come down to ~100% with the proposed SIMD blending implementation in JVET-O0280

## Slide 6
Performance results
 |  |  | RA |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.24% | 0.04% | 102% | 102%
Class A2 | -0.06% | -0.06% | -0.02% | 103% | 101%
Class B | -0.09% | -0.06% | -0.10% | 101% | 99%
Class C | -0.21% | -0.21% | -0.37% | 102% | 99%
Class E |  |  |  |  | 
Overall | -0.10% | -0.13% | -0.13% | 102% | 100%
Class D | -0.07% | -0.09% | 0.20% | 102% | 99%
Class F | -0.07% | 0.07% | -0.01% | 102% | 103%
 |  |  | LD |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.23% | -0.48% | -0.40% | 101% | 90%
Class E | -0.07% | -0.22% | -1.21% | 102% | 98%
Overall |  |  |  |  | 
Class D | -0.16% | -0.21% | 0.09% | 102% | 90%
Class F |  |  |  |  | 
Method 1I
Encoder complexity will probably come down to ~100% with the proposed SIMD blending implementation in JVET-O0280

## Slide 7
Conclusion
It is proposed to allow combination of existing VVC blocks: CIIP and TPM
Decoder inference processing is identical to CIIP
Decoder partitioning and blending is identical to TPM
Average RA BD-rates of -0.08% for method 1, and of -0.10% for method 1I with no additional decoder complexity and 102% encoder complexity (this will probably come down to ~100% with the proposed SIMD blending implementation in JVET-O0280)
Considerable gains for class C (-0.21% in RA)
Partial LD results show promising gains for ~101-102% encoder complexity
Simple tweaks could improve the results (e.g. current implementation doesn’t make use of any additional ctx variable)

## Slide 8: Thank you
www.bbc.co.uk/rd

## Slide 9
Additional informative results:
A simplified method is being tested where only the first two out of three modes are considered
Less signalling and slightly less complexity at encoder side
Gains (from partial results) seem to be almost preserved
 |  |  | RA |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.21% | -0.26% | -0.28% | 101% | 100%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.06% | -0.07% | 0.12% | 101% | 98%
Class F |  |  |  |  | 
 |  |  | LD |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C |  |  |  |  | 
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.15% | -0.48% | -0.01% | 102% | 97%
Class F |  |  |  |  |