## Slide 1: Non-CE4: CIIP using triangular partitions
Saverio Blasi, Gosala Kulupana, André Seixas Dias,
15th JVET Meeting, Gothenburg
JVET O0522

## Slide 2
General idea
Straightforward combination of existing VVC blocks: CIIP and TPM
CIIP combines an intra and inter predictions for a block
TPM performs combination of two inter-predictions using a triangular partitioning
We propose to perform CIIP but using the TPM partitioning scheme and blending
This is basically just a different weighting scheme for the CIIP combination
Three CIIP triangle options are proposed:

## Slide 3
Proposed method
CIIP triangle is signalled as an alternative to conventional CIIP. In this initial implementation no new ctx variables are introduced
If CIIP triangle is used, then one of 3 CIIP triangle modes is signalled
At decoder processing stage, two neighbouring blocks are checked to see if they are intra-coded (exactly as in CIIP), to sort the three CIIP triangle modes
Mode | Binarization
Mode 1 | 0
Mode 2 | 10
Mode 3 | 11

## Slide 4
Proposed method
Two methods are proposed to compute the intra-mode to use for the intra partition:
Method 1: Intra-mode is always PLANAR (as in CIIP)
Method II: Intra-mode is inferred from two neighbouring blocks using simple process:
If both neighbouring CUs are intra-coded using the same mode intraDir0, then TriangleIntraDir = intraDir0
Else if N0 is intra-coded and N1 is not, then TriangleIntraDir = intraDir0
Else if N1 is intra-coded and N0 is not, then TriangleIntraDir = intraDir1
Else TriangleIntraDir = PLANAR
Intra-mode is also inferred from neighbouring blocks

## Slide 5
Performance results
 |  |  | RA |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.26% | 0.04% | 102% | 101%
Class A2 | -0.04% | -0.01% | 0.01% | 102% | 101%
Class B | -0.05% | 0.03% | -0.05% | 102% | 100%
Class C | -0.19% | -0.24% | -0.19% | 101% | 101%
Class E |  |  |  |  | 
Overall | -0.08% | -0.11% | -0.06% | 102% | 101%
Class D | -0.06% | -0.08% | 0.35% | 101% | 100%
Class F | -0.04% | 0.01% | -0.03% | 101% | 103%
 |  |  | LD |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.11% | 0.19% | 0.08% | 100% | 98%
Class C | -0.18% | -0.46% | -0.28% | 100% | 95%
Class E | 0.01% | -0.13% | -0.37% | 101% | 94%
Overall | -0.10% | -0.11% | -0.15% | 100% | 96%
Class D | -0.11% | -0.45% | 0.59% | 102% | 92%
Class F | -0.04% | 0.33% | -0.20% | 103% | 103%
Method 1
Encoder complexity will probably come down to ~100% with the proposed SIMD blending implementation in JVET-O0280

## Slide 6
Performance results
 |  |  | RA |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.24% | 0.04% | 102% | 102%
Class A2 | -0.06% | -0.06% | -0.02% | 103% | 101%
Class B | -0.09% | -0.06% | -0.10% | 101% | 99%
Class C | -0.21% | -0.21% | -0.37% | 102% | 99%
Class E |  |  |  |  | 
Overall | -0.10% | -0.13% | -0.13% | 102% | 100%
Class D | -0.07% | -0.09% | 0.20% | 102% | 99%
Class F | -0.07% | 0.07% | -0.01% | 102% | 103%
 |  |  | LD |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.14% | -0.08% | -0.09% | 102% | #NUM!
Class C | -0.23% | -0.48% | -0.40% | 101% | 90%
Class E | -0.07% | -0.22% | -1.21% | 102% | 98%
Overall | -0.15% | -0.25% | -0.47% | 102% | #NUM!
Class D | -0.16% | -0.21% | 0.09% | 102% | 90%
Class F | -0.13% | 0.64% | -0.06% | 103% | 102%
Method 1I
Encoder complexity will probably come down to ~100% with the proposed SIMD blending implementation in JVET-O0280

## Slide 7
Conclusion
It is proposed to allow combination of existing VVC blocks: CIIP and TPM
Decoder inference processing is identical to CIIP
Decoder partitioning and blending is identical to TPM
Average RA BD-rates of -0.08% for method 1, and of -0.10% for method 1I with no additional decoder complexity and 102% encoder complexity (this will probably come down to ~100% with the proposed SIMD blending implementation in JVET-O0280)
Considerable gains for class C (-0.21% in RA)
LD results show promising gains for ~101-102% encoder complexity
Simple tweaks could improve the results (e.g. current implementation doesn’t make use of any additional ctx variable)

## Slide 8: Thank you
www.bbc.co.uk/rd

## Slide 9
Summary of the idea
Straightforward combination of existing VVC blocks: CIIP and TPM
CIIP is performed using TPM partitioning and blending
Blending is already available in decoder. It was commented during this meeting that this is a simple operation that can be performed on the fly
It was commented by hardware experts that this could be seen as a simplification, as less samples in the block require blending – most are just substitutions from either the intra or inter predictors.
Example: in 32x32 chroma block
  CIIP requires to blend 1024 samples.
  CIIP with triangular partitions requires to blend 94 samples

## Slide 10
Summary of the idea
The proposed modification to CIIP fills a real gap within the current VVC process: there are cases where a triangular partition may be beneficial, but only one partition can be predicted accurately using Merge

## Slide 11
Visual analysis
Tool is mostly used to predict moving objects over static areas of background

## Slide 12
Visual analysis
Tool is mostly used to predict moving objects over static areas of background

## Slide 13
Visual analysis
Tool is mostly used to predict moving objects over static areas of background

## Slide 14
Visual analysis

## Slide 15
Visual analysis

## Slide 16
Visual analysis

## Slide 17
Visual analysis

## Slide 18
Visual analysis

## Slide 19
Visual analysis

## Slide 20
Visual analysis

## Slide 21
Visual analysis