## Slide 1: JVET-O0548 – Combined bilateral/SAO loop filter
J. Ström, P. Wennersten, J. Enhorn, D. Liu, K. Andersson and R. Sjöberg
VISTA
ER DRI
2019-01-31

## Slide 2: Thanks
Thanks to Qualcomm and HHI for a lot of effort of crosschecking!

## Slide 3: Concerns addressed compared to JVET-N0493
No extra loop-filter stage compared to JVET-N0493
  JVET-N0493 received criticisms that the number of loop filter stages was increased to 4
  In this contribution, we combine the bilateral filter with SAO
Proven improvement even when deblocking RDO is turned on
  It was argued that JVET-N0493 might not add BD-rate gain when deblocking-RDO is turned on
  In this contribution, we test the bilateral filter + deblocking RDO against an anchor with deblocking-RDO turned on
Panic mode possible
  When an encoder gets an extra difficult image, it needs to enter ”panic mode”, were most tests and processing is turned off.
  For JVET-N0493 there was no way of turning the filter off halfways through an image.
  In this contribution, we have a variant that can turn the filter off per CTU.

## Slide 4: No extra loop filter stage
In this contribution, bilateral filtering and SAO are combined.
No extra samples needed compared to only SAO
Both filters use the same input, and the output is combined.
  Filtering can happen in any order, or in parallel, or in lock-step per sample.

## Slide 5: Results test 1 AI
 |  | Over VTM-5.0 |  |  |  |  | 
 | Y |  | U | V | EncT | EncT fast | DecT
Class A1 | -0.30% |  | 0.30% | 0.22% | 118% | 107% | 107%
Class A2 | -0.39% |  | 0.08% | 0.11% | 114% | 106% | 102%
Class B | -0.35% |  | 0.23% | 0.27% | 115% | 107% | 103%
Class C | -0.55% |  | 0.11% | 0.20% | 112% | 106% | 104%
Class E | -0.46% |  | 0.18% | 0.21% | 114% | 104% | 106%
Overall | -0.41% |  | 0.18% | 0.21% | 115% | 106% | 104%
Class D | -0.49% |  | 0.30% | -0.02% | 109% | 105% | 102%
Class F | -0.61% |  | 0.14% | -0.03% |  | 105% | 103%

## Slide 6: Results test 1 RA
 |  | Over VTM-5.0 |  |  |  |  | 
 | Y |  | U | V | EncT | EncT fast | DecT
Class A1 | -0.37% |  | -0.14% | 0.05% | 109% | 103% | 103%
Class A2 | -0.49% |  | -0.13% | 0.01% | 108% | 103% | 102%
Class B | -0.48% |  | 0.08% | 0.01% | 107% | 102% | 103%
Class C | -0.61% |  | 0.04% | 0.01% | 108% | 101% | 101%
Class E |  |  |  |  |  |  | 
Overall | -0.49% |  | -0.02% | 0.02% | 108% | 102% | 102%
Class D | -0.54% |  | 0.21% | 0.27% | 105% | 101% | 100%
Class F | -0.65% |  | 0.00% | -0.18% |  | 97% | 104%

## Slide 7: Results test 1 LD
 |  | Over VTM-5.0 |  |  |  |  | 
 | Y |  | U | V | EncT | EncT fast | DecT
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | -0.25% |  | 0.93% | 0.76% | 110% |  | 103%
Class C | -0.52% |  | 0.82% | 0.59% | 111% | 104% | 104%
Class E | -0.16% |  | 0.44% | 1.02% | 108% | 101% | 105%
Overall | -0.32% |  | 0.77% | 0.77% | 110% |  | 104%
Class D | -0.71% |  | 0.82% | 1.30% | 110% | 104% | 99%
Class F |  |  |  |  |  |  | 

## Slide 8: Proven improvement even when deblocking-RDO is turned on
Just testing against CTC, the performance is
  -0.41% (AI), -0.49% (RA), -0.32% (LD)
Testing against an anchor where deblocking-RDO is turned on gives
  -0.28% (AI), -0.39% (RA), -0.19% (LD)
Hence most of the gain is retained when deblocking-RDO is turned on.

## Slide 9: Results test 2 AI
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.18% | 0.21% | 0.22% | 111% | 105%
Class A2 | -0.29% | 0.15% | 0.09% | 109% | 107%
Class B | -0.20% | 0.22% | 0.23% | 111% | 102%
Class C | -0.44% | 0.25% | 0.03% | 119% | 104%
Class E | -0.32% | 0.14% | 0.24% | 108% | 105%
Overall | -0.28% | 0.20% | 0.16% | 112% | 104%
Class D | -0.42% | 0.17% | 0.11% | 112% | 100%
Class F |  |  |  |  | 

## Slide 10: Results test 2 RA
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.26% | 0.10% | 0.08% | 104% | 104%
Class A2 | -0.39% | -0.02% | -0.13% | 104% | 100%
Class B | -0.36% | 0.05% | 0.06% | 107% | 100%
Class C | -0.53% | 0.02% | -0.26% | 106% | 103%
Class E |  |  |  |  | 
Overall | -0.39% | 0.04% | -0.06% | 105% | 101%
Class D | -0.56% | 0.16% | 0.13% | 106% | 99%
Class F |  |  |  |  | 

## Slide 11: Results test 2 LD
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.12% | 0.93% | 1.46% | 107% | 100%
Class C | -0.45% | 1.00% | 0.71% | 106% | 100%
Class E | 0.03% | 0.90% | 0.02% | 106% | 103%
Overall | -0.19% | 0.95% | 0.85% | 106% | 101%
Class D | -0.71% | 0.59% | 0.58% | 104% | 98%
Class F |  |  |  |  | 

## Slide 12: Panic mode possible
Just testing against CTC, the performance is
  -0.41% (AI), -0.49% (RA), -0.32% (LD)
Testing with a variant that can turn off bilateral filtering per CTU gives
  -0.41% (AI), -0.48% (RA), -0.29% (LD)
Hence a version capable of panic mode does not degrade performance.

## Slide 13: Results test 3 AI
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.30% | 0.31% | 0.23% | 118% | 103%
Class A2 | -0.39% | 0.08% | 0.11% | 115% | 106%
Class B | -0.35% | 0.23% | 0.27% | 114% | 104%
Class C | -0.55% | 0.11% | 0.21% | 116% | 105%
Class E | -0.45% | 0.18% | 0.22% | 118% | 105%
Overall | -0.41% | 0.18% | 0.21% | 116% | 104%
Class D | -0.48% | 0.30% | -0.02% | 115% | 105%
Class F | -0.61% | 0.15% | -0.02% | 106% | 105%

## Slide 14: Results test 3 RA
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.35% | -0.13% | 0.06% | 108% | 102%
Class A2 | -0.48% | -0.12% | 0.02% | 107% | 100%
Class B | -0.47% | 0.09% | 0.02% | 108% | 102%
Class C | -0.60% | 0.05% | 0.02% | 107% | 101%
Class E |  |  |  |  | 
Overall | -0.48% | -0.01% | 0.03% | 108% | 102%
Class D | -0.52% | 0.23% | 0.29% | 105% | 96%
Class F | -0.62% | 0.03% | 0.20% | 106% | 103%

## Slide 15: Results test 3 LD
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.24% | 0.94% | 0.77% | 111% | 102%
Class C | -0.51% | 0.83% | 0.61% | 111% | 102%
Class E | -0.07% | 0.52% | 1.10% | 109% | 103%
Overall | -0.29% | 0.80% | 0.80% | 110% | 103%
Class D | -0.69% | 0.84% | 1.32% | 113% | 100%
Class F |  |  |  |  | 

## Slide 17: Arithmetic operations
Operations per modification value | add +(round add) | add width | shift | check
 | 1 (1) | 10, 11 | 1 | 
 |  |  |  | 2
sum | 1 (1) |  | 1 | 2
Operations per modification value | add +(round add) | add width | shift | check
 | 1 (1) | 10, 11 | 1 | 
 |  |  |  | 2
sum | 1 (1) |  | 1 | 2

## Slide 18: Arithmetic operations per sample
Step | add (+round add) | add width | shift | check
and | 2 (2) | 10, 11 | 2 | 4
and | 2 (2) | 10, 11 | 4 | 4
 | 7 | 6,7,8 |  | 
 | 1 | 10 | 1 | 
 | 1 (1) | 10 | 1 | 
total per pixel | 13 + (5) |  | 8 | 8
Step | add (+round add) | add width | shift | check
 | 2 (2) | 10, 11 | 2 | 4
 | 2 (2) | 10, 11 | 4 | 4
 | 7 | 6,7,8 |  | 
 | 1 | 10 | 1 | 
 | 1 (1) | 10 | 1 | 
total per pixel | 13 + (5) |  | 8 | 8
13 additions plus 5 rounding additions per pixel, 8 shifts and 8 checks
Largest addition width is 11 bits