## Slide 1: JVET-O0548 – Combined bilateral/SAO loop filter
J. Ström, P. Wennersten, J. Enhorn, D. Liu, K. Andersson and R. Sjöberg
VISTA
ER DRI
2019-01-31

## Slide 2: Thanks
Thanks to Qualcomm, HHI and Huawei for a lot of effort of crosschecking!
(JVET-O1035 and JVET-O1099)

## Slide 3: Concerns addressed compared to JVET-N0493
No extra loop-filter stage compared to JVET-N0493
  JVET-N0493 received criticisms that the number of loop filter stages was increased to 4
  In this contribution, we combine the bilateral filter with SAO
Proven improvement even when deblocking RDO is turned on
  It was argued that JVET-N0493 might not add BD-rate gain when deblocking-RDO is turned on
  In this contribution, we test the bilateral filter + deblocking RDO against an anchor with deblocking-RDO turned on
Panic mode possible
  When an encoder gets an extra difficult image, it needs to enter ”panic mode”, were most tests and processing is turned off.
  For JVET-N0493 there was no way of turning the filter off halfways through an image.
  In this contribution, we have a variant that can turn the filter off per CTU.

## Slide 4: No extra loop filter stage
In this contribution, bilateral filtering and SAO are combined.
No extra samples needed compared to only SAO
Both filters use the same input, and the output is combined.
  Filtering can happen in any order, or in parallel, or in lock-step per sample.

## Slide 5: In detail
DBIF = DBIF(I(x,y) + surrounding samples)
DSAO = DSAO(I(x,y) + surrounding samples)
and the final pixel is constructed as
output = clip( I(x,y) + DBIF + DSAO)
Previously: output = clip(I(x,y) + DSAO)

## Slide 6: Results test 1 AI
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.30% | 0.30% | 0.22% | 107% | 107%
Class A2 | -0.39% | 0.08% | 0.11% | 106% | 102%
Class B | -0.35% | 0.23% | 0.27% | 107% | 103%
Class C | -0.55% | 0.11% | 0.20% | 106% | 104%
Class E | -0.46% | 0.18% | 0.21% | 104% | 106%
Overall | -0.41% | 0.18% | 0.21% | 106% | 104%
Class D | -0.49% | 0.30% | -0.02% | 105% | 102%
Class F | -0.61% | 0.14% | -0.03% | 105% | 103%

## Slide 7: Results test 1 RA
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.37% | -0.14% | 0.05% | 103% | 103%
Class A2 | -0.49% | -0.13% | 0.01% | 103% | 102%
Class B | -0.48% | 0.08% | 0.01% | 102% | 103%
Class C | -0.61% | 0.04% | 0.01% | 101% | 101%
Class E |  |  |  |  | 
Overall | -0.49% | -0.02% | 0.02% | 102% | 102%
Class D | -0.54% | 0.21% | 0.27% | 101% | 100%
Class F | -0.65% | 0.00% | 0.18% | 97% | 104%

## Slide 8: Results test 1 LD
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.25% | 0.93% | 0.76% | #NUM! | 103%
Class C | -0.52% | 0.82% | 0.59% | 104% | 104%
Class E | -0.16% | 0.44% | 1.02% | 101% | 105%
Overall | -0.32% | 0.77% | 0.77% | #NUM! | 104%
Class D | -0.71% | 0.82% | 1.30% | 104% | 99%
Class F | #NUM! | #NUM! | #NUM! | #NUM! | #NUM!

## Slide 9: Proven improvement even when deblocking-RDO is turned on
Just testing against CTC, the performance is
  -0.41% (AI), -0.49% (RA), -0.32% (LD)
Testing against an anchor where deblocking-RDO is turned on gives
  -0.28% (AI), -0.39% (RA), -0.19% (LD)
Hence most of the gain is retained when deblocking-RDO is turned on.

## Slide 10: Results test 2 AI
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.18% | 0.21% | 0.22% | 111% | 105%
Class A2 | -0.29% | 0.15% | 0.09% | 109% | 107%
Class B | -0.20% | 0.22% | 0.23% | 111% | 102%
Class C | -0.44% | 0.25% | 0.03% | 119% | 104%
Class E | -0.32% | 0.14% | 0.24% | 108% | 105%
Overall | -0.28% | 0.20% | 0.16% | 112% | 104%
Class D | -0.42% | 0.17% | 0.11% | 112% | 100%
Class F | -0.54% | 0.06% | 0.04% | 106% | 105%
(slower encoder)

## Slide 11: Results test 2 RA
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.26% | 0.10% | 0.08% | 104% | 104%
Class A2 | -0.39% | -0.02% | -0.13% | 104% | 100%
Class B | -0.36% | 0.05% | 0.06% | 107% | 100%
Class C | -0.53% | 0.02% | -0.26% | 106% | 103%
Class E |  |  |  |  | 
Overall | -0.39% | 0.04% | -0.06% | 105% | 101%
Class D | -0.56% | 0.16% | 0.13% | 106% | 99%
Class F | -0.60% | 0.03% | -0.03% | 106% | 104%
(slower encoder)

## Slide 12: Results test 2 LD
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.12% | 0.93% | 1.46% | 107% | 100%
Class C | -0.45% | 1.00% | 0.71% | 106% | 100%
Class E | 0.03% | 0.90% | 0.02% | 106% | 103%
Overall | -0.19% | 0.95% | 0.85% | 106% | 101%
Class D | -0.71% | 0.59% | 0.58% | 104% | 98%
Class F | -0.37% | 0.00% | -0.20% | 103% | 106%
(slower encoder)

## Slide 13: Panic mode possible
Just testing against CTC, the performance is
  -0.41% (AI), -0.49% (RA), -0.32% (LD)
Testing with a variant that can turn off bilateral filtering per CTU gives
  -0.41% (AI), -0.48% (RA), -0.29% (LD)
Hence a version capable of panic mode does not degrade performance.

## Slide 14: Results test 3, AI
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.30% | 0.31% | 0.23% | 111% | 103%
Class A2 | -0.39% | 0.08% | 0.11% | 110% | 106%
Class B | -0.35% | 0.23% | 0.27% | 110% | 104%
Class C | -0.55% | 0.11% | 0.21% | 106% | 105%
Class E | -0.45% | 0.18% | 0.22% | 106% | 105%
Overall | -0.41% | 0.18% | 0.21% | 109% | 104%
Class D | -0.48% | 0.30% | -0.02% | 113% | 105%
Class F | -0.61% | 0.15% | -0.02% | 106% | 105%

## Slide 15: Results test 3, RA
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.35% | -0.13% | 0.06% | 107% | 102%
Class A2 | -0.48% | -0.12% | 0.02% | 106% | 100%
Class B | -0.47% | 0.09% | 0.02% | 105% | 102%
Class C | -0.60% | 0.05% | 0.02% | 103% | 101%
Class E |  |  |  |  | 
Overall | -0.48% | -0.01% | 0.03% | 105% | 102%
Class D | -0.52% | 0.23% | 0.29% | 101% | 96%
Class F | -0.62% | 0.03% | 0.20% | 102% | 103%

## Slide 16: Results test 3, LD
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.24% | 0.94% | 0.77% | #NUM! | 102%
Class C | -0.51% | 0.83% | 0.61% | 109% | 102%
Class E | -0.07% | 0.52% | 1.10% | 106% | 103%
Overall | -0.29% | 0.80% | 0.80% | #NUM! | 103%
Class D | -0.69% | 0.84% | 1.32% | 109% | 100%
Class F | #NUM! | #NUM! | #NUM! | #NUM! | #NUM!

## Slide 17: Overview
Center sample is filtered using neighboring samples
  Only right sample and belows samples needed
Difference is formed
Difference used to look-up modifier value
Sum together modifier values
Apply strength:
Filtered output:

## Slide 18: Complexity comparison to Hadamard filter
Step | width | number
forward transform |  | 
const int y0 = x0 + x2; | 10 | 1
const int y1 = x1 + x3; | 10 | 1
const int y2 = x0 - x2; | 10 | 1
const int y3 = x1 - x3; | 10 | 1
const int t0 = y0 + y1; | 11 | 1
const int t1 = y0 - y1; | 11 | 1
const int t2 = y2 + y3; | 11 | 1
const int t3 = y2 - y3; | 11 | 1
table look-up |  | 
-tbl[(-z + HTDF_TBL_RND)≫ HTDF_TBL_SHIFT) | 7 | 3
-tbl[(-z + HTDF_TBL_RND)≫ HTDF_TBL_SHIFT) | 7 | 3
-tbl[(-z + HTDF_TBL_RND)≫ HTDF_TBL_SHIFT) | 7 | 3
Step | width | number
backward transform |  | 
const int iy0 = t0 + t2; | 13 | 1
const int iy1 = t1 + t3; | 12 | 1
const int iy2 = t0 - t2; | 12 | 1
const int iy3 = t1 - t3; | 12 | 1
const int ix0 = iy0 +iy1; | 14 | 1
const int ix1 = iy0 - iy1; | 14 | 1
const int ix2 = iy2 + iy3; | 14 | 1
const int ix3 = iy2 - iy3; | 14 | 1
normalization |  | 
(pOut[p0_out] + HTDF_CNT_SCALE_RND) >> HTDF_CNT_SCALE | 15 | 1
In summary, just for the transform, we get 1 15-bit adder, 4 14-bit adders, 1 13-bit adder, 3 12-bit adders,
4 11-bit adders, 4 10-bit adders and one 7-bit adder.
In contrast, the present contribution has 6 11-bit adders, 5 10-bit adders, 1 9-bit adder, 1 8-bit adder, 7 7-bit adders and 2 6-bit adders.

## Slide 19: Adder widths – in detail
Width | Number of additions Hadamard | Number of additions Bilateral
15-bit adder | 1 | 
14-bit adder | 4 | 
13-bit adder | 1 | 
12-bit adder | 3 | 
11-bit adder | 4 | 6
10-bit adder | 4 | 5
9-bit adder |  | 1
8-bit adder |  | 1
7-bit adder | 9 | 7
6-bit adder |  | 2
In total | 26 | 22
Whereof rounding adds | 4 | 5
Not counting rounding adds | 22 | 17

## Slide 20: Memory requirements
Bilateral filter: 60 bytes
Hadamard (from CE1-2.3): 70 bytes

## Slide 21: Arithmetic operations
Operations per modification value | add +(round add) | add width | shift | check
 | 1 (1) | 10, 11 | 1 | 
 |  |  |  | 2
sum | 1 (1) |  | 1 | 2
Operations per modification value | add +(round add) | add width | shift | check
 | 1 (1) | 10, 11 | 1 | 
 |  |  |  | 2
sum | 1 (1) |  | 1 | 2

## Slide 22: Arithmetic operations per sample
Step | add (+round add) | add width | shift | check
and | 2 (2) | 10, 11 | 2 | 4
and | 2 (2) | 10, 11 | 4 | 4
 | 7 | 6,7,8 |  | 
 | 1 | 10 | 1 | 
 | 1 (1) | 10 | 1 | 
total per pixel | 13 + (5) |  | 8 | 8
Step | add (+round add) | add width | shift | check
 | 2 (2) | 10, 11 | 2 | 4
 | 2 (2) | 10, 11 | 4 | 4
 | 7 | 6,7,8 |  | 
 | 1 | 10 | 1 | 
 | 1 (1) | 10 | 1 | 
total per pixel | 13 + (5) |  | 8 | 8
13 additions plus 5 rounding additions per pixel, 8 shifts and 8 checks
Largest addition width is 11 bits